## Slide 1: VFMAC Design Spec

## Slide 2: instruction list
addition
  fadd/vfadd/vfwadd: a*1+c
  fsub/vfsub/vfwsub/vfrsub: a*1-c
multiply
  fmul/vfmul/vfwmul: a*b+0
mac
  fmadd/vfmadd/vfmacc/vfwmacc: a*b+c
  fmsub/vfmsub/vfmsac/vfwmsac: a*b-c
  fnmsub/vfnmsub/vfnmsac/vfwnmsac: -(a*b)+c
  fnmadd/vfnmadd/vfnmacc/vfwnmacc: -(a*b)-c
reduction
dot-product

## Slide 3: V2/F0 stage
Reduction/dot-product FSM
src_gen: VRF, scalar FRF selection
Constant generation
  constant 1 for addition
  constant 0 for multiplication: 0 for multiply is generated in F1, because dot-product needs f1_op3 to backup the addend
    delay might be hide into
Operand SEW adjustment for widening operations
Pipe valid generation from FSM/mask

## Slide 4: Data Path
expA
164-bits align. shifter
inv
csa(56-a+b-c-bias)
encode
4:2 CSA
partial product reduction
f2
expB
expC
fracC
fracA
fracB
f1
partial sticky: st1
3:2 CSA
HA carry
HA inv. carry
HA sum
LZA pos + neg
f3
sign detection
normalization
164
special value detection
Eff. sub
Eff. sub
164
st1
complement
LZA string
OR network
eff. sub
d
Part of dual adder
Part of dual adder
eff. sub
LZCsubnorm[6]
LZCsubnorm[5]
LZCsubnorm[0]
d<=2
lshift 54/25/12 bits
sign-ext
164bit = 1 // preserved 1 bit for big addend round to exp+1
+ 53 // addend
+ 2 // guard bits between addend and multiply result
+106 // multiply result
+ 2 // see subnormal corner case 1
110
complement : 161 bits compare
ha+partial adder: xor + xor + 2 aoi

## Slide 5
RI = RUP & ~final_sign | RDN & final_sign
neg (a*b) + sub(c)
eff_sub = (neg ^ sign_a ^ sign_b) ^ (sub ^ sign_c)
final sign = eff_sub &comp. | (sub ^ sign(c))
RN = RNE | RMM
161 110 109 107 106 0
xx.x.......x xxx x......x
DP as an example
format
after normalization
dual adder
S+1 S
52
4-bit adder
3
107
st1
carry
carry/sticky calc
4-bit adder
4-bit adder
round decision
LSB correction
ovf = Y0[51] | Y1[51] & Z[4]
Y0
Y1
Z
sticky
sticky
RI
inc
f4
ovf
novf

## Slide 6: F1: 4:2 CSA
Don’t cascade two FAs directly, convert it to canonical form
Propagation Delay is about 1.5 times of 3:2 CSA

## Slide 7: F1: Modified Booth Encoding
Partial product is sign-extended when encoded as -1X or -2X
To eliminate the width of CSA arrays:
  invert the MSB of sign-extension bit of the multiplicand and rewrite the partial product into the grey background part + our new partial product:
The carry chain will be the same. But with the greyed out constants for sign-extension, we can add them together:

## Slide 8: F1: Addend Alignment and Partial Sticky Bit Generation
d = expC` - expA` + expB` - bias
Alignment amount = 56-d

## Slide 9: exponent calculation
align diff <= 2
align diff > 2
x
…
x
…
x
55
exp = expA’ + expB’ + 2 - lzc
x
…
x
…
x
exp = expC’ – eff_sub
LZC
lzc_gt2 = align_amount
align_amount
…
x
x
…
0
x
x
eff. sub
lzc_gt2 = align_amount +1
0…0
0…0
x…x
x
x
0…0
eff. add
without LZA error
x…x
0
1
x…x
1
x
with
LZA error

## Slide 10: F2: LZA
LZA pos
sign detection
LZA string
OR network
LZA neg
LZA string
OR network
LZA
eff. sub
LZA string
OR network
LZA eff. add
extra LZD cost
extra positive LZA cost
effective sub

## Slide 11: F2: LZA for A-B
Identify
To combine W>0 and W<0 string, extra wi-1 should be considered

## Slide 12: F2: LZA
Only applicable to X-Y case, both X and Y > 0
Leading zero of X+Y can’t simply derive from max(expX, expY)
  Normal + Normal * Sub-Normal
  1.x * 2-1020 + x.x * 2-1020 =>
Normal * Sub-Normal produces a case

## Slide 13: F2: Sign Detection
using tree comparator
  A + B => normal case
  A – B => compared with ~B
    when A = ~B then A < B

## Slide 14: F3: Normalization, sub-normal prediction
LZCsubnorm = (56-d) < 0 ? expC’ – expsubnorm
expA’ + expB’ + 56 - expsubnorm
x
x
…
x
x
x
…
x
x
Cinv
A*B
56-d < 0
53
106
x
x
…
x
x
x
…
x
x
106
d = 1
x
x
…
x
x
x
…
x
x
106
d < 0
expC’ – LZC <= expsubnorm
expA’ + expB’ + 56 – LZC <= expsubnorm
expA’ + expB’ + 56 – LZC <= expsubnorm
for DP, expsubnorm=-1022
d = expC’ - expA’ + expB’
56-d < 0
56-1
56-d
LZC
LZC
LZC[6] < LZCsubnorm[6]
LZC[5] < LZCsubnorm[5]
LZC[0] < LZCsubnorm[0]
Final LZC selection

## Slide 15: F4: sticky bit generation
Evalution of A+B=K Conditions Without Carry Propagation

## Slide 16: subnormal
Input
  hidden 1 should be calculated from exponent
Result
  right shift needed?
  shift amount adjustment

## Slide 17: critical path improvement opportunity
hidden 1 generation before partial sum encoding
  no optimize
    3:2 csa, latency = 1, 53-bit -> 27 partial product + 1 carry array
      27 -> 18 -> 12 -> 8+1 -> 6 -> 4 ->3-> 2 = 7
    4:2 csa, latency = 1.5
      27+1 -> 14 -> 6+2 -> 4 -> 2 = 6
  (a.x * b.y) = (ab+ay)+bx+xy :27+1 + 2 PPs
    4:2 csa
      27+1 -> 14+2 -> 8 -> 4 -> 2 = 6
  summarize slow parts to one partial product:26+1+2 PPs
    4:2 csa
      26 -> 12+2+2 -> 8+1 -> 6 -> 4 -> 2 = 6.5
stick bit and final exponent selection on fraction = 0
  can’t reuse A+PP CSA with A+B=K equation, the CSA used in F2 is A + PP
  A+B=K  A+B+~K = -1  2C + S = -1  2C = ~S
carry
slow bits

## Slide 18: MAC subnormal corner case 1
opA is minimum of subnormal 0x00000000_00001
opB is normal number
expC’ < expA’ + expB’ - 52
x
…
0
00…0 …
mul result
104
aligned addend
1
52
0
0
…
missing round bit, sticky bit
s

## Slide 19: MAC subnormal corner case 2
Widening instruction with subnormal addend
and align diff > 3
0
000000
x
…
mul result
104
aligned addend
x
LZA range 109b
opC_lzc
1
align amount
solutions
  extend LZA to 161 bits
    extra 52 bits LZA
    extra one level LZC OR-tree
  recalculate normalization amount by opC LZC
    LZC for opC subnormal input, one 23-bit LZC and one 10-bit LZC
    Addition adder for alignamount + opC_lzc

## Slide 20: UF exception
After rounding: the result is strictly between ±emin as the exponent is unbounded
  When the result is subnormal
  When the result is round from subnormal to normal:
    if the result is a subnormal when round as a normal number

## Slide 21: backup slides

## Slide 22: exponent calculation
x
…
x
…
x
104
src DP: 53 bits
x
…
x
…
src SP: 24 bits
src HP: 11 bits
align_amount:
DP fw.vv: 56 - expC + expA + expB - DP_BIAS
DP wid.vv: 56 - expC + expA + expB - SP_BIAS
DP wid.wv: 56 - expC + expA + expB + DP_BIAS - SP_BIAS * 2
f/w.vv/wv:
fw – fixed width
wid – widening
wv – op3 is widening
vv – op3 is not wideing

## Slide 26
dual adder
S+1 S
3-bit CSA
adders
LSB correction
carry
sticky
RI
RI|RN
4
4
carry
R
0 50 51 53 54 161
x.x........x xxx x......x
51
3
108
RN
LSB
DP as an example
format
after normalization
st1
comp