## Slide 1: [Alpaca]: FPU MISC Pipeline uArch
Driving Innovations™
Eric
2019/8/26

## Slide 2: Misc. Pipeline uArch

## Slide 3: Misc. Pipeline Instructions
Conversion between FP and Integer
  Integer to FP
    16-bit int to SP/HP
    Word to SP/HP
  FP to Integer
    HP to 16-bit int/Word
    SP to 16-bit int/Word
FP Sign Injection
  FSGNJ, FSGNJN, FSGNJX
FCMP
FMIN_MAX
FCLASS
FMV

## Slide 4: Single-Width Floating-Point/Integer Type Convert Instructions
Conversion operations are provided to convert to and from floating-point values and unsigned and signed integers, where both source and destination are SEW wide.
SEW = conv(SEW)
Vfcvt.xu.f.v vd, vs2, vm # Convert float to unsigned integer
Vfcvt.x.f.v vd, vs2, vm # Convert float to signed integer
Vfcvt.f.xu.v vd, vs2, vm # Convert unsigned integer to float
Vfcvt.f.x.v vd, vs2, vm # Convert signed integer to float
The conversions follow the same rules on exceptional conditions as the scalar conversion instructions. The conversions always use the dynamic rounding mode in frm.

## Slide 5: Widening Floating-Point/Integer Type Convert Instructions
A set of conversion instructions are provided to convert between narrower integer and floating-point data types to a type of twice the width (2*SEW= conv(SEW)).
Vfwcvt.xu.f.v vd, vs2, vm # Convert float to double-width unsigned integer
Vfwcvt.x.f.v vd, vs2, vm # Convert float to double-width signed integer
Vfwcvt.f.xu.v vd, vs2, vm # Convert unsigned integer to double-width float
Vfwcvt.f.x.v vd, vs2, vm # Convert signed integer to double-width float
Vfwcvt.f.f.v vd, vs2, vm # Convert single-with float to double-width float

## Slide 6: Narrowing Floating-Point/Integer Type-Convert Instructions
A set of conversion instructions are provided to convert wider integer and floating-point data types to a type of half the width (SEW = conv(2*SEW)).
Vfncvt.xu.f.v vd, vs2, vm # Convert double-width float to unsigned integer
Vfncvt.x.f.v vd, vs2, vm # Convert double-width float to signed integer
Vfncvt.f.xu.v vd, vs2, vm # Convert double-width unsigned integer to float
Vfncvt.f.x.v vd, vs2, vm # Convert double-width signed integer to float
Vfncvt.f.f.v vd, vs2, vm # Convert double-width float to single-width float

## Slide 7: Integer to FP (1/)
  Perform two’s complement when input is negative
  Long: bit[104:0]={41’b0, int_num[63:0]}, rd_exp=63
  Word: bit[104:0]={41’b0, int_num[31:0], 32’b0}, rd_exp=31
  16bit: bit[104:0]={41’b0, int_num[15:0], 48’b0} rd_exp=15
  8-bit: bit[104:0]={29’b0, int_num[7:0], 56’b0}, rd_exp=7
105 | 104 | … | 76 | 75 | … |  |  | 64 | 63 | 62 | 61 | 60 | 59 | 58 | 57 | 56 | 55 | 54 | 53 | 52 | 51 | 50 | 49 | 48 |  |  | … |  |  | 32 | 31 |  |  | 2 | 1 | 0
52 | 51 |  | 23 | 22 |  |  |  |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0L | R | [ |  |  |  |  |  |  |  |  | S |  |  |  |  |  | ]
DP
HP
Word operand
16-bit operand
FP format
bit
8-bit operand
Long operand
SP

## Slide 8: Integer to FP (1/)xx
  Perform two’s complement when input is negative
  Long: bit[104:0]={41’b0, int_num[63:0]}, rd_exp=63
  Word: bit[104:0]={41’b0, int_num[31:0], 32’b0}, rd_exp=31
  16bit: bit[104:0]={41’b0, int_num[15:0], 48’b0} rd_exp=15
  8-bit: bit[104:0]={29’b0, int_num[7:0], 56’b0}, rd_exp=7
104 | 103 | … | 75 | 74 | … |  |  | 64 | 63 | 62 | 61 | 60 | 59 | 58 | 57 | 56 | 55 | 54 | 53 | 52 | 51 | 50 |  |  |  |  | … |  |  | 32 | 31 |  |  | 2 | 1 | 0
52 | 51 |  | 23 | 22 |  |  |  |  | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0L | R | [ |  |  |  |  |  |  |  | S |  |  |  |  |  | ]
DP
HP
Word operand
16-bit operand
FP format
bit
8-bit operand
Long operand
SP

## Slide 9: Integer to FP (2/)
  Normalization:
    Count leading zero of bit[63:0] (LZD) (rd_exp’=rd_exp- lzd)
    Left shift 12 bits if target is SP, left shift 29 bits if target is DP
    Left shift bit[92:0] by lz_num[5:0] (6 level mux)
  Rounding: (54-bit adder needed: bit[93:39])
    Detect Sticky bit (st) (| bit[38:0])
    According to round mode and st, add 1 on LSB or on Round bit
    If bit[93](DP)/bit[76](SP)/bit[64](HP)==1  exp+1, fraction=0
92 | 91 | … | 75 | 74 | … |  |  | 64 | 63 | 62 |  |  | … |  |  | 56 | 55 |  | … | 40 | 39 | 38 |  | 48 | 47 |  | … |  |  | 32 | 31 |  |  | 2 | 1 | 0
52 | 51 |  | 23 | 22 |  |  |  |  | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0L | R | [ |  |  |  |  |  |  |  | S |  |  |  |  |  | ]
DP
HP
Word operand
16-bit operand
FP format
bit
8-bit operand
Long operand
SP

## Slide 10: FP to Integer
Rounding for SP to Long
  Exp<52: rsh (52-exp), Leading 12 bits are 0
    need to round (at least 1bit shifted to bit[10:0])
    Integer = {12’b0, bit[62:11]}
  52 ≦ Exp ≦ 63: right shift (63-exp),
    no need to round
    Integer = {bit[63:0]}
11 10 0
result
12’b0
result
11 10 0
Round bit
No rounding
63
63

## Slide 11: FP to Integer
  Right shift by sh_amount (subnormal don’t care)
    0<exp<52: sh_amount = 52-exp, then rounded by 54bit adder
      64bit_int[63:0] ={12’b0,bit[62:11]
      32bit_int[31:0] = bit[42:11]
      16bit_int[15:0] = bit[26:11]
      8bit_int[7:0] = bit[18:11]
    exp >= 52: sh_amount = 63-exp, no rounding
      64bit_int[63:0]=bit[63:0]
63 | 62 | 61 | 60 | 59 |  |  | … |  | 53 | … |  | 40 |  |  |  |  |  |  |  | 12 | 11 | 10 | 9 | 8 | … | 2 | 1 | 0
52 | 51 | 50 |  |  |  |  | D | P |  |  |  |  |  |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
23 | 22 | 21 |  |  |  |  | S | P |  |  |  | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 | 9 |  |  |  |  |  | H | P | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | L | R | [ |  | S |  |  | ]
bit
To Rounding Adder

## Slide 12: Convert Between DP and SP
D to S
  Right shift by 63-35+1=29 bit
  Rounding
  Subnormal handling
  Exception detection (overflow, underflow,…)
S to D
  Use NBS (left shift) for normal or subnormal input
  No Rounding is needed
63 | 62 | 61 |  |  |  |  |  |  | 35 |  |  |  |  |  |  |  |  |  |  | 12 | 11 | 10 | 9 | 8 | … | 2 | 1 | 0
52 | 51 | 50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 23 | 22 |  |  |  |  |  |  |  |  |  |  | 0 L | R | [ |  | S |  |  | ]
bit
To Rounding Adder

## Slide 13: Convert Between SP and HP
S to H
  Right shift by 63-21=42 bit +
    (-exp-13) if target result is subnorm, i.e. -13>sp_exp>-25)
  Rounding
  Subnormal handling
H to S
  Use NBS (left shift) for normal or subnormal input
  No Rounding is needed
63 | 62 | 61 |  |  |  |  | 39 |  | 35 | … | 21 | 20 |  |  |  |  |  |  |  | 12 | 11 | 10 | 9 | 8 | … | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 L | R | [ |  | S |  |  | ]
bit
To Rounding Adder

## Slide 14: Convert From SP to BF16
D to S
  Right shift by 63-21=42 bit +
    (-exp-13) if target result is subnorm, i.e. -13>sp_exp>-25)
  Rounding
  Subnormal handling
S to D
  Use NBS (left shift) for normal or subnormal input
  No Rounding is needed
63 | 62 | 61 |  |  |  |  |  |  | 35 | … | 21 | 20 |  | 18 |  |  |  |  |  | 12 | 11 | 10 | 9 | 8 | … | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 L | R | [ |  | S |  |  | ]
bit
To Rounding Adder

## Slide 17: Convert Instructions
Conversion needs Left Shifter
  Integer to FP
  HP to SP
    left shift when subnormal input, otherwise don’t need shifter
Conversion needs Right Shifter
  FP to Integer
  SP to HP
  SP to Bfloat

## Slide 18: uArch of Convert Instructions
2’s comp.
Normalization (Left shifter)
Alignment (Right shifter)
Shift amount
54-bit adder
Round digit gen
st0
st1
rounding_mode
F2I result
I2F/F2F result
sign
FP2Int/FP Path
Int2FP/HP2SP Path
FP1
FP2
2’s complement
no_round
instr_type
LZD
…

## Slide 19: Vector Floating-Point Sign-Injection Instructions
The result takes all bits except the sign bit form the vector vs2 operands.
  The rm (rounding mode) field indicates J[N]/JX
For vfsgnj, the result’s sign bit is v/rs1’s sign bit.
Vfsgnj.vv vd, vs2, vs1, vm # Vector-vector vd[i] = {vs1[i].MSB, vs2[i]}
Vfsgnj.vf vd, vs2 , rs1, vm # Vector-scalar vd[i] = {f[rs1].MSB, vs2[i]}
For vfsgjn, the result’s sign bit is the opposite of v/rs1’s sign bit.
Vfsgjn.vv vd, vs2 , vs1, vm # Vector-vector vd[i] = {~vs1[i].MSB, vs2[i]}
Vfsgjn.vf vd, vs2 , rs1, vm # Vector-scalar vd[i] = {~f[rs1].MSB, vs2[i]}
For vfsgnjx, the sign bit is the XOR of the sign bits of v/rs1 and vs2.
Vfsgnjx.vv vd, vs2 , vs1, vm # Vector-vector vd[i] = {vs2[i].MSB ^ vs1[i].MSB, vs2[i]}
Vfsgnjx.vf vd, vs2 , rs1, vm # Vector-vector vd[i] = {vs2[i].MSB ^ f[rs1].MSB, vs2[i]}

## Slide 20: Vector Floating-Point Compare Instructions
Write the comparison result to a mask register (not necessarily V0).
Compare equal
Vfeq.vv vd, vs2, vs1, vm # Vector-vector vd[i] = (vs2[i] == vs1[i])
Vfeq.vf vd, vs2 , rs1, vm # Vector-scalar vd[i] = (vs2[i] == f[rs1])
Compare not equal
Vfne.vv vd, vs2, vs1, vm # Vector-vector vd[i] = (vs2[i] != vs1[i])
Vfne.vf vd, vs2 , rs1, vm # Vector-scalar vd[i] = (vs2[i] != f[rs1])
Compare less than
Vflt.vv vd, vs2, vs1, vm # Vector-vector vd[i] = (vs2[i] < vs1[i])
Vflt.vf vd, vs2 , rs1, vm # Vector-scalar vd[i]. = (vs2[i] < f[rs1])

## Slide 21: Vector Floating-Point Compare Instructions
Compare less than or equal
Vfle.vv vd, vs2, vs1, vm # Vector-vector vd[i].LSB = (vs2[i] <= vs1[i])
Vfle.vf vd, vs2 , rs1, vm # Vector-scalar vd[i].LSB = (vs2[i] <= f[rs1])
Compare greater than
Vfgt.vf vd, vs2 , rs1, vm # Vector-scalar vd[i].LSB = (vs2[i] > vs1[i])
Compare greater than or equal
Vfge.vf vd, vs2 , rs1, vm # Vector-scalar vd[i].LSB = (vs2[i] >= f[rs1])

## Slide 22: Vector Floating-Point Compare Instructions

## Slide 23: Vector Floating-Point Compare Instructions
This feature is removed from RISC-V spec.
To help implement the C99 floating-point comparison functions, a vford instruction is added that sets a mask register if the arguments are ordered.
  One of the source operands is treated as NaNs, result should be 0 (unordered).
Vford.vv vd, vs2, vs1, vm # Vector-vector
Vford.vf vd, vs2, rs1, vm # Vector-scalar

## Slide 24: Vector Floating-Point MIN/MAX Instructions
Floating-point minimum
Vfmin.vv vd, vs2, vs1, vm #Vector-vector vd[i] = min (vs2[i], vs1[i])
Vfmin.vf vd, vs2, rs1, vm # Vector-scalar vd[i] = min (vs2[i], f[rs1])
Floating-point maximum
Vfmax.vv vd, vs2, vs1, vm # Vector-vector vd[i] = max (vs2[i], vs1[i])
Vfmax.vf vd, vs2, rs1, vm # Vector-scalar vd[i] = max (vs2[i], f[rs1])

## Slide 25: FMIN and FMAX Instructions
FMIN-MAX
  The rm field indicates MIN/MAX
  FMIN: Write the smaller of rs1 and rs2 to rd
  FMAX: Write the larger of rs2 and rs2 to rd
  The value −0.0 is considered to be less than the value +0.0.
  Both inputs are NaNs, the result is the canonical NaN.
  Only one operand is a NaN, the result is the non-NaN operand.
  Signaling NaN inputs raise the invalid operation exception, even when the result is not NaN.

## Slide 26: Vector Floating-Point Classify Instruction
Vfclass.v vd, vs2, vm # Vector-vector vd[i] = classify(vs2[i])
The 10-bit mask produced by this instruction is placed in the LSB of the result elements.
This instruction is only defined for SEW=16b above, so the result will always fit in the destination elements.

## Slide 27: Vector Floating-Point Merge Instruction
Mask (vm=0):
  Vfmerge.vf vd, vs2, rs1, v0.t # vd[i] = v0[i].LSB ? f[rs1] : vs2[i]
Unmask (vm=1)
  Vfmerge.vf vd, v0, rs1 # vd[i] = f[rs1]
    The instruction must have the vs2 field set to v0, with all other values for vs2 reserved.
    Pseudo instruction vmv.v.f vd, rs1 which expands to vfmerge.vf vd, v0, rs1

## Slide 28: Floating-Point Scalar Move Instructions
The floating-point scalar read/write instructions transfer a single value between a scalar f register and element 0 of as vector register. The instructions ignore LMUL and vector register groups.
Vfmv.f.s rd, vs2 # rd = vs2[0] (rs1=0)
If SEW > FLEN, the least-significant FLEN bits are transferred and the upper SEW-FLEN bits are ignored. If SEW < FLEN, the value is NaN-boxed (1-extended) to FLEN bits.
Vfmv.s.f vd, rs1 # vd[0] = rs1 (vs2=0)
If SEW < FLEN, the least-significant bits are copied and the upper XLEN-SEW bits are ignored. If SEW > FLEN, the value is NaN-boxed (1-extended) to SEW bits.
The other elements in the destination vector register ( 0 < index < VLEN/SEW) are zeroed. If vl=0, no operation is performed and the destination register is not updated.

## Slide 29
Thank You!

## Slide 30: FP Compare Instructions
FCMP
  The rm filed indicates FEQ, FLT and FLE
  FEQ (rs1=rs2), FLT (rs1 < rs2), FLE (rs1≦rs2)
  Writing 1 to the integer register rd if the condition holds, and 0 otherwise.
  FLT, FLE  performs a signaling comparisons
    An Invalid Operation exception is raised if either input is NaN.
  FEQ  performs a quiet comparison
    Only signaling NaN inputs cause an Invalid Operation exception
  For all three instructions, the result is 0 if either operand is NaN.

## Slide 31: Integer to FP (1/)
  Perform two’s complement when input is negative
  Source is Word: bit[43:0]={12’b0, int_num[31:0]}
    Word to SP/HP: rd_exp=31
  Source is 16-bit: bit[43:0]={12’b0, int_num[15:0], 16’b0}
    16-bit to SP/HP: rd_exp=15
  Source is 8-bit: bit[43:0]={12’b0, int_num[7:0], 24’b0}
    8-bit to HP: rd_exp=7
43 | 42 | 41 |  |  | … |  |  | 32 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 |  |  |  | … |  |  |  | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0L | R | [ |  |  |  |  |  |  |  | S |  |  |  |  |  | ]
SP
HP
Word operand
16-bit operand
FP format
12-bit
bit
8-bit operand

## Slide 32: Integer to FP (2/)
  Normalization:
    Count leading zero of bit[31:0] (LZD) (rd_exp’=rd_exp- lzd)
    Left shift 12 bits if target is SP
    Left shift bit[43:0] by lz_num[4:0] (5 level mux)
  Rounding: (25-bit adder needed: bit[44:20])
    Detect Sticky bit (st) (| bit[19:0])
    According to round mode and st, add 1 on LSB or on Round bit
    If bit[44](SP)/bit[32](HP)==1  exp+1, fraction=0
43 | 42 | 41 |  |  | … |  |  | 32 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 |  |  |  | … |  |  |  | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0L | R | [ |  |  |  |  |  |  |  | S |  |  |  |  |  | ]
SP
HP
Word operand
16-bit operand
FP format
12-bit
bit
8-bit operand

## Slide 33: FP to Integer
To use smaller rounding adder:
  Exp<23: rsh (23-exp), Leading 8 bits are 0
    need to be rounded (at least 1bit shifted to bit[7:0])
    Result integer = {8’b0, bit[31:8]}
  23 ≦ Exp ≦ 31: right shift (31-exp),
    no need to be rounded
    Result integer = {bit[31:0]}
8 7 0
8’b0
8 7 0
Round bit
No rounding is needed
31
31
result
result

## Slide 34: FP to 32/16/8 Bit Integer
  Right shift by sh_amount
    0<exp<23: sh_amount = 23-exp, then rounding by 25bit adder
      32bit_int[31:0] ={8’b0,bit[31:8]}
      16bit_int[15:0] = bit[23:8]
      8bit_int[7:0] = bit[15:8]
    exp >= 23: sh_amount = 31-exp, no rounding
      32bit_int[31:0]=bit[31:0]
      16bit_int: exception
      8bit_int: exception
31 | 30 | 29 | 28 |  |  |  |  |  |  |  |  | … |  |  |  |  |  |  |  | 9 | 8 | 7 | 6 | 5 | … | 2 | 1 | 0
23 | 22 | 21 |  |  | S | P |  |  |  |  |  |  |  |  |  |  |  | 3 | 2 | 1 | 0 |  |  |  |  |  |  | 
10 | 9 | 8 | 7 | 6 | H | P | 3 | 2 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | L | R | [ |  | S |  |  | ]
bit
To Rounding 25-bit Adder

## Slide 35: Convert Between SP and HP
SP to HP
  Right shift by (31-18=13)
    + (-exp-13) if target result is subnorm, i.e. -13>sp_exp>-25)
  Rounding
  Subnormal handling
    If SP input is subnorm: underflow
    If HP output is subnorm and hidden bit==1: set exp=1
HP to SP
  bit[31:0] = {hp[10:0],20’b0}
  Use LZD to left shift subnormal input
31 | 30 | 29 |  |  |  |  |  |  | 18 |  |  |  |  |  |  |  |  |  | 8 | 7 | 6 | 5 | … | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 L | R | [ |  | S |  |  | ]
bit
To be Rounded in 25-bit Adder

## Slide 36: Convert Between SP and Bfloat
SP to Bfloat
  Right shift by 31-15=16 bit (do not detect subnormal)
  Rounding
  Subnormal handling
    SP subnorm and Bfloat hidden bit==1  bfloat exp set to 1
Bfloat to SP
  sp[31:0] = {bfloat[15:0],16’b0}
31 | 30 | 29 |  |  |  |  |  |  |  |  |  | 15 |  |  |  |  |  |  | 8 | 7 | 6 | 5 | … | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 L | R | [ |  | S |  |  | ]
bit
To be rounded in 25-bit Adder

## Slide 37: Convert Between SP and HPxx
SP to HP
  Right shift by (31-18=13)
    + (-exp-13) if target result is subnorm, i.e. -15>sp_exp>-25)
  Rounding
  Subnormal handling
    If SP input is subnorm: underflow
    If HP output is subnorm and hidden bit==1: set exp=1
HP to SP
  bit[31:0] = {hp[10:0],20’b0}
  Use LZD to left shift subnormal input
31 | 30 | 29 |  |  |  |  |  |  | 18 |  |  |  |  |  |  |  |  |  | 8 | 7 | 6 | 5 | … | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 L | R | [ |  | S |  |  | ]
bit
To be Rounded in 25-bit Adder

## Slide 38: Convert Between SP and Bfloatxx
SP to Bfloat
  Right shift by 31-15=16 bit (do not detect subnormal)
  Rounding
  Subnormal handling
    SP subnorm and Bfloat hidden bit==1  bfloat exp set to 1
Bfloat to SP
  sp[31:0] = {bfloat[15:0],16’b0}
31 | 30 | 29 |  |  |  |  |  |  |  |  |  | 15 |  |  |  |  |  |  | 8 | 7 | 6 | 5 | … | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 L | R | [ |  | S |  |  | ]
bit
To be rounded in 25-bit Adder