## Slide 1: FP SIMD DIV/SQRT uArch
202104
Larry

## Slide 2: Agenda
List of abbreviation
Overview
Configuration
Interface
uArch Overview
FP DIV/SQRT/Estimation Instructions
Data Placement
Instruction list

## Slide 3: List of abbreviation (1/)
Abbreviation | Definition
DSU | Divider and Square Root Unit
LZC | Leading zero count

## Slide 4: List of parameter (1/)
Abbreviation | Definition
XLEN | The current width of an x register in bits (32 for RV32 or 64 for RV64)
FLEN | The current width of a f register in bits (32 for SP, 64 for DP)

## Slide 5: Overview (1/)
2-stage pipeline
Supported data types
Instruction handling
  FP DIV/SQRT instruction using radix-4 SRT algorithm
  FP estimation instruction using look-up table
Precision | Width | Sign | Expo | Mant
HP | 16 | 1 | 5 | 10
SP | 32 | 1 | 8 | 23
DP | 64 | 1 | 11 | 52

## Slide 6: Overview (2/)
Instruction latency
*DIV/SQRT instruction have not forwarding path
x is not supported
Instruction | Latency |  |  | 
 | Scalar |  | Vector | 
DIV/SQRT | HP | 13* | HP | 13*
 | SP | 20* | SP | 20*
 | DP | 34* | DP | 34*
VFRECE7 | x | x | 3* | 
VFRSQRTE7 | x | x | 3* | 

## Slide 7: Configurability
Feature | Options
XLEN | 64
FLEN* | 16/32/64
VLEN | 512/256/128
SIMD_WIDTH | 512/256/128
ELEN* | 32/64
*If RVV = 0, FLEN can be configured to 32/64
*If RVV = 1, FLEN is equivalent to ELEN

## Slide 8: Interface

## Slide 9: Pipe Interface (1/)
Module name is vc_vfp_fdiv_simd64.v
Supported FLENs are 32/64 and XLEN is the same with FLEN
Hierarchy diagram

## Slide 10: Pipe Interface (2/)
Signal name | Type | Description
core_clk | Input | Clock
core_reset_n | Input | Negative Edge Reset
f1_valid[3:0] | Input | Valid signal
f1_ex_ctrl[4:0] | Input | Control signal for encoding. More info in instruction encoding slide.
f1_sew[2:0] | Input | Indicate element width
f1_ediv[1:0] | Input | Un-used
f1_round_mode[2:0] | Input | Round mode. 3’b000: RNE, 3’b001: RTZ, 3’b010: RDN, 3’b011: RUP, 3’b100: RMM
f1_op1_data[63:0] | Input | Source oprand1. The format is {DP}, {SP, SP} or {HP, HP, HP, HP}. DP, SP and HP width are 64-bit, 32-bit and 16-bit
f1_op2_data[63:0] | Input | Source oprand2. The format is {DP}, {SP, SP} or {HP, HP, HP, HP}. DP, SP and HP width are 64-bit, 32-bit and 16-bit

## Slide 11: Pipe Interface (3/)
Signal name | Type | Description
f2_wdata_en[7:0] | Output | Byte write enable.
f2_wdata[63:0] | Output | Result data. Result format is {DP}, {SP, SP} or {HP, HP, HP, HP}. DP, SP and HP width are 64-bit, 32-bit and 16-bit
f2_flag_set[4:0] | Output | Result flag {Invalid Operation (nv), Divide by zero (dz), overflow(of), underflow(uf), Inexact(nx)}

## Slide 12: uArch overview

## Slide 13: FDIV uArch (1/)
*Remainder and rounding adder blocks share 67-bit adder

## Slide 14: FDIV uArch (2/)
Div instruction datapath
  Step 1: Normalize source value
  Step 2: Compute result by DSU
  Step 3: Calculate sticky
  Step 4: Shift right for subnormal
  Step 5: Do rounding
Sqrt instruction datapath
  Step 1: normalize source value
  Step 2: Compute result by DSU
  Step 3: Calculate sticky
  Step 4: Shift right for subnormal
  Step 5: Do rounding

## Slide 15: FDIV uArch (3/)
Vector estimation instruction

## Slide 16: FDIV uArch (4/)
DSU Datapath
  Input
  Output
For 2’sc

## Slide 17: FDIV uArch - Compare (5/)
For 1 element
For 4 elements
Red circles indicates shared logics

## Slide 18: FDIV uArch - Compare (6/)
For 1 element
For 4 elements
Red circles indicates shared logics

## Slide 19: FP DIV/SQRT/Estimation Instructions

## Slide 20: FP DIV/SQRT/Estimation Instructions
The detail is FDIV_design_spec in T:\users\klmn\larryzzr\FP_design_spec_Larry\FDIV

## Slide 21: Data Alignment

## Slide 22: Data Alignment – DSU (1/)
The shared divisor keep normalized significand. We tend to align LSB and use masks to pick needed bits up then to generate the corresponding selected divisor/sqrt operand
e0
e1
e2
e3
e0
e1
e2
e3

## Slide 23: Data Alignment – DSU (2/)
The shared 3:2 CSA calculate sum and carry words and source data align MSB and just use masks to disable unneeded part of selected divisor/sqrt operand and then do logic-or to get final divisor/sqrt operand
e0
e1
e2
e3

## Slide 24: Data Alignment – VFP_FIV64 (3/)
The shared staging flop keep data for remainder adder, quotient/ quotient-1 from DSU and rounding adder. We need to find data alignment for the following path to get minimize area or highest freq.
  3:2 CSA  Staging flop  3:2 CSA
    Keep original data alignment
  3:2 CSA  Staging flop  Remainder adder
  Current_qr(Quotient)  Staging flop  Subnormal
  Subnormal shifter  Staging flop  Rounding adder

## Slide 25: Data Alignment – VFP_FIV64 (4/)
The data flow is 3:2 CSA  Staging flop  Remainder adder
  TYPE1: Align data after staging flop
    Extra multiplexer logics
    May affect timing (mux + 67-bit adder + sticky gen)
  TYPE2: Align data before staging flop
    Extra multiplexer logics
    Use more 3 FFs to keep aligned data
TYPE2
TYPE1
align
align
Remainder Adder
Remainder Adder
Staging FFs
Staging FFs
3:2 CSA
3:2 CSA
TYPE1
TYPE2

## Slide 26: Data Alignment – VFP_FIV64 (5/)
The data flow is Current_qr  Staging flop  Subnormal shifter
  The data align to LSB and it is better for subnormal shifter because we can generate round and sticky bit easily.

## Slide 27: Data Alignment – VFP_FIV64 (6/)
Subnormal shifter  Staging flop  Rounding adder
  Align data before staging flop
    There is timing gap between subnormal shifter and staging flop. The extra multiplexer can be added to there and haven’t timing effect.
Subnormal shifter HP/ SP/ DP
Subnormal shifter
HP
Subnormal shifter
HP/ SP
Subnormal shifter
HP
Staging Flop
Rounding Adder
Mask and Logic-OR

## Slide 28: Data Alignment – VFP_FIV64 (7/)
Shared OR network for LZC align to MSB for counting leading zero and use mask to pick needed bits up. The following right Fig. is shared OR-network and the orange rectangle is shared gates under FLEN32
  Please note the figure is an example for 32-bit LZC

## Slide 29: Data Alignment – VFP_FIV64 (8/)
Shared normalization shifter structure is as below and use 4 16-bit normalizer and extra logics to support 1-DP, 2-SP, 4-HP normalization.

## Slide 30: Data Alignment – VFP_FIV64 (9/)
Use 1, 2 or 4 16-bit normalizer to shift HP, SP or DP
If the source data type is SP, we chain 2 16-bit normalizer to shift this data. Propagation path will propagate shifted out data from low part normalizer
  For DP, E0  E1  E2  E3
  For SP, E2  E3, E0  E1
propagate
propagate
Notes: sa[5] = DP & ~(|sig[63:32])
sa[4] = (DP|SP) & ~(|sig[63:48])
e3_sa[3:0] = (sa[5:4] == 0) ? E3_LZC[3:0] : (sa[5:4] == 1) ? E2_LZC[3:0] : (sa[5:4] == 2) ? E1_LZC[3:0] : E0_LZC[3:0] ;
e2_sa[3:0] = (sa[5:4] == 0) ? E2_LZC[3:0] : (sa[5:4] == 1) ? E1_LZC[3:0] : (sa[5:4] == 2) ? E0_LZC[3:0] : 0;
e1_sa[3:0] = (sa[5:4] == 0) ? E1_LZC[3:0] : (sa[5:4] == 1) ? E0_LZC[3:0] : (sa[5:4] == 2) ? 0 : 0 ;
e0_sa[3:0] = (sa[5:4] == 0) ? E0_LZC[3:0] : (sa[5:4] == 1) ? 0 : (sa[5:4] == 2) ? 0 : 0 ;

## Slide 31: Data Alignment – VFP_FIV64 (10/)
Shared subnormal shifter structure is as below and use 4 16-bit shifter and extra logics to support 1-DP, 2-SP, 4-HP subnormal shift.

## Slide 32: Data Alignment – VFP_FIV64 (11/)
Use 1, 2 or 4 16-bit shifter to shift HP, SP or DP
If the source data type is SP, we chain 2 16-bit shifter to shift the corresponding data. Propagation path will propagate shifted out data from high part shifter
  For DP, E3  E2  E1  E0
  For SP, E3  E2, E1  E0
propagate
propagate

## Slide 33: Data Alignment – DSU (12/)
The following table show reduced FFs and logics
Name | Before |  | After |  | Reduce FFs | 
FLEN | 64 | 32 | 64 | 32 | 64 | 32
Divisor | 99 | 70 | 53 | 48 | 46 | 22
Current_qr0/1 | 214 | 156 | 110 | 104 | 114 | 52
Counter | 15 | 14 | 5 | 4 | 10 | 10
ds_ctr_cs | 8 |  | 2 |  | 6 | 
ds_busy | 4 |  | 1 |  | 3 | 
 | 340 | 252 | 171 | 159 | 179 | 93
Name | Before |  | After |  | Reduced logics | 
FLEN | 64 | 32 | 64 | 32 | 64 | 32
3:2 CSA | 58-bit 3:2 CSA 29-bit 3:2 CSA 2x16-bit 3:2 CSA | 2x29-bit 3:2 CSA 2x16-bit 3:2 CSA | 64-bit 3:2 CSA |  | 55 FAs | 26 FAs

## Slide 34: Data Alignment – VFP_FIV64 (13/)
The following table show reduced FFs
Name | Before |  | After |  | Reduce FFs | 
FLEN | 64 | 32 | 64 | 32 | 64 | 32
Staging Flop | 238 | 180 | 128/134 | 128/134 | 110/104 | 52/46
ds_busy_d1 | 4 |  | 1 |  | 3 | 
f2_scalar_fpu_instr | 4 |  | 1 |  | 3 | 
f2_frs_hp | 4 |  | 1 |  | 3 | 
f2_frs_sp | 4 |  | 1 |  | 3 | 
f2_frs_dp | 4 |  | 1 |  | 3 | 
f2_round_mode | 12 |  | 3 |  | 9 | 
f2_div_instr | 4 |  | 1 |  | 3 | 
f2_sqrt_instr | 4 |  | 1 |  | 3 | 
f2_vfrece7_instr | 4 |  | 1 |  | 3 | 
f2_vfrsqrte7_instr | 4 |  | 1 |  | 3 | 
 | 286 | 228 | 140/146 | 140/146 | 146/140 | 88/82
The highlight(red) indicate that staging flop width is 67-bit

## Slide 35: Data Alignment – VFP_FIV64 (14/)
The following table show reduced logics
Name | Before |  | After | 
FLEN | 64 | 32 | 64 | 32
Remainder adder | 58-bit adder 29-bit adder 2x16-bit adder | 2x29-bit adder 2x16-bit adder | 67-bit adder | 2x33-bit adder
Rounding adder | 54-bit adder 25-bit adder 2x12-bit adder | 2x25-bit adder 2x12-bit adder | 57-bit adder* | 2x26-bit adder*
*if we reuse remainder adder, then we can reduce 57-bit adder or 2x26-bit adder.

## Slide 36: Data Alignment – Summary (15/)
The following table show reduced FFs
Name | Before |  | After |  | Reduce FFs | 
FLEN | 64 | 32 | 64 | 32 | 64 | 32
VFP_FDIV64+DSU | 626 | 480 | 311/317 | 299/305 | 325/329 | 181/175
SIMD_WIDTH=512 |  |  |  |  | 2600/2552 | 1448/1400
The highlight(red) indicate that staging flop width is 67-bit
Name | Before |  | After |  |  | Reduced logics | 
FLEN | 64 | 32 | 64 | 32 |  | 64 | 32
CSA | 58-bit CSA 29-bit CSA 2x16-bit CSA | 2x29-bit CSA 2x16-bit CSA | 64-bit CSA |  |  | 55 FAs | 26 FAs
Remainder adder | 58-bit adder 29-bit adder 2x16-bit adder | 2x29-bit adder 2x16-bit adder | 67-bit adder |  | 2x33-bit adder |  | 
Rounding adder | 54-bit adder 25-bit adder 2x12-bit adder | 2x25-bit adder 2x12-bit adder | 57-bit adder* |  | 2x26-bit adder* |  | 
*if remainder adder is reused, then we can reduce 57-bit adder or 2x26-bit adders.

## Slide 37: Instruction list

## Slide 38: Instruction list
The fdiv function unit encoding