## Slide 1: FP DIV/SQRT uArch
202101
Larry

## Slide 2: Agenda
List of abbreviation
Overview
Configuration
uArch Overview
FP DIV/SQRT Instructions
FP Estimation Instructions
Round digit generation
Twice Rounding Detection
Enhancements
Instruction list
Merge IDIV and FDIV methods

## Slide 3: List of abbreviation (1/)
Abbreviation | Definition
DSU | Divider and Square Root Unit
LZD | Leading zero detection
LZC | Leading zero count

## Slide 4: List of parameter (1/)
Abbreviation | Definition
XLEN | The current width of an x register in bits (32 for RV32 or 64 for RV64)
FLEN | The current width of a f register in bits (32 for SP, 64 for DP)

## Slide 5: Overview (1/)
2-stage pipeline
Supported data types
Instruction handling
  FP DIV/SQRT instruction using radix-4 SRT algorithm
  FP estimation instruction using look-up table
Precision | Width | Sign | Expo | Mant
HP | 16 | 1 | 5 | 10
SP | 32 | 1 | 8 | 23
DP | 64 | 1 | 11 | 52

## Slide 6: Overview (2/)
Instruction latency
*DIV/SQRT instruction can not be dispatch to function unit back-to-back and the instructions reduce 1 cycle.
x is not supported
Instruction | Latency |  |  | 
 | Scalar |  | Vector | 
DIV/SQRT | HP | 13* | HP | 13*
 | SP | 20* | SP | 20*
 | DP | 34* | DP | 34*
VFRECE7 | x | x | 3 | 
VFRSQRTE7 | x | x | 3 | 

## Slide 7: Configurability
Feature | Options
XLEN | 64
FLEN* | 16/32/64
VLEN | 512/256/128
SIMD_WIDTH | 512/256/128
ELEN* | 32/64
*If RVV = 0, FLEN can be configured to 32/64
*If RVV = 1, FLEN is equivalent to ELEN

## Slide 8: uArch overview

## Slide 9: VPU stage
Frontend
Function unit
Replace

## Slide 10: Function Unit Lane Hierarchy
src_gen is for source data selection
  Select data for read port 0/ 1/ 2/ 3 or scalar register
  Describe detail according to Chevy’s latest spec or v0/v1 decode table
ELEN=32
ELEN=64

## Slide 11: FDIV uArch (1/)
The original datapath
  Generate sticky 3 times
  Reduce staging FFs
  Rounding method

## Slide 12: FDIV uArch (2/)
The modified datapath
  Generate sticky 3  2 times
  Rounding method

## Slide 13: FDIV uArch (3/)
Div instruction datapath
  Step 1: Normalize source value
  Step 2: Compute result by DSU
  Step 3: Calculate sticky
  Step 4: Shift right for subnormal
  Step 5: Do rounding
Sqrt instruction datapath
  Step 1: normalize source value
  Step 2: Compute result by DSU
  Step 3: Calculate sticky
  Step 4: Shift right for subnormal
  Step 5: Do rounding

## Slide 14: FDIV uArch (4/)
Vector estimation instruction

## Slide 15: FDIV uArch (5/)
DSU Datapath
For 2’sc

## Slide 16: FP Div/SQRT Instructions

## Slide 17: FP Div/SQRT Instructions datapath
Div instruction datapath
  Step 1: Normalize source value
  Step 2: Compute result by DSU
  Step 3: Calculate sticky
  Step 4: Shift right for subnormal
  Step 5: Do rounding
Sqrt instruction datapath
  Step 1: normalize source value
  Step 2: Compute result by DSU
  Step 3: Calculate sticky
  Step 4: Shift right for subnormal
  Step 5: Do rounding

## Slide 18: FP Div/SQRT Instructions (1/)
Integer to floating-point dataflow
  Unpack source data
  Normalize significand and increase exponent
  Use DSU to compute result of div/sqrt
  Generate partial sticky
  Shift right significand and generate partial sticky if exponent value is subnormal
  Generate round digit
  Do rounding
Enhancements
  Reducing look-up table
  Reduce instruction latency (1 cycle)
  Reduce sticky generation times
  Modified rounding method
  Reduce 2 level adder to 1 level
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 19: FP Div/SQRT Instructions (2/)
Algorithm
    SRT algorithm
    DIV/SQRT look-up table
Recursive equation
  Div 
    is in the range [1.0, 2)
    is normalize divisor
    is in the range [-2/3d, 2/3d)
    is in the range [1.0, 2)
    Digit set () is [-2, -1, 0, 1, 2]
  Sqrt 
    is in the range [0.25, 1)
    is in the range [, )
    is in the range [0.5, 1)
    Digit set () is [-2, -1, 0, 1, 2]
    1st round of is 1.0
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 20: FP Estimation Instructions

## Slide 21: FP Estimation Instructions (1/)
Instruction dataflow
  Unpack input data
  Normalize data, compute exponent and detect special value in parallel
  Look-up vfrece7/vfesqrte7 table and do exception detection
  Calculate result exponent
  Shift right significand value if exponent is subnormal
  Produce special value according to the corresponding exception if detected
F1 stage works
  Normalize data
  Compute exponent
  Detect special value
F2 stage works
  Look-up vfrece7/vfesqrte7 table
  Do exception detection
  Shift right significand value if exponent is subnormal
  Produce special value according to the corresponding exception if detected
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 22: FP Estimation Instructions (2/)
Produce special value, exception flag according to the corresponding table in vector-spec
vfrsqrte7.v
vfrece7.v
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 23: Round digit generation & Twice Rounding Detection

## Slide 24: Round digit generation (1/)
Generate rounding increment according to rounding modes
Rounding modes
  RNE (Round to Nearest, ties to Even)
  RTZ (Round Towards Zero)
  RDN (Round DowN)
  RUP (Round UP)
  RMM (Round to nearest, ties to Max Magnitude)
  ROD (Round towards ODd)
Rounding increment under different rounding mode
Sign | L | R | S |  | RNE | RTZ | RDN | RUP | RMM | ROD
0 | 0 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +1
0 | 0 | 0 | 1 |  | +0 | +0 | +0 | +1 | +0 | +1
0 | 0 | 1 | 0 |  | +0 | +0 | +0 | +1 | +1 | +1
0 | 0 | 1 | 1 |  | +1 | +0 | +0 | +1 | +1 | +1
0 | 1 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +0
0 | 1 | 0 | 1 |  | +0 | +0 | +0 | +1 | +0 | +0
0 | 1 | 1 | 0 |  | +1 | +0 | +0 | +1 | +1 | +0
0 | 1 | 1 | 1 |  | +1 | +0 | +0 | +1 | +1 | +0
1 | 0 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +1
1 | 0 | 0 | 1 |  | +0 | +0 | +1 | +0 | +0 | +1
1 | 0 | 1 | 0 |  | +0 | +0 | +1 | +0 | +1 | +1
1 | 0 | 1 | 1 |  | +1 | +0 | +1 | +0 | +1 | +1
1 | 1 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +0
1 | 1 | 0 | 1 |  | +0 | +0 | +1 | +0 | +0 | +0
1 | 1 | 1 | 0 |  | +1 | +0 | +1 | +0 | +1 | +0
1 | 1 | 1 | 1 |  | +1 | +0 | +1 | +0 | +1 | +0

## Slide 25: Round digit generation (2/)
1. Do rounding only
  A + increment (1 bit) (A has not round bit)
Abbreviation
  L is LSB/ R is round bit / S is sticky bit / Tie is (R & ~S)
Rounding mode | Rounding inc
RNE (Round to Nearest, ties to Even) | 1. R then clear sum LSB if tie/ 2. R & (L ¦ S)
RTZ (Round Towards Zero) | 0
RDN (Round DowN) | ~sign & (R ¦ S)
RUP (Round UP) | sign & (R ¦ S)
RMM (Round to nearest, ties to Max Magnitude) | R
ROD (Round towards ODd) | 1. Set LSB 2. ~L

## Slide 26: Twice Rounding Detection

## Slide 27: Twice Rounding Detection (1/)
Do 1st rounding for normal format then the value should bound to subnormal format and do 2nd rounding.
  Normal format  Subnormal format  Round to normal value
The design just do rounding once and detect this case like as Fig.
Example
  SP(0x387FE000, exponent = -15, sig = 1.11111111110000000000000)  HP
  The result will be subnormal HP, so the function do round first and then bound to subnormal format.
  Normal format 1.1111111111 (do rounding)
  Bound to subnormal format 0.1111111111_1  raise underflow flag
  Bounded subnormal result should be round up to 1.0000000000_0

## Slide 28: Twice Rounding Detection (2/)
In this condition f2_round_adder_src1 is subnormal format because of exponent
  Detect bit pattern like as
    HP  0.1111111111
    SP  0.11111111111111111111111
    DP  0.111111111111111111111111111111111111111111111111111
To find the all one bit pattern (fraction and round bit) and other condition according to rounding mode. The following slide will describe it.

## Slide 29: Twice Rounding Detection (3/)
The table show all cases of asserting underflow under twice rounding case.
  Left V  subnormal to normal
  Right V  Assert underflow flag
  Assert special underflow flag if the condition have 2V.
  R: round bit
  Sm: MSB of sticky field
  St: other sticky field
  S = (Sm | St)
Sign | R | Sm | St |  | RNE |  | RTZ |  | RDN |  | RUP |  | RMM |  | ROD | 
0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 1 |  |  | V |  | V |  | V | V | V |  | V |  | V
0 | 0 | 1 | 0 |  |  | V |  | V |  | V | V | V |  | V |  | V
0 | 0 | 1 | 1 |  |  | V |  | V |  | V | V | V |  | V |  | V
0 | 1 | 0 | 0 |  | V | V |  | V |  | V | V | V | V | V |  | V
0 | 1 | 0 | 1 |  | V | V |  | V |  | V | V |  | V | V |  | V
0 | 1 | 1 | 0 |  | V |  |  | V |  | V | V |  | V |  |  | V
0 | 1 | 1 | 1 |  | V |  |  | V |  | V | V |  | V |  |  | V
1 | 0 | 0 | 0 |  |  |  |  |  |  |  |  |  |  |  |  | V
1 | 0 | 0 | 1 |  |  | V |  | V | V | V |  | V |  | V |  | V
1 | 0 | 1 | 0 |  |  | V |  | V | V | V |  | V |  | V |  | V
1 | 0 | 1 | 1 |  |  | V |  | V | V | V |  | V |  | V |  | V
1 | 1 | 0 | 0 |  | V | V |  | V | V | V |  | V | V | V |  | V
1 | 1 | 0 | 1 |  | V | V |  | V | V |  |  | V | V | V |  | V
1 | 1 | 1 | 0 |  | V |  |  | V | V |  |  | V | V |  |  | V
1 | 1 | 1 | 1 |  | V |  |  | V | V |  |  | V | V |  |  | V

## Slide 30: Twice Rounding Detection (4/)
A : Assert underflow flag.
The condition should qualify bit pattern and the following condition under different rounding mode
  RNE  R&~Sm
  RTZ  0
  RDN sign&(R^(Sm|St))  sign&(R^S)
  RUP  ~sign&(R^(Sm|St))  ~sign&(R^S)
  RMM  R&~Sm
  ROD 0
Sign | R | Sm | St |  | RNE | RTZ | RDN | RUP | RMM | ROD
0 | 0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 0 | 1 |  |  |  |  | A |  | 
0 | 0 | 1 | 0 |  |  |  |  | A |  | 
0 | 0 | 1 | 1 |  |  |  |  | A |  | 
0 | 1 | 0 | 0 |  | A |  |  | A | A | 
0 | 1 | 0 | 1 |  | A |  |  |  | A | 
0 | 1 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 0 | 1 |  |  |  | A |  |  | 
1 | 0 | 1 | 0 |  |  |  | A |  |  | 
1 | 0 | 1 | 1 |  |  |  | A |  |  | 
1 | 1 | 0 | 0 |  | A |  | A |  | A | 
1 | 1 | 0 | 1 |  | A |  |  |  | A | 
1 | 1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 | 1 |  |  |  |  |  |  | 

## Slide 31: Enhancements

## Slide 32: Enhancements (1/)
Reduce 2 gates delay
  1-A  1 + (~A+1)  2+~A
Reduce FFs
  Keep divisor RF(vc_vfp_dsu) value at ds_fraction_2 RF(vc_vfp_fdiv)
    Reduce 100-bit FFs per lane (2*(54(pipe0) +11(pipe1)+24(pipe2)+11(pipe3)))
Reduce 1 latency for div and sqrt
  Dispatch div/sqrt instruction 1 cycle early

## Slide 33: Instruction list

## Slide 34: Instruction list
The fdiv function unit encoding

## Slide 35: Merge IDIV and FDIV methods

## Slide 36: Merge IDIV and FDIV methods (1/)
Two methods to merge/fuse IDIV and FDIV function units.
  Merge two function units
    Reuse staging FFs and return result according to instruction type
  Fuse two function units
    Do 2’sc for input and output if negative
    Reuse radix-4 SRT look-up table
    Extend quotient handling logics
    Add Left shifting logic to handle integer result
    Hard to implement remainder instruction using SRT
Merge 2 function units
Fuse 2 function unit

## Slide 37: Backup

## Slide 38: Radix-2 divider using SRT (1/)
SRT named for its creators (Sweeney, Robertson, and Tocher)
Generate 1-bit partial remainder in 1 iteration
Quotient

## Slide 39: Radix-2 divider using SRT (2/)
Shifted partial remainder () is in the range [-2d, 2d)
Digit set
  -1  subtract -d
  0  subtract 0
  1  subtract d

## Slide 40: Radix-2 divider using SRT & CSA(1/)
Shifted partial remainder () is in the range [-2d, 2d)
Digit set
  -1  [-2d, -1/2)
  0  [-1/2, 0)
  1  [0, 2d)

## Slide 41: Radix-2 divider using SRT & CSA(2/)
Let and
Add the most significant 4 bits of u and v, t result may have 1 bit error (’b0.01 = 0.25) because of carry from low part. The threshold gap is greater than 0.25.
XXXX XXXX
XXXX XXXX
X
carry

## Slide 42: Radix-2 divider using SRT & CSA(3/)
The following Fig. is radix-2 divider datapath
Use sum of partial carry and sum string to select
BACK

## Slide 43: Radix-4 divider using SRT (1/)
SRT named for its creators (Sweeney, Robertson, and Tocher)
Generate 2-bit partial remainder in 1 iteration
Shifted partial remainder () is in the range [-4d, 4d)
Digit set

## Slide 44: Radix-4 divider using SRT (2/)
p is shifted partial remainder and d is divisor
(3 * divisor) is hard to implement so we want to restrict the quotient digits to [−2, 2] from [-3, 3] but we have some changes.

## Slide 45: Radix-4 divider using SRT (3/)
Restrict the quotient digits to [−2, 2] from [-3, 3]
  is in the range [-hd, hd)
  is in the range [-4hd, 4hd)
  We should be able to bring the worst-case values to within [-hd, hd) by adding ±2d to it
   

## Slide 46: Radix-4 divider using SRT (4/)
quotient digits to [−2, -1, 0, 1, 2] from [-3, -2, -1, 0, 1, 2, 3]
  is in the range [-d, d)
quotient digits is [−2, -1, 0, 1, 2]
  is in the range [-2/3d, 2/3d)

## Slide 47: Radix-4 SRT - Quotient Handling (1/)
Generate 2-bit partial quotient in each iteration and the corresponding value is {-2, -1, 0, 1, 2}. The final quotient like as 1. 1 -2 1 -1 1 2 but it can not use directly and the correct result is 1.020312.
The following will describe how to handle negative partial quotient.
  In each iteration, we should keep (partial quotient, ) and (partial quotient -1, )
  The next round can select (partial quotient -1) if the partial quotient is negative.
Example:
BACK
 |  |  | select |  | 
 |  | -2() |  |  | 
 |  | 1() |  |  | 
 |  |  | select |  | 

## Slide 48: Radix-4 DIV and SQRT –(1/)
DIV
  is in the range [-2/3d, 2/3d)
  Digit set () is [-2, -1, 0, 1, 2]
  is in the range [1.0, 2)
  is dividend
SQRT
  is in the range [-2/3, 2/3) [-4/3, 4/3)
  Digit set () is [-2, -1, 0, 1, 2]
    Digit set adjustment is for reducing look-up table
  is in the range [0.5, 1)
  is ((radicand >> 1) – 1)
2 | 3’b010 | 
1 | 3’b001 | 
0 | 3’b000 | 
-1 | 3’b111 | 
-2 | 3’b110 | 
2 | 3’b010 | 
1 | 3’b001 | 
0 | 3’b000 | 
-1 | 3’b111 | 
-2 | 3’b110 | 

## Slide 49: Radix-4 SRT Look-up Table (1/)
The Fig is DIV SRT look-up table.
Quotient of DIV is in [1, 2)
BACK
The Fig is SQRT SRT look-up table.
Quotient of SQRT is in [0.5, 1)

## Slide 50: Temporal Root selection for SQRT
SQRT instruction will use high-order root to take SRT look-up table then generate 2-bit quotient in each round. But root digit selection rule cannot be used for all iterations because root is unknown in early iterations.
The Fig. show value according to digit set and the corresponding bounded value are (1 * 4/3) , (0.75 * 4/3) and (0.5 * 4/3)
  0 1.00
  -10.11
  -20.10
The first round root is 0.1101
Notes: The sqrt result of each values
0.9375 => 0.9682458365518542212948163499456 0.1111
0.875 => 0.93541434669348534639593718307914 0.1110
0.8125 => 0.90138781886599732327980531686762 0.1110
0.75 => 0.86602540378443864676372317075294 0.1101
0.6875 => 0.82915619758884996227873318416767 0.1101
0.625 => 0.79056941504209483299972338610818 0.1100
0.5625 => 0.75 0.1100
0.5 => 0.70710678118654752440084436210485 0.1011

## Slide 51: Look-up Table Adjustment
Merge div & sqrt look-up
  Merge the look-up tables
Lib | Feq. | Original | Modified
28HPC+ | 1Ghz | 21.3kgates | 21.2kgates
28HPC+ | 1.25Ghz | 22.7kgates | 22.5kgates