## Slide 1: FP MISC uArch
202012
Larry

## Slide 2: Agenda
List of abbreviation/parameter
Overview
Configuration
Interface (TODO)
uArch overview
Conversion Instructions
Round digit/2’sc inc generation
Comparing & Others instructions
Cross Lane Forwarding Path
Enhancements
Data Alignment
Instruction list
Instruction encoding (TODO)

## Slide 3: List of abbreviation (1/)
Abbreviation | Definition
F2I/F2F/I2F | F: Floating-point, I: integer
ABS | Alignment barrel shift
NBS | Normalization barrel shift
2’sc | 2’s complement
LZD | Leading zero detection
LZC | Leading zero count

## Slide 4: List of parameter (1/)
Abbreviation | Definition
XLEN | The current width of an x register in bits (32 for RV32 or 64 for RV64)
FLEN | The current width of a f register in bits (32 for SP, 64 for DP)
VLEN | Vector length
ELEN | Element width

## Slide 5: Overview (1/)
2-stage pipeline
Supported data types
  BFloat16/HP/SP/DP
  Int8/Int16/Int32/Int64
The followings are supported instructions and the corresponding latency
  Conversion (I2F, F2F, F2I)
  Comparing/min/max
  Sign injection/classify/move
Precision | Width | Sign | Expo | Mant
HP | 16 | 1 | 5 | 10
Bfloat16 | 16 | 1 | 8 | 7
SP | 32 | 1 | 8 | 23
DP | 64 | 1 | 11 | 52

## Slide 6: Overview (2/)
Instruction latency
Instruction | Latency |  |  | 
 | Scalar |  | Vector | 
Conversion | 2 |  | Widening | 2
 |  |  | Narrowing | 3
Sign injection | 2 |  | 2 | 
Min/max | 2 |  | 2 | 
Comparing | 1 |  | 2 | 
Classify | 1 |  | 2 | 
Move | toFRF | 2 | 2 | 
 | toXRF | 1 |  | 

## Slide 7: Configurability
Feature | Options
XLEN | 64
FLEN* | 16/32/64
VLEN | 512/256/128
SIMD_WIDTH | 512/256/128
ELEN* | 32/64
*If RVV = 0, FLEN can be configured to 32/64
*If RVV = 1, FLEN is equivalent to ELEN

## Slide 8: uArch overview

## Slide 9: VPU stage
Frontend
Function unit

## Slide 10: Function Unit Lane Hierarchy
src_gen is for source data selection
  Select data for read port 0/ 1/ 2/ 3 or scalar register
FSM is for reduction instructions to generate control signals
Lane_carry_control handle data forwarding between each lane
ELEN=32
ELEN=64

## Slide 11: FMIS uArch (1/)

## Slide 12: FMIS uArch (2/)
INT to FP

## Slide 13: FMIS uArch (3/)
FP to INT
Zero

## Slide 14: FMIS uArch (4/)
FP widening
FP narrowing
Bfloat16 to SP
Zero

## Slide 15: FMIS uArch (5/)
Comparing instructions
Others instructions
Scalar fp result (XRF)

## Slide 16: Conversion instructions

## Slide 17: Integer to FP Datapath
INT to FP

## Slide 18: Integer to FP (1/)
Integer to floating-point dataflow
  Data packing
  Do 3 things in parallel
    Do 2’sc for negative integer
    Generate LZC
    Find bit pattern for correction
  Normalize data and generate sticky bit
  Pack to significand format according destination precision
  Do rounding
Enhancements
  Detect Leading zero before 2’sc
  Structuralized OR network
  Rearrange data alignment for I2F
    Reduce selection multiplexers
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 19: Integer to FP (2/)
Data packing
  Reduce selection mux
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 20: Integer to FP (3/)
Normalization
  Calculate leading zero number
    Generate string for LZC (Detect Leading zero before 2’sc)
  Exponent calculation
    Rearrange data alignment for reducing selection mux
    Result expo = (XLEN – 1) – LZC (expo hasn’t bias)
  Apply structuralized OR network to calculate LZC
  Apply barrel shift to normalize source data
  Apply structuralized OR network to generate sticky bit
Rounding
  Generate round digit according to round mode and sticky
  Select (exponent) or (exponent+1) according to carry bit

## Slide 21: FP to Integer Datapath
FP to INT
Zero

## Slide 22: FP to integer (1/)
Floating to integer dataflow
  Data packing
  Right shift packed data according to difference of exponent
  Generate round digit
  Do rounding and 2’sc at the same time
Enhancements
  Rearrange data alignment for F2I
  Merge 64bit and 54bit adder

## Slide 23: FP to integer (2/)
Unpack and align data
  Align all precision source value at (XLEN - 1) bit like as following fig
Shift amount (exponent hasn’t bias)
  ABS should support 65 shift amount value when XLEN is 64`
    Shift all significand to sticky field
    Add logic to detect shift amout == 64, 65
  Apply 65-bit adder to handle (exponent < 64)
    Shift amount: (XLEN – 1) – exponent (exponent hasn’t bias)
Round digit/2’sc inc generation merge rounding and 2’sc steps

## Slide 24: FP to FP Datapath
FP widening
FP narrowing
Bfloat16 to SP
SP to Bfloat16

## Slide 25: FP to FP – Widening FP (1/)
Widening instruction dataflow
  Calculate LZC for subnormal value and do normalization
  No Rounding is needed
  No subnormal result
Data packing
  Align hidden one and calculate LZC
    Subnormal input will be shifted to normal fp format
  Packing data according to destination precision

## Slide 26: FP to FP – Narrowing FP (2/)
Narrowing instruction dataflow
  Calculate subnormal result flag
  Use subnormal result flag to select shift amount (shift to normal/subnormal)
  Calculate exponent without bias
  Generate shifted value and round digit
  Do rounding
Enhancement
  Rearrangement data alignment for narrowing FP
    Because 64-bit and 54-bit adders are merged.

## Slide 27: FP to FP – Narrowing FP (3/)
Calculate subnormal result flag
  Use exponent to detect that result may be subnormal value (exponent has bias)
    DP to SP subnormal (exponent - 1023 <= -127, exponent < 897)
    DP to HP subnormal (exponent - 1023 <= -15, exponent < 1009)
    SP to HP subnormal (exponent - 127 <= -15, exponent < 113)

## Slide 28: FP to FP – Narrowing FP (4/)
Shift amount
  If normal result, ABS shift input value to normal format
    DP to SP: 40
    DP to HP: 53
    SP to HP: 53
    SP to Bfloat16: 56
  If subnormal result, ABS shift input value to subnormal format
    DP to SP: – exponent – 127 + 40 + 1 = ~exponent + 1 – 86 = ~exponent – 85 (use +)
    DP to HP: – exponent – 15 + 53 + 1 = ~exponent + 1 + 39 = ~exponent + 40
    SP to HP: – exponent – 15 + 53 + 1 = ~exponent + 1 + 39 = ~exponent + 40
exponent hasn’t bias

## Slide 29: Round digit/2’sc inc generation

## Slide 30: Round digit/2’sc inc generation (1/)

## Slide 31: Round digit/2’sc inc generation (2/)
Do rounding and 2’sc at the same time or one of those
Merge rounding and 2’sc steps to improve critical path
No inclement LSB Inclement LSB0 Inclement LSB1
If rounding no inclement LSB => set inc=1
If rounding inclement LSB => set inc=0
If RNE tie clear LSB and LSB was 1 => set inc=1
  Round-bit=1 & round_digit=01 & LSB = 1
    should inclement LSB, but LSB will be cleared, so set inc=1
  No Round-to-odd in F2I instruction
3 round to 3
0011 -> 0011
2’s c: inv+1(inc)
1100
+ 1
-------- ---------
1101 1101
-3 -3
4 round to 5
0100 -> 0101
2’s c: inv+0(inc)
1011 1010
+ 1 + 1
-------- ---------
1100 1011
-4 -5
3 round to 4
0011 -> 0100
2’s c: inv+0(inc)
1100 1011
+ 1 + 1
-------- ---------
1101 1100
-3 -4
Add Proof steps
Notes: A is value after rounding
R is rounding inclement
B = A+R
Result = B’+1 = (A+R)’+1
R = 0, Result = A’+1
R = 1, Result = A’-1+1 = A’

## Slide 32: comparing & others instructions

## Slide 33: Comparing & Others instructions datapath
Comparing instructions
Others instructions
Scalar fp result (XRF)

## Slide 34: Comparing & Others Instructions
Comparing & others instruction block diagram detail
bf2s: bfloat16 to single

## Slide 35: Comparing Instructions
Comparing instructions
  Scalar: return 0/1
  Vector: Write the comparison result to a mask register
Min/Max instructions
  The rm field indicates MIN/MAX
  FMIN: Write the smaller of rs1 and rs2 to rd
  FMAX: Write the larger of rs2 and rs2 to rd
  The value −0.0 is considered to be less than the value +0.0.
  Both inputs are NaNs, the result is the canonical NaN.
  Only one operand is a NaN, the result is the non-NaN operand.
  Signaling NaN inputs raise the invalid operation exception, even when the result is not NaN.

## Slide 36: Others Instructions
Sign-injection instructions
  The result takes all bits except the sign bit form the vector vs2 operands.
  The rm (rounding mode) field indicates J[N]/JX
Classify instructions
  The 10-bit mask produced by this instruction is placed in the LSB of the result elements.
  This instruction is only defined for SEW=16b above, so the result will always fit in the destination elements.
Rd bit | Meaning
0 | rs1 is -inf
1 | rs1 is a -normal number
2 | rs1 is a -subnormal number
3 | rs1 is -0
4 | rs1 is +0
5 | rs1 is a +subnormal number
6 | rs1 is a +normal number
7 | rs1 is +inf
8 | rs1 is a signaling NaN
9 | rs1 is a quiet NaN

## Slide 37: Cross Lane datapath

## Slide 38: Narrowing & Mask Instruction Datapath
Narrowing and mask instruction format is special and those instruction result will go through to lower lane. (e.g. Lane 1 Lane 0)
The following instruction need to shift to narrowing format
  Lane produce result and pack result
  Lane_Carry_control pack result and duplicated

## Slide 39: Reduction Instructions Datapath
Reduction instruction data flow
  Do the corresponding operator to deal with each vector data
  Merge elements in lane first then merge remain results
VLEN=256, SIMD=256, LMUL=2, SEW=16, VL=VLMAX
Add FSM diag
Time

## Slide 40: Enhancements

## Slide 41: Enhancement list (1/)
Enhance sticky generation path (st1)
Detect Leading zero before 2’sc
Rearrange data alignment for I2F
Rearrange data alignment for F2I
Rearrange data alignment for narrowing FP
Merge 64bit and 54bit adder and non-conversion data path
MISC

## Slide 42: Structuralized OR network (1/)
LZC logic

## Slide 43: Structuralized OR network (2/)
LZC = 5d’13 = 5’b01101
LZC[4] = 0, L4_sticky = |bit[15:0]
LZC[3] = 1, L3_sticky = L4_sticky | 1’b0
LZC[2] = 1, L2_sticky = L3_sticky | 1’b0
LZC[1] = 0, L1_sticky = L2_sticky | bit[17:16]
LZC[0] = 1, L0_sticky = L1_sticky | (LZC[0]) ? bit[18] : |bit[19:18];
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0
0
1
1
0
1
or
or
Notes: l5_sticky = 1’b0
l4_sticky = (f1_s_lz_num[5] == 1’b1) ? l5_sticky :|bit[15:0]
L3_sticky = (f1_s_lz_num[5:4] == 2’b11) ? l4_sticky :
l4_sticky | (| bit[27:24])

## Slide 44: Structuralized OR network (3/)
BACK
Notes: l5_sticky = 1’b0
l4_sticky = (f1_s_lz_num[5] == 1’b1) ? l5_sticky :|bit[15:0]
L3_sticky = (f1_s_lz_num[5:4] == 2’b11) ? l4_sticky :
l4_sticky | (| bit[27:24])

## Slide 45: Leading zero detection before 2’sc (1/)
Generate LZC early
  What’s input string?

## Slide 46: Leading zero detection before 2’sc (2/)
String for LZD is invert negative integer value
LZD 1-bit error
  Example
    A  8’b11110000 (neg integer) (1+0*)
    A 1’sc  8’b00001111  LZC = 4, sticky = 0, nds_dat = 8’b00000000
    A 2’sc  8’b00010000  LZC = 3, sticky = 0, nds_dat = 8’b10000000
  Correction
    LZC minus 1
      LZC = LZC – 1 (4 – 1 = 3)
    Sticky is zero because all source is shifted out
      Sticky = 0
    Set MSB of normalization data
      Nor_data = 8’b10000000 (8’b00000000 | 8’b10000000)

## Slide 47: Leading zero detection before 2’sc (3/)
Bit pattern detection

## Slide 48: Leading zero detection before 2’sc (4/)
Plan A:
  Timing is better than Plan B
  Extra logics
    6-bit subtractor
    1-bit or gate
Plan B:
  Extra logic
    6-bit subtractor
BACK

## Slide 49: Rearrange data alignment for I2F (1/)
Modify integer value alignment from 63-bit to 0-bit
  Reduce data type selection
For FLEN 32 (pipe0, pipe2)
  Just force lz_num[5] to 1’b1
For FLEN 16 (pipe1, pipe3)
  Just force lz_num[5:4] to 2’b11
lz_num is leading zero count
After 2’sc

## Slide 50: Rearrange data alignment for I2F (2/)
The following show reduced multiplexers
BACK

## Slide 51: Rearrange data alignment for F2I (1/)
Apply a 65-bit adder and keep round bit at [-1]
65-bit adder
BACK

## Slide 52: Rearrange data alignment for narrowing FP (1/)
This rearrangement is for merging two adders
All destination result types are aligned at LSB
  ABS should support 65-bit right shift
BACK

## Slide 53: Merge 64bit and 54bit adder (1/)
Use 65-bit adder to do 64-bit 2’sc and 54-bit rounding
  LSB of 65-bit is for round bit
Rearrange data alignment for all conversion instructions
Adjust shift amount according to changing alignment
BACK

## Slide 54: MISC (1/)
Move logics before 65-bit adder to F1 stage if meet target timing
Generate exp_inc before 65-bit adder
  Bit pattern detection

## Slide 55: Interface

## Slide 56: Back-End Hierarchy

## Slide 57: Function Unit Interface

## Slide 58: VFP_FMIS Interface (1/)
Signal name | Type | Description
core_clk | Input | Clock
core_reset_n | Input | Negative Edge Reset
lane_pipe_id_0 | Input | ID
f1_valid | Input | 
f1_fmis_scalar_valid | Input | Indicate scalar type instruction
f1_ex_ctrl | Input | Control signal for encoding
f1_sew | Input | Indicate element width
f1_ediv | Input | Un-used
f1_round_mode | Input | Round mode
f1_widen | Input | Widening instruction
f1_narrow | Input | Narrowing instruction
f1_sign | Input | Signed integer source
f1_vmask | Input | Mask

## Slide 59: VFMIS_64 Interface (2/)
Signal name | Type | Description
f1_op1_invalid | Input | 
f1_op2_invalid | Input | 
f1_op1_data | Input | 
f1_op2_data | Input | 
f1_cmp_inv_op | Output | 
f1_wdata_en | Output | 
f1_wdata | Output | 
f2_result_type | Output | 
f2_cmp_result | Output | 
f2_narr_wdata | Output | 
f2_wdata_en | Output | 
f2_wdata | Output | 
f2_flag_set | Output | 

## Slide 60: Instruction List

## Slide 61: Supported scalar fp instruction list (1/)
Sign-injection instruction
  fsgnj.[hsd]
  fsgnjn.[hsd]
  fsgnjx.[hsd]
Compare instruction
  feq.[hsd]
  flt.[hsd]
  fle.[hsd]
Classify instruction
  fclass.[hsd]
Move instruction
  fmv.x.[hwd]
  fmv.[hwd].x

## Slide 62: Supported scalar fp instruction list (2/)
Conversion between int and fp
Conversion between fp and fp
Int width\fp_width | F16(HP) | F32(SP) | F64(DP)
I32 | fcvt.w.h fcvt.wu.h fcvt.h.w fcvt.h.wu | fcvt.w.s fcvt.wu.s fcvt.s.w fcvt.s.wu | fcvt.w.d fcvt.wu.d fcvt.d.w fcvt.d.wu
I64 | fcvt.l.h fcvt.lu.h fcvt.h.l fcvt.h.lu | fcvt.l.s fcvt.lu.s fcvt.s.l fcvt.s.lu | fcvt.l.d fcvt.lu.d fcvt.d.l fcvt.d.lu
SRC \ DST | F16(HP) | Bfloat16 | F32(SP) | F64(DP)
F16(HP) | X | X | fcvt.s.h | fcvt.d.h
Bfloat16 | X | X | fcvt.s.bf16 | X
F32(SP) | fcvt.h.s | fcvt.bf16.s | X | fcvt.d.s
F64(DP) | fcvt.h.d | X | fcvt.s.d | X

## Slide 63: Supported vector fp instruction list (1/)
14.11. Vector Floating-Point MIN/MAX Instructions
  Floating-point minimum
    vfmin.vv vd, vs2, vs1, vm # Vector-vector
    vfmin.vf vd, vs2, rs1, vm # Vector-scalar
  Floating-point maximum
    vfmax.vv vd, vs2, vs1, vm # Vector-vector
    vfmax.vf vd, vs2, rs1, vm # Vector-scalar
14.12. Vector Floating-Point Sign-Injection Instructions
  For vfsgnj, the result’s sign bit is v/rs1’s sign bit.
    vfsgnj.vv vd, vs2, vs1, vm # Vector-vector
    vfsgnj.vf vd, vs2, rs1, vm # Vector-scalar
  For vfsgjn, the result’s sign bit is the opposite of v/rs1’s sign bit.
    vfsgnjn.vv vd, vs2, vs1, vm # Vector-vector
    vfsgnjn.vf vd, vs2, rs1, vm # Vector-scalar
  For vfsgnjx, the sign bit is the XOR of the sign bits of v/rs1 and vs2.
    vfsgnjx.vv vd, vs2, vs1, vm # Vector-vector
    vfsgnjx.vf vd, vs2, rs1, vm # Vector-scalar

## Slide 64: Supported vector fp instruction list (2/)
14.13. Vector Floating-Point Compare Instructions
  Compare equal
    vmfeq.vv vd, vs2, vs1, vm # Vector-vector
    vmfeq.vf vd, vs2, rs1, vm # Vector-scalar
  Compare not equal
    vmfne.vv vd, vs2, vs1, vm # Vector-vector
    vmfne.vf vd, vs2, rs1, vm # Vector-scalar
  Compare less than
    vmflt.vv vd, vs2, vs1, vm # Vector-vector
    vmflt.vf vd, vs2, rs1, vm # Vector-scalar
  Compare less than or equal
    vmfle.vv vd, vs2, vs1, vm # Vector-vector
    vmfle.vf vd, vs2, rs1, vm # Vector-scalar
  Compare greater than
    vmfgt.vf vd, vs2, rs1, vm # Vector-scalar
  Compare greater than or equal
    vmfge.vf vd, vs2, rs1, vm # Vector-scalar

## Slide 65: Supported vector fp instruction list (3/)
14.14. Vector Floating-Point Classify Instruction
  vfclass.v vd, vs2, vm # Vector-vector
14.15. Vector Floating-Point Merge Instruction
  vfmerge.vfm vd, vs2, rs1, v0 # vd[i] = v0.mask[i] ? f[rs1] : vs2[i]
14.16. Vector Floating-Point Move Instruction
  vfmv.v.f vd, rs1 # vd[i] = f[rs1]
14.17. Single-Width Floating-Point/Integer Type-Convert Instructions
  vfcvt.xu.f.v vd, vs2, vm # Convert float to unsigned integer.
  vfcvt.x.f.v vd, vs2, vm # Convert float to signed integer.
  vfcvt.rtz.xu.f.v vd, vs2, vm # Convert float to unsigned integer, truncating.
  vfcvt.rtz.x.f.v vd, vs2, vm # Convert float to signed integer, truncating.
  vfcvt.f.xu.v vd, vs2, vm # Convert unsigned integer to float.
  vfcvt.f.x.v vd, vs2, vm # Convert signed integer to float.

## Slide 66: Supported vector fp instruction list (4/)
14.18. Widening Floating-Point/Integer Type-Convert Instructions
  vfwcvt.xu.f.v vd, vs2, vm # Convert float to double-width unsigned integer.
  vfwcvt.x.f.v vd, vs2, vm # Convert float to double-width signed integer.
  vfwcvt.rtz.xu.f.v vd, vs2, vm # Convert float to double-width unsigned integer truncating.
  vfwcvt.rtz.x.f.v vd, vs2, vm # Convert float to double-width signed integer truncating.
  vfwcvt.f.xu.v vd, vs2, vm # Convert unsigned integer to double-width float.
  vfwcvt.f.x.v vd, vs2, vm # Convert signed integer to double-width float.
  vfwcvt.f.f.v vd, vs2, vm # Convert single-width float to double-width float.
14.19. Narrowing Floating-Point/Integer Type-Convert Instructions
  vfncvt.xu.f.w vd, vs2, vm # Convert double-width float to unsigned integer.
  vfncvt.x.f.w vd, vs2, vm # Convert double-width float to signed integer.
  vfncvt.rtz.xu.f.w vd, vs2, vm # Convert double-width float to unsigned integer truncating.
  vfncvt.rtz.x.f.w vd, vs2, vm # Convert double-width float to signed integer truncating.
  vfncvt.f.xu.w vd, vs2, vm # Convert double-width unsigned integer to float.
  vfncvt.f.x.w vd, vs2, vm # Convert double-width signed integer to float.
  vfncvt.f.f.w vd, vs2, vm # Convert double-width float to single-width float.
  vfncvt.rod.f.f.w vd, vs2, vm # Convert double-width float to single-width float rounding towards odd.

## Slide 67: Supported vector fp instruction list (5/)
15.3. Vector Single-Width Floating-Point Reduction Instructions
  vfredmax.vs vd, vs2, vs1, vm # Maximum value
  vfredmin.vs vd, vs2, vs1, vm # Minimum value
Custom instruction
  vfwcvt.s.bf16 vd, vs2, vm
  vfncvt.bf16.s vd, vs2, vm

## Slide 68: Backup

## Slide 69: Data alignment

## Slide 70: Data Alignment (1/)
XLEN = 64 and FLEN = 64 (For pipe0)

## Slide 71: Data Alignment (2/)
XLEN = 32 and FLEN = 32 (For pipe0, pipe2)
XLEN = 16 and FLEN = 16 (For pipe1, pipe3 )

## Slide 72: Rounding mode (1/)
Alternative rounding options are also available. IEEE 754 specifies the following rounding modes:
  round to nearest
    where ties round to the nearest even digit in the required position (the default and by far the most common mode)
  round to nearest
    where ties round away from zero (optional for binary floating-point and commonly used in decimal)
  round up (toward +∞;)
    negative results thus round toward zero
  round down (toward −∞)
    negative results thus round away from zero
  round toward zero (truncation)
    it is similar to the common behavior of float-to-integer conversions, which convert −3.9 to −3 and 3.9 to 3

## Slide 73: Rounding mode (2/)
Sign,LSB,round,stick | RNE | RTZ | RDN | RUP | RMM
0_000 | +0 | +0 |  |  | 
0_001 | +0 | +0 |  |  | 
0_010 | +0 | +0 |  |  | 
0_011 | +1 | +0 |  |  | 
0_100 | +0 | +0 |  |  | 
0_101 | +0 | +0 |  |  | 
0_110 | +1 | +0 |  |  | 
0_111 | +1 | +0 |  |  | 
1_000 | +0 | +0 |  |  | 
1_001 | +0 | +0 |  |  | 
1_010 | +0 | +0 |  |  | 
1_011 | +1 | +0 |  |  | 
1_100 | +0 | +0 |  |  | 
1_101 | +0 | +0 |  |  | 
1_110 | +1 | +0 |  |  | 
1_111 | +1 | +0 |  |  |