## Slide 1: VFMAC Design Spec

## Slide 2: Interface
input | Bit width | Description
core_clk | 1 | clock signal
core_reset_n | 1 | reset signal, active low
lane_pipe_id0 | 1 | indicates whether this is pipe0 of lane0, which also takes scalar operations
f1_valid | 1 | valid input
f1_round_mode | 3 | rounding mode
f1_ex_ctrl | 5 | operation, see andes_vip/patterns/plan/Vector_inst_decode_v0stage.xlsx for encodings
f1_sew | 2 | element width 0:reserved 1:16-bit 2:32-bit 3:64-bit
f1_ediv | 2 | unused
f1_op_wide | 1 | widening operation

## Slide 3: Interface
input | Bit width | Description
f1_op1/2/3 | 64 | operands 1/2/3: op1 * op2 + op3
f1_op_mask | 1 | indicates whether the input operand is masked used with ordered reduction to bypass un-canonicalized operand
f1_op1/3_hp | 1 | indicates op1/3 is in HP format
f1_align_amount_adjustment | 10 | a value to adjust the alignment amount (this is for timing consideration, move the calculation to F0)
f1_op1/2/3_subnormal_hp | 1 | indicates operand1/2/3 is a subnormal value in HP format
f1_op1/2/3_subnormal_sp | 1 | indicates operand1/2/3 is a subnormal value in SP format

## Slide 4: Interface
output | Bit width | Description
f4_wdata_en | 1 | valid output
f4_wdata | 64 | output data of operation
f4_flag_set | 5 | exceptions {invalid, divide-by-zero, underflow, overflow, inexact}
f4_result_type | 2 | result format 0: reserved 1: half-precision/bfloat16 2: TF32 3: reserved

## Slide 5: instruction list
addition
  fadd/vfadd/vfwadd: a*1+c
  fsub/vfsub/vfwsub/vfrsub: a*1-c
multiply
  fmul/vfmul/vfwmul: a*b+0
mac
  fmadd/vfmadd/vfmacc/vfwmacc: a*b+c
  fmsub/vfmsub/vfmsac/vfwmsac: a*b-c
  fnmsub/vfnmsub/vfnmsac/vfwnmsac: -(a*b)+c
  fnmadd/vfnmadd/vfnmacc/vfwnmacc: -(a*b)-c
reduction
dot-product

## Slide 6: V2/F0 stage
Reduction/dot-product FSM
src_gen: VRF, scalar FRF selection
Constant generation
  constant 1 for addition
  constant 0 for multiplication: 0 for multiply is generated in F1, because dot-product needs f1_op3 to backup the addend
    delay might be hide into
Operand SEW adjustment for widening operations
Pipe valid generation from FSM/mask

## Slide 7: Data Path
expA
161-bits align. shifter
inv
csa(56-a+b-c-bias)
encode
4:2 CSA
partial product reduction
f2
expB
expC
fracC
fracA
fracB
f1
partial sticky: st1
3:2 CSA
HA carry
HA inv. carry
HA sum
LZA pos + neg
f3
sign detection
normalization
55msb
106lsb
special value detection
Eff. sub
Eff. sub
107lsb
st1
complement
LZA string
OR network
eff. sub
d
f4
Part of dual adder
Part of dual adder
eff. sub
d
LZCsubnorm[6]
LZCsubnorm[5]
LZCsubnorm[0]
d<0
Left shift 54 bits

## Slide 8
RI = RUP & ~final_sign | RDN & final_sign
neg (a*b) + sub(c)
eff_sub = (neg ^ sign_a ^ sign_b) ^ (sub ^ sign_c)
final sign = eff_sub &comp. | (sub ^ sign(c))
RN = RNE | RMM
0 50 51 54 55 161
x.x........x xxxx x......x
DP as an example
format
after normalization
Rest dual adder
S+1 S
51
4-bit adder
3
107
st1
carry
carry/sticky calc
5-bit adder
5-bit adder
round decision
LSB correction
Y0[161] | Y1[161] & Z[4]
Y0[161:111]
Y1
Z
sticky
sticky
RI
Y0[161]

## Slide 9: F1: 4:2 CSA
Don’t cascade two FAs directly, convert it to canonical form
Propagation Delay is about 1.5 times of 3:2 CSA

## Slide 10: F1: Modified Booth Encoding
Partial product is sign-extended when encoded as -1X or -2X
To eliminate the width of CSA arrays:
  invert the MSB of sign-extension bit of the multiplicand and rewrite the partial product into the grey background part + our new partial product:
The carry chain will be the same. But with the greyed out constants for sign-extension, we can add them together:

## Slide 11: F1: Addend Alignment and Partial Sticky Bit Generation
d = expC` - expA` + expB` - bias
Alignment amount = 56-d

## Slide 12: F2: LZA
LZA pos
sign detection
LZA string
OR network
LZA neg
delay = log(64)
LZA pos
sign detection
LZA string
OR network
LZA neg
LZA string
OR network
LZA
A-B
LZA string
OR network
LZA
B-A
LZA eff. add
long latency
low cost
extra LZD cost
extra positive LZA cost
latency
AX25V100 | A25 series

## Slide 13: F2: LZA
Identify
To combine W>0 and W<0 string, extra wi-1 should be considered

## Slide 14: F2: LZA
Only applicable to X-Y case, both X and Y > 0
Leading zero of X+Y can’t simply derive from max(expX, expY)
  Normal + Normal * Sub-Normal
  1.x * 2-1020 + x.x * 2-1020 =>
Normal * Sub-Normal produces a case

## Slide 15: F2: Sign Detection
using tree comparator
  A + B => complemnt = 0
  A – B => compared with ~B
    when A = ~B then A < B

## Slide 16: F3: Normalization, sub-normal prediction
LZCsubnorm = (56-d) < 0 ? expC’ – expsubnorm
expA’ + expB’ + 56 - expsubnorm
x
x
…
x
x
x
…
x
x
Cinv
A*B
56-d < 0
53
106
x
x
…
x
x
x
…
x
x
106
d = 1
x
x
…
x
x
x
…
x
x
106
d < 0
expC’ – LZC <= expsubnorm
expA’ + expB’ + 56 – LZC <= expsubnorm
expA’ + expB’ + 56 – LZC <= expsubnorm
for DP, expsubnorm=-1023
d = expC’ – (expA’ + expB’)
56-d < 0
56-1
56-d
LZC
LZC
LZC[6] < LZCsubnorm[6]
LZC[5] < LZCsubnorm[5]
LZC[0] < LZCsubnorm[0]
Final LZC selection

## Slide 17: F4: sticky bit generation
Evalution of A+B=K Conditions Without Carry Propagation

## Slide 18: subnormal
Input
  hidden 1 should be calculated from exponent
Result
  right shift needed?
  shift amount adjustment

## Slide 19: critical path improvement opportunity
hidden 1 generation before partial sum encoding
  no optimize
    3:2 csa, latency = 1, 53-bit -> 27 partial product + 1 carry array
      27 -> 18 -> 12 -> 8+1 -> 6 -> 4 ->3-> 2 = 7
    4:2 csa, latency = 1.5
      27+1 -> 14 -> 6+2 -> 4 -> 2 = 6
  (a.x * b.y) = (ab+ay)+bx+xy :27+1 + 2 PPs
    4:2 csa
      27+1 -> 14+2 -> 8 -> 4 -> 2 = 6
  summarize slow parts to one partial product:26+1+2 PPs
    4:2 csa
      26 -> 12+2+2 -> 8+1 -> 6 -> 4 -> 2 = 6.5
stick bit and final exponent selection on fraction = 0
  can’t reuse A+PP CSA with A+B=K equation, the CSA used in F2 is A + PP
  A+B=K  A+B+~K = -1  2C + S = -1  2C = ~S
carry
slow bits

## Slide 20: Multiplication subnormal corner case

## Slide 21: backup slides

## Slide 25
dual adder
S+1 S
3-bit CSA
adders
LSB correction
carry
sticky
RI
RI|RN
4
4
carry
R
0 50 51 53 54 161
x.x........x xxx x......x
51
3
108
RN
LSB
DP as an example
format
after normalization
st1
comp