## Slide 1: Mpcore Low Power Interfeace
20190612
Jimmy

## Slide 2: MP System
ACU & L2
Core 0
Dtag 0
Core 1
Dtag 1
SMU
Sleep Handshake
clock
Power Control Register R/W
Bus Decode
Clock gen
Xtal
PLL
Clock enable

## Slide 3: Low Power Signals
PCS Interface
rdy_for_snoop[3:0]
sleep_req[3:0]
sleep_ok[3:0]
core_wfi_mode | core is in wait for interrupt mode
rdy_for_snoop | D$ & Dtag initial done and can accept snoop request
sleep_req | Request coreX to quit SMP and enter sleep mode
sleep_ok | CoreX is ready to enter sleep mode
Mpcore
Core
Core
Core
core_wfi_mode[3:0]
SMU
L2_IDLE
L2C
srrep_done[3:0]

## Slide 4: Sleep Mode
1
Step | Signal | Condition
0 | rdy_for_snoop assert | D$ & Dtag initail done
1 | Smpen asserrt | (rdy_snoop =1) & ~(sleep_req & wfi)
2 | Sleep_req assert | Set SMU sleep mode command
3 | core_wfi_mode | Core executes WFI instruction & all bus request is done
4 | Smpen deasserrt | sleep_req & wfi
5 | Sleep_ok assert | Core_wfi_mode =1 & sleep_req=1 & all srresp has been returned
6 | Ipi assert | Inter process interrupt to wakeup core
7 | Sleep_ok deassert | Sleep_req is deassert
3
2
4
5
6
7

## Slide 5: Signals
input l2c_clk;
input l2c_reset_n;
input mX_savalid;
input mX_saready;
input mX_srvalid;
input mX_srready;
input mX_srresp[1];
input mX_sdvalid;
input mX_sdready;
input hartX_core_wfi_mode input mX_rdy_for_snoop input pcs_coreX_sleep_req output pcs_coreX_sleep_ok output mX_smp_en;