## Slide 1: Vicuna AE350 SMU Design Specification
Driving Innovations™
Ellis Chen
2019-03-11

## Slide 2: Outline
Feature of ae350_smu_pd
ae350_rstgen
  Add path for reset core 0
ae350_smu
  Old/New hierarchy block diagram
ae350_smu_apbif
  New register for power control
ae350_smu_mpd (Main power domain)
  Remove core clock/power related logic
ae350_smu_pd (Core/L2 power domain)
  Interface
  FSM for DVFS/power control

## Slide 3: Feature of ae350_smu_pd
Two kinds of control mode configuration
  DVFS
  Power
Support for a power/clock domain control
  Power source
  Clock source
  Isolation cell
  Retention cell
Support for wakeup event mask
Support for light sleep/deep sleep modes
Support for dynamic voltage frequency scaling (DVFS)

## Slide 4: Assumption for simplification
Only one clock source and voltage source
  Simplify multi-core DVFS flow
Clock/Power scaling and on/off are control by different channel
  1 channel for DVFS
  4 channel for light sleep (clock-gated) and deep sleep (power off)

## Slide 5: ae350_rstgen
In ae350_rstgen, core0_resetn is controlled by aresetn_src.
core[1~3]_resetn is controlled by SMU.
Add a path for reset core 0

## Slide 6: Old hierarchy block diagram in AE350
ae350_smu_apbif
ae350_smu_mpd
ae350_smu_aopd_top
ae350_smu_aopd_core
ae350_aopd_pin
ae350_aopd_clkgen
ae350_aopd_rstgen
ae350_aopd_testgen
ae350_smu
Registers
FSM for power mode
Test signal connection
Clock signal with test_mode mux
Reset signal with test_mode mux
IO Pad for aopd_porb/om/jtag_tck/wakeup/rtc_wakeup/mpd_pwr_pff
Synchronizer for RTC signal

## Slide 7: New block diagram for power control
ae350_smu(Always-on region)
ae350_smu_pd(Power)
Core 0 and L2/Core 1~3
FSM for power mode
ae350_smu_pd(DVFS)
FSM for DVFS mode
pd_vol_scale_req
pd_vol_stable
pd_vol_scale
pd_vol_scale_ack
pd_frq_scale_req
pd_frq_scale
pd_frq_scale_ack
pd_clk_stable
pd_clk_off0~3
pd_standby0~3
pd_ret_en0~3
pd_iso_en0~3
pd_pwr_off0~3
ae350_smu_apbif
pd_clk_off_all
APB
pd_all_standby
smu_interrupt_pd0~3
smu_interupt_dvfs
Notes: SMU 5 channel : 1 DVFS , 4 Power Switch Clock Switch

## Slide 8: Macro and parameter for ae350_smu
Name | Description | Value
PD_NUM | Number of power domain | 1~4
CYCLE_WIDTH | Bit width for ret_cyc and iso_cyc | 4
DISALBE_INIT_WIDTH | Bit width for disable_init | Single core: 2 Multi-core: 2*N+1
FIX_VOLTAGE | Hardwired voltage related control to 0 in FPGA flow | none
Parameter
Marco
Name | Description | Value
NDS_IO_PD1 NDS_IO_PD2 NDS_IO_PD3 | I/O port for multi-cores | none

## Slide 9: Macro and parameter for ae350_smu_pd
Name | Description | Value
DVFS | Indicate this channel is for DVFS | yes: DVFS channel no: Power channel
WAKEUP_WIDTH | Bit width for wakeup_event | 7
Parameter

## Slide 10: New CSR for ae350_smu
Power Mode Cycle Register (PMCR) (0x100)
Name | Bit | Type | Description | Reset
ret_cyc | CYCLE_WIDTH-1:0 | RW | Cycles for retention state waiting | 0x0
iso_cyc | CYCLE_WIDTH+15:16 | RW | Cycles for isolation state waiting | 0x0
Power Mode Disable Initialization Register (PMDIR) (0x104)
Name | Bit | Type | Description | Reset
disable_init | DISALBE_INIT_WIDTH-1:0 | RW | Control disable init for memories | 0x0
*Cycle time is SMU clock

## Slide 11: New CSR for ae350_smu
Power Status Register (PSR) (0x204)
Name | Bit | Type | Description | Reset
pd_status | 3:0 | RO | Power status for each power domain 0x0:ACTIVE 0x1:DVFS 0x2:ISOLATION 0x3:RETENTION 0x4:LIGHTSLEEP 0x5:DEEPSLEEP | 0x0
Power Wakeup Record Register (PWRR) (0x208)
Name | Bit | Type | Description | Reset
pd_wakeup_record | WAKEUP_WIDTH-1:0 | RW | Record pd_wakeup_event with wakeup_en mask when power command is finished | 0x0
Power Domain Select Register (PDSR) (0x200)
Name | Bit | Type | Description | Reset
pd_select | 3:0 | RW | Select power domain for power command | 0x0
*Software lock is required while accessing SMU in multi-core system.
Notes: SMU address mapping=0xF0100000~0xF01FFFFF
Only one core

## Slide 12: New CSR for ae350_smu_pd
Power Control Register (PCR) (0x210)
Name | Bit | Type | Description | Reset
pd_ctrl_cmd | 3:0 | RW | Power control command 0: No action 1: DVFS 2: Light Sleep 3: Deep Sleep | 0x0
pd_ctrl_frq | 7:4 | RW | Frequency vector for DVFS | 0x0
pd_ctrl_vol | 11:8 | RO | Reserved for voltage vector for DVFS | 0x0
Wakeup Enable Register (WER) (0x20C)
Name | Bit | Type | Description | Reset
pd_wakeup_en | WAKEUP_WIDTH-1:0 | RW | Wakeup event enable 0:Disable wakeup event 1:Enable wakeup event | 0xffffffff

## Slide 13: New CSR for ae350_smu
Power Interrupt Register (PIR) (0x214)
Name | Bit | Type | Description | Reset
pd_ctrl_int_en | 0 | RW | Assert SMU interrupt for this power domain after power command is done. This bit is automatically asserted when pd_ctrl_cmd is DVFS. | 0x0
pd_ctrl_int_pending | 1 | RW | SMU interrupt pending bit Write 0 to clear interrupt | 0x0

## Slide 14: Power mode definition
DVFS
  Purpose: Dynamic change power for workload requirement
  Function: Change voltage and frequency
  Latency: For voltage/clock source, it might takes ms scale for scaling and stable.
Light Sleep
  Purpose: Fast response for interrupt and save power
  Function: Core and RAM are clock-gated.
  Latency: fast for enabling clock switch
Deep Sleep
  Purpose: Stop core and save most power
  Function: Core and RAM are powered off.
  Latency: For voltage/clock source, it might takes ms scale for turn-on and stable.

## Slide 15: ae350_smu_mpd
Remove core clock/power related logic
  standby state machine
  smu2core_standby_req
  smu2core_wakeup_ok
  core2smu_wfi_mode

## Slide 16: ae350_smu Interface
Global signal for all power domain
  smu_disable_init[31:0](input): Indicate signal which is asserted by PMDIR
    For icache_disable_init/dcache_disable_init/l2_disable_init
  debug_wakeup(input): When debug_wakeup is asserted, the bus power and clock will be on for debug module access.

## Slide 17: ae350_smu_pd Interface
Control signal from power domain (with synchronizer)
  pd_standby(input): Indicate this power domain is ready for power change
    Connect to core_wfi_mode that core ready for power change
  pd_all_standby(input): Indicate all power domains are standby
  pd_wakeup_event[WAKEUP_WIDTH-1:0](input): Indicate this power domain should be wakeup
    Connect to msip/meip/mtip/rtc_alarm/wi/smu for cores wakeup event

## Slide 18: ae350_smu_pd Interface
Control signal with ae350_smu_apbif
  smu_ret_cyc_we(input): Indicate smu_ret_cyc is updated
  smu_ret_cyc[CYCLE_WIDTH-1:0](input): Indicate retention cycle
  smu_iso_cyc_we(input): Indicate smu_iso_cyc is updated
  smu_iso_cyc[CYCLE_WIDTH-1:0](input): Indicate isolation cycle
  smu_wakeup_enable_we(input): Indicate smu_wakeup_enable is updated
  smu_wakeup_enable[WAKEUP_WIDTH:0](input): Indicate pd_wakeup_event is valid for wakeup
  smu_pwr_ctrl_cmd_we(input): Indicate smu_pwr_ctrl_* is updated
  smu_pwr_ctrl_cmd[3:0] (input): Indicate power command
  smu_pwr_ctrl_frq[3:0] (input): Indicate frequency vector
  smu_pwr_ctrl_vol[3:0] (input): Indicate voltage vector
  smu_pwr_ctrl_cmd_pending[3:0] (output): Indicate power command pending in ae350_smu_pd
  smu_pwr_status[3:0] (output): Indicate power status

## Slide 19: ae350_smu_pd Interface
Power control signal with voltage/clock source
  pd_vol_stable(input): Voltage is stable for the power domain from voltage regulator
  pd_vol_scale_req(output): Voltage scaling vector require to voltage regulator
  pd_vol_scale(output): Voltage scaling vector to voltage regulator
  pd_vol_scale_ack(input): Voltage scaling vector ack from voltage regulator
  pd_frq_stable(input): Frequency is stable for the power domain from clock generator
  pd_frq_scale_req(output): Frequency scaling vector require to clock generator
  pd_frq_scale(output): Frequency scaling vector to clock generator
  pd_frq_scale_ack(input): Frequency scaling vector ack from clock generator
Power control signal for power domain
  pd_iso_en(output): Isolation indicator
  pd_ret_en(output): Retention indicator
  pd_clk_off(output): Clock shut-off indicator
  pd_pwr_off(output): Power region shut-off indicator
  pd_rstn(output): Power region reset indicator

## Slide 20: List of wakeup event
RISC-V
  Software PLIC: msip
  PLIC: meip
  PLMT: mtip
  Debug mode: debugint (Not maskable)
Platform
  RTC: rtc_alarm
  SMU: smu
  External event
Notes: PLIC:
11268:assign int_src[1] = rtc_int_period;
11269:assign int_src[2] = rtc_int_alarm;
11270:assign int_src[3] = pit_intr;
11271:assign int_src[4] = spi1_int;
11272:assign int_src[5] = spi2_int;
11273:assign int_src[6] = i2c_int;
11274:assign int_src[7] = gpio_intr;
11275:assign int_src[8] = uart1_int;
11276:assign int_src[9] = uart2_int;
11277:assign int_src[10] = dma_int;
11278:assign int_src[11] = 1'b0;
11279:assign int_src[12] = 1'b0;
11280:assign int_src[13] = 1'b0;
11281:assign int_src[14] = 1'b0;
11282:assign int_src[15] = 1'b0;
11283:assign int_src[16] = 1'b0;
11284:assign int_src[17] = ssp_intr;
11285:assign int_src[18] = sdc_int;
11286:assign int_src[19] = mac_int;
11287:assign int_src[20] = lcd_intr;
11288:assign int_src[21] = 1'b0;
11289:assign int_src[22] = 1'b0;
11290:assign int_src[23] = 1'b0;
11291:assign int_src[24] = 1'b0;
11292:assign int_src[25] = 1'b0;
11293:assign int_src[26] = smu2core_standby_req;
11294:assign int_src[27] = smu2core_wakeup_ok;
11295:assign int_src[28] = 1'b0;
11296:assign int_src[29] = 1'b0;
11297:assign int_src[30] = 1'b0;
11298:assign int_src[31] = 1'b0;

## Slide 21: Sample block diagram for single core power domain
Clock Generator
VRM
Power domain
Isolation cell
Retention cell
pd_standby
pd_pwr_off
pd_ret_en
pd_iso_en
pd_vol_scale_req
pd_vol_stable
pd_vol_scale
pd_vol_scale_ack
pd_frq_scale_req
pd_frq_scale
pd_frq_scale_ack
core_clk
vout
SRAM
SMU
PLIC
PLMT
Debug System
Always-on domain
Customer provided
Core domain (cpu_core_top)
Software PLIC
RTC
Platform domain
AXI
pd_clk_stable
pd_clk_en

## Slide 22: Sample block diagram for multi-core power domain
Clock Generator
VRM
pd_vol_scale_req
pd_vol_stable
pd_vol_scale
pd_vol_scale_ack
pd_frq_scale_req
pd_frq_scale
pd_frq_scale_ack
vout0~3
SMU
PLIC
PLMT
Debug System
Always-on domain
Customer provided
Core domain (cpu_core_top)
Software PLIC
RTC
Platform domain
AXI
pd_clk_stable
pd_clk_off0~3
Power domain
Isolation cell
Retention cell
SRAM
core_clk0~3
pd_standby0~3
pd_ret_en0~3
pd_iso_en0~3
pd_pwr_off0~3
Notes: Power switch may be in power domain.

## Slide 23: Sample block diagram for power domain
Always-on domain
Customer provided
Core domain
Platform domain

## Slide 24: FSM for power mode
ST_ACTIVE
ST_ISOLATION
ST_RETENTION
ST_LIGHTSLEEP
ST_DEEPSLEEP
pd_standby==1&&
cmd==DEEPSLEEP
pd_standby==1&&
cmd==LIGHTSLEEP
counter>=ret_cyc
counter>=iso_cyc
counter>=iso_cyc
counter>=ret_cyc
pd_wakeup_event&&
pd_clk_stable
pd_wakeup_event&&
pd_pwr_stable
ST_RESET
counter>=2

## Slide 25: FSM for DVFS mode
ST_ACTIVE
ST_DVFS
pd_all_standby==1&&
cmd==DVFS
pd_frq_scale_ack if (new_frq_scale!=old_frq_scale)
pd_vol_scale_ack if (new_vol_scale!=old_vol_scale)

## Slide 26: Single core DVFS flow
Core wants to do DVFS by itself
  Core send power command to SMU
  Core setup SMU interrupt enable
  Core executes WFI
  SMU handles power command
  SMU asserts in interrupt to Core
  Core exits WFI mode

## Slide 27: Core to Core wakeup flow
Core 0 asks Core 1 to deep sleep mode
  Core 0 send power command to SMU for Core 1
  Core 0 inform other Core 1 to enter WFI mode
  SMU handles power command
  Core 1 enters deep sleep mode
  Core 1 wakeup by Core 0 by Software PLIC

## Slide 28: Multi-Core DVFS flow
Cluster executes frequency change
  Core 0 lock SMU access
  Core 0 setup DVFS command to SMU
  Core 0 inform other cores to execute WFI
  Core 0 executes WFI
  SMU wait all power domains are in standby mode
  SMU handles DVFS command to all cores
  PD0(Core 0) is wakeup by SMU interrupt
    SMU interrupt is automatically asserted by DVFS command.
  Core 0 send IPI to wakeup other cores
  Core 0 unlock SMU access
Notes: Assert SMU interrupt without command for DVFS only
DVFS channel has high clock priority to other channels
*Osban review L2C email
*SMU interrupt is claimed by only one core in PLIC.

## Slide 29: Issue: Interrupt occur during DVFS flow
Method 1
  Disable all interrupt source
  Cons: Long latency for interrupt response
Method 2
  Abort DVFS command

## Slide 30: Debug module and SMU interactive
Debug module supported bus access
  Wakeup bus when debug_wakeup is asserted by debug module
    In AE350 SMU design, enable main bus clock.
  Debug module wakeup a core by SMU interrupt
Debug module is not supported bus access
  Wakeup core 0 for debug
    An additional wakeup source debugint is required.

## Slide 31: Timing diagram for deep sleep mode
Power off
pd_standby
pd_iso_en
pd_ret_en
pd_pwr_off
pd_clk_off
ST_ACTIVE
ST_ISOLATION
ST_RETENTION
ST_DEEPSLEEP
ST_RETENTION
ST_ISOLATION
ST_ACTIVE
pd_rstn
core_resetn

## Slide 32: Power control signal by FSM
 | pd_iso_en | pd_ret_en | pd_clk_off | pd_pwr_off
ST_ACTIVE | 0 | 0 | 0 | 0
ST_DVFS | 0 | 0 | 1 | 0
ST_ISOLATION | 1 | 0 | 0 | 0
ST_RETENTION | 1 | 1 | 0 | 0
ST_LIGHTSLEEP | 1 | 1 | 1 | 0
ST_DEEPSLEEP | 1 | 1 | 1 | 1

## Slide 33: L2C design request for power mode
For light sleep(clock-gated) mode and DVFS
  L2C should stop snooping when cores are executing WFI separated
  L2C should enter standby mode automatically after all cluster are in WFI mode
    Queue in L2C should be empty
  Coherence slave port should be disable while DVFS is doing or L2C is in light sleep mode
    Master should know that coherence slave port is temporarily unavailable.
In L2C standby mode
  A output indicate that L2C is busy
    SMU handles power change when L2C is not busy.

## Slide 34: Jimmy’s reply
L2C should stop snooping when cores are executing WFI separated
  L2 will stop snooping to the core when the its’ output port “ready_for_snoop” is de-asserted.
L2C should enter standby mode automatically after all cluster are in WFI mode.
  L2 will add one output port “l2_idle” and it should be asserted when all transactions in L2 have been done.
Coherence slave port
  In this situation, there is no clock in L2 and perhaps we should handle this in system level by adding a wrapper.

## Slide 35: Issue: debug when core power off before
Scenario
  Core 0 setup trigger module
  Core enter deep sleep mode
  Core 0 wakeup by interrupt
  In this case, Core 0 lose all setting in trigger module and OpenOCD and debug module can’t detect this situation.
  Solution
    Use retention cells or always-on region for debug CSRs (HW solution)
    Backup by other bus master
    Do not backup debug CSRs and OpenOCD handles this issue

## Slide 36: Future work
Core 0 and L2 are de-coupled in power domain.
Power domain inside SMU for ultra-low power
Different frequency between cores and L2