## Slide 1: MP Low Power Flow

## Slide 2: MP System
ACU & L2
Core 0
Dtag 0
Core 1
Dtag 1
SMU
Sleep Handshake
clock
Power Control Register R/W
Bus Decode
Clock gen
Xtal
PLL
Clock enable

## Slide 3: Low Power Signals
PCS Interface
rdy_for_snoop[3:0]
sleep_req[3:0]
sleep_ok[3:0]
core_wfi_mode | core is in wait for interrupt mode
rdy_for_snoop | D$ & Dtag initial done and can accept snoop request
sleep_req | Request core 0 to quit SMP and enter sleep mode
sleep_ok | Core 0 is ready to enter sleep mode
Mpcore
Core
Core
Core
core_wfi_mode[3:0]
SMU
L2_IDLE
L2C
srrep_done[3:0]

## Slide 4: Core Low Power Mode

## Slide 5: Power Mode
Power Mode | Normal | Standby | LightSleep | DeepSleep
Core | active | clock gated | clock off | power off
D$ & Dtag | active | active |  | 

## Slide 6: Standby Mode
Standby: core executes WFI instruction and state of SMU is active, D$ & Dtag are still active
Pcs_sleep_req | 0
Pcs_sleep_ok | 0
Core_wfi_mode | 1
Pcs Status | Active
Pcs sleep mode | x

## Slide 7: Light Sleep Mode
LightSleep: core execute WFI instruction and state of SMU is sleep, all circuit of core is not active
Pcs_sleep_req | 1
Pcs_sleep_ok | 1
Core_wfi_mode | 1
Pcs Status | Sleep
Pcs sleep mode | LightSleep

## Slide 8: Light Sleep Mode
Get IPI
disable local interrupt to prevent from exiting wfi mode (or prevent from the interrupt)
  set xtie/xeie as 0 and set xsie as 1
  set meie/mtie as 0 and set msie as 1, if wfi executes in S mode
to prevent from dirty dcache
  xstatus.xie=0
set SMU wakeup enable & MISC control
set SMU light sleep command  sleep_req asserted
to let DMA/MAC access memory correctly for snoop
  flush dcache (CCTL)
  dcache off
wfi  l2 stop send snoop request to core & wait all snoop response returned, than sleep_ok asserted.

## Slide 9: Light Sleep Mode
1
Step | Signal | Condition
0 | rdy_for_snoop assert | D$ & Dtag initail done
1 | Smpen asserrt | (rdy_snoop =1) & ~(sleep_req & wfi)
2 | Sleep_req assert | Set SMU light sleep command
3 | core_wfi_mode | Core executes WFI instruction & all bus request is done
4 | Smpen deasserrt | sleep_req & wfi
5 | Sleep_ok assert | Core_wfi_mode =1 & sleep_req=1 & all srresp has been returned
6 | Ipi assert | Inter process interrupt to wakeup core
7 | Sleep_ok deassert | Sleep_req is deassert
3
2
4
5
6
7

## Slide 10: Deep Sleep Mode
DeepSleep: core execute WFI instruction and state of SMU is sleep, all circuit of core is power off
Pcs_sleep_req | 1
Pcs_sleep_ok | 1
Core_wfi_mode | 1
Pcs Status | Sleep
Pcs sleep mode | DeepSleep