## Slide 1: TLC2AXI500
Bill 2020/10/21

## Slide 2: Features
Compliant with AXI4 protocols
  Supports AXI exclusive access
  Supports AxCACHE information
  Supports AxPROT information
Compliant with TileLink Cached (TL-C)
  Supports beat interleaving in TileLink channel D
Configurable clock synchronization
  asynchronous
  synchronous N:1 (TileLink clock frequency : AXI clock frequency)
Configurable 32–64 bits address width
Configurable 32/64/128/256 bits data width
Configurable 4–8 ID width
Supports up to 128 bytes burst size
Configurable sink id width
Support user sidebands

## Slide 3: Latency
A/C Channel Latency
  a_valid/c_valid to arvalid/awvalid/wvalid
  1 cycle (min)
D Channel Latency
  rvalid/bvalid to d_valid
  1 cycle
E channel latency
  0 cycle
B channel
  Hardwired to 0

## Slide 4: Parameters
ACLK_SYNC: sync, async
ADDR_WIDTH: 32-64
DATA_WIDTH: 32/64/128/256
ID_WIDTH: 4-8
AXI_USER_WIDTH
TL_SINK_WIDTH
ASYNC_DEPTH

## Slide 5: Block Diagram

## Slide 6: Elastic Buffer
Microarchitecture of Network-on-Chip Routers

## Slide 7: User
The width is defined by AXI_USER_WIDTH
TileLink A, C channels to AXI AW, W, R channels
AXI R, B channels to TileLink D channels
TileLink A, C channels to TileLink D channels

## Slide 8: New BIU