## Slide 1: D23 LBIU

## Slide 2: Discussion (3/29)
PLIC (CLIC) / PLMT (embedded) / PLDM (embedded)
  optional / internal / peripheral
  ae350_cpu_subsystem
  core_top/core/ucore
  Plans for internal IPs

## Slide 3: Discussion (3/29)
N22 internal IP gate_count
uTLB+PMP
CLIC

## Slide 4: Requirement
CPU_SUBSYSTEM
  3 Bus interface:
    Master (output): CPU to System Bus
    Master (output): Debug to System Bus
    Slave (input) : Slave Port (System Bus to LM)
  The BMC in CPU_SUBSYSTEM supports data_width 32 / 64
    Use Size-Down if data_width > 64
PLMT / Internal Timer
  Supports free clock ratio between core_clk and mtime_clk

## Slide 5: Requirement
PLIC / CLIC
PLDM
  Internal DM supports System bus Access(?
  Supports debug spec v0.14
  JDTM port (cpu_subsystem interface)
    DMI_AHB or JTAG?
** PPA for internal IP
Ref to N8 EDM (SIZE CPU:EDM)

## Slide 6: Reference: AE350_CPU_SUBSYSTEM in 25/27
BMC300(AXI) / BMC200(AHB)
AE350_CPU_SUBSYSTEM
BUSDEC300(AXI) / BUSDEC200 (AHB)
PLMT
PLIC
PLIC_SW
DEBUG
slv0
slv1
slv2
slv3
CORE_TOP
BUSDEC200 (AHB)
SYSTEM BUS
i_AXX
d_AXX
AXX
slv1
slv8
slv9
slv10
cpuslv_AXX
AXI2AHB
SIZEDN
*BIU_DATA_WIDTH
*AE350_DATA_WIDTH
*PIP MAX DATA_WIDTH = 64
*BMC MAX DATA_WIDTH = 256

## Slide 7: Reference: ucore/core/core_top in N22
If the internal PL-IPs are selected, the Timer/CLIC/DM will be Instantiated in core level
N22 has ucore level
  In 25/27 ucore and LM_ctrls are packed as vc_core level
Core level includes LM control
Core-Top level includes core and RAMs
N22 has JTAG interface on core_top

## Slide 8: Reference: N22 BIU and LBIU
In N22, the address decode is done in LSU and issues the request to BIU or LBIU.
To BIU part: Private DM / System Bus To LBIU part: FIO/PPI/ CLIC/Private Timer
N22 has hardwire priority: CLIC > timer > FIO > PPI > System Bus
read timer behavior
N22 gate-count for private IP

## Slide 9: CPU_SUBSYSTEM with internal IPs
If any peripheral IP exist, the CPU subsystem looks like original version.
Pack BMC and peripheral IPs to simplified the cpu_subsystem code structure.
cpu_subsystem coding issue:
  MP?
  CORE_BIU AXI or AHB
  internal IPs
  peripheral IP interface AHB/AXI
  LM + AHB-Lite
  *** AHB only

## Slide 10: CPU_SUBSYSTEM with internal IPs
If all peripheral IPs are selected as internal version, the BMC will not be instantiated
The cpu_subsystem hierarchy will be simplified to:
  core_top
  busdec200 (for Slave Port)

## Slide 11: Simplified CPU_SUBSYSTEM (1)
Default has specific ports for PLIC/PLDM/PLMT
Reduce BMC/BUSDEC
Don’t need AXI/AHB for the interface between BIU and PIP (?)
BIU gate-count (X)

## Slide 12: Simplified CPU_SUBSYSTEM (2)
If one of PLMT/PLDM/PLIC is not internal version.
Turns on a specific port to access peripheral IPs
Reduce BMC
The BUSDEC can be implemented by address only (don’t need BUSDEC100/BUSDEC300 here)
BIU gate-count (X)

## Slide 13: CPU_SUBSYSTEM coding(?
core_top (
`ifdef AXI
AXIIF
`endif
`ifdef AHB
AHBIF
`endif
`ifdef INTERNAL_DEBUG_AXI
DEBUG_IF_AXI
`endif
`ifdef INTERNAL_DEBUG_AHB
DEBUG_IF_AHB
`endif
)
pack (
`ifdef AXI
CORE_AXIIF
SYS_BUS_AXIIF
`endif
`ifdef AHB
CORE_AHBIF
SYS_BUS_AHBIF
`endif
`ifdef INTERNAL_DEBUG_AXI
DEBUG_IF_AXI_in
DEBUG_IF_AXI_out
`endif
`ifdef INTERNAL_DEBUG_AHB
DEBUG_IF_AHB_in
DEBUG_IF_AHB_out
`endif
)
Core_top
AHBIF
AHB BMC
AXIIF
AXI BMC
ifdef AHB
ifdef AXI

## Slide 14: Reference: N22 Private Timer
The private timer for N22 which is driven by core_clk is in core level
  It means the core_clk can’t be stopped
In core_top level, there is a toggle pulse generator. This pulse will toggle when every mtime_clk pose-edge
The private timer sync and count the toggle-pulse for mtime_clk counting, it means:
  The core_clk must faster than mtime_clk
  The core_clk : mtime_clk is better limited at 2:1 (Freq)

## Slide 15: Plan: Internal Timer for D23
To allow core_clk be stopped, separate core_clk:
  Always on core_clk  for internal timer / debug(DMI) / CLIC(?)
  Gated core_clk  for ucore
  The gating module will be added in core_top level
The NCEPLMT100 supports the free clock ratio between mtime_clk and core_clk
  Instantiate the NCEPLMT100 in core level directly
  Add mtime_clk at core_top interface and connect to NCEPLMT100
Gate Count may be a problem:
  NCEPLMT100  4.1K (AHB)
    busif  3.4K
    mtime  0.7K
  Maybe use self-define interface can reduce gate-count in busif
input clk: core_clk, aopd_timer_clk, aopd_debug_clk, aopd_clic_clk
(mtime_clk)

## Slide 16: Reference: N22 Private DM
N22 reduce the PLDM’s code
  Halt resume is not supported
DM.SYS_BUS_ACC is not supported
JTAG module is instantiated in core level (has JTAG signal on core interface)
N22 integrate PLDM + debug CSR + TRIGER(TDATA) as debug subsystem.

## Slide 17: Plan: Internal Debug for D23
Internal DM will not support SYS_BUS
Keep all functions in debug spec v0.14
Use PLDM directory
move JDTM to ae350
  The JDTM is in AE350_AOPD now (always on)
  The Core_top interface for debug will be DMI_AHB

## Slide 18: Reference: N22 CLIC

## Slide 19: Plan: CLIC for D23

## Slide 20: CLIC – Register for each Int control

## Slide 21: CLIC – CLICINTIP

## Slide 22: CLIC – setup priority
Use cliccfg.NLBITS to setup the priority bits:
  ex. 8bits => max priority 255
set clicintctl.PRIORITY for priority setting

## Slide 23: Gate Count
 | Internal | On Bus
Timer | 1.58K | 4.1K
 |  | BusIF 0.7K
debug | 8K (*include jtag 1.3K) | PLDM
 | DM 5.88K | 7K
 | JTAG 1.3K | 
CLIC / PLIC | 1.47K | 6.3K / 4.7K (HW/SW)
 | 0.7K (sync) (0.1K*7) | 

## Slide 24: Gate Count - Timer
Timer | Internal Timer (in N22) | NCEPLMT100 | Diff
Total Gate Count | 1.58K | 3.99K | -2.41K
BusIF | - | 3.19K | -
Mtime | 1.55K | 0.7K | -
Synchronizer | 0.03K | 0.06K | -
Interface | Self-Define (valid/ready) | AHB | -
Data Width | 32 | 32 | -

## Slide 25: Gate Count - Debug
Debug | Internal Debug(in N22) | NCEPLDM200 | Diff
Total Gate Count | 8K | 7K | -
DM | 5.88K | 7K | -1.12K
JTAG | 1.3K | - | -
Interface | AHB | AHB | -
SYS_BUS_ACCESS | no | no (SYS_BUS AHB: 0.7K) | -
Data Width | 32 | 32 | -

## Slide 26: Gate Count – CLIC/PLIC
Debug | CLIC | PLIC (HW) | PLIC (SW)
Total Gate Count | 8K | 5.16K | 
DM | 5.88K | 7K | 
JTAG | 1.3K | - | 
Interface | AHB | AHB (Don’t support DW) | 
SYS_BUS_ACCESS | no | no | 
Data Width | 32 | 32 | 

## Slide 27: Limitation - Timer
 | Integrated PIP | NCEPLMT100
Clock Ratio (Freq) (Core : Mtime) | > 2:1 | Any Ratio
Bus interface | Self-Define (32) | AHB/AXI (32/64)
Response Latency | About 4 mtime cycle (?) | illegal inst + mtime handler
core_clk status | core_clk always alive | core_clk can be stopped
target number | 1 | 1~1024
mtime clk sync/async |  | 
Remove shadow in integrated timer
mtime clk use async handling but connect with sync bus_clk
self-define uses req/ack
Add always-on core_clk from clkgen

## Slide 28: Limitation - Debug
 | Integrated PIP | NCEPLDM200
Program Buffer Size | 1 / 2 / 8 | 1 / 2 / 8
Bus Interface | self-define (32) | AHB / AXI (32/64)
DMI Interface | AHB (32) | AHB (32)
Halt Group | Not Supported | Supported
Group Resume | Not Supported | Supported
Cross Trigger | Not Supported | Supported
System Bus Access | Not Supported | Supported
Debug Wait State | Not Supported | Supported
Program buffer Size use 1 / 2 / 8 in design.
New AE350 for D23, include JDTM in AE350_AOPD + AE350_CPU_SUBSYSTEM
How to support debug wait state  TBD
In first CHH stage: PLDM has two implement stage:
For first version: use PLDM and add a new port in BIU
2nd: Reduce integrated Debug Gate Count (Interface Enhance)

## Slide 29: Limitation - CLIC
 | CLIC | PLIC
Interrupt number | 1~1024 | 1~1024
Bus Interface | self-define (32) | AHB / AXI (32/64)
DMI Interface | AHB (32) | AHB (32)
Target Number | 1 | 1~16
Max Priority | 3/7/15/31/63/127/255 | 3/7/15/31/63/127/255
Async Int | Supported | Supported
Edge Trigger | Supported | Supported

## Slide 30: Ref: N22 CLIC Interface
Signal | Source | Destination | Description
msip | core IF | CLIC | 
mtip | core IF / Timer | CLIC | 
meip | core IF | CLIC | 
mip_imecci | ucore | CLIC | 
mip_bwei | ucore | CLIC | 
mip_pmovi | ucore | CLIC | 
clic_irq[CLIC_IRQ_NUM-20:0] | core IF | CLIC | 

## Slide 31: Ref: N22 CLIC Interface
Signal | Source | Destination | Description
icb_cmd_valid | BIU | CLIC | Self-Define interface (BIU  CLIC) The CLIC.CSR in N22 is accessed by BIU Same Cycle response
icb_cmd_ready | BIU | CLIC | 
icb_cmd_addr | BIU | CLIC | 
icb_cmd_wmask | BIU | CLIC | 
icb_cmd_read | BIU | CLIC | 
icb_cmd_wdata | BIU | CLIC | 
icb_rsp_valid | CLIC | BIU | 
icb_rsp_ready | CLIC | BIU | 
icb_rsp_rdata | CLIC | BIU | 
icb_rsp_err | CLIC | BIU | 

## Slide 32: Ref: N22 CLIC Interface
Signal | Source | Destination | Description
clic_irq_taken | ucore (n22_ucore) | CLIC | 
core_in_int | ucore (n22_ucore) | CLIC | 
clic_int_mode | ucore (n22_ucore) | CLIC | 
mnxti_valid_taken | ucore (n22_ucore) | CLIC | 

## Slide 33: Ref: N22 CLIC Interface
Signal | Source | Destination | Description
clic_active | CLIC | CLK_CTRL | 
clic_irq_o | CLIC | ucore (n22_exu) | 
clic_irq_id | CLIC | ucore (n22_exu) | 
clic_irq_shv | CLIC | ucore (n22_exu) | vector CLIC is selected 0: Jump to mtvec 1: Jump to mtvt
mintstatus_mil_r | ucore (n22_exu) | CLIC | 
clic_irq_lvl | CLIC | ucore (n22_exu) | 
clic_prio_gt_thod | CLIC | ucore (n22_exu) | 

## Slide 34: Integrated PIPs Clock Gating
Requirement:
  Gate the CLIC, Timer, and Debug Module when they are IDLE
  Debug Module IDLE:
    Core free run + JTAG state machine in IDLE
    In halt mode: debug wait state
  Timer IDLE:
    Gate Timer_clk: No timer setting
    Gate mtime_clk: Stoptime
  CLIC IDLE:
    No interrupt
    No CLIC setting request

## Slide 35: chh_core and clkgen
As figure

## Slide 36: Clocks in chh_core Level
 | Source | Clock (default) | Clock Enable Source
Core Clock |  | on | WFI
LM Clock | Core Clock | on | 
Timer Clock | Core Clock | off | BIU (biu_path)
Mtime Clock | PCLK (AE350) | on | Core (stoptime)
DM Clock | Core Clock | off | JTAG FSM + CORE (csr_halt_mode + dbg_wait_state)
CLIC Clock | Core Clock | off | BIU (biu_path)
AON core clk |  | on | 

## Slide 37: Clock Gating – Timer (1)
Timer Programming Sequence
  Write mtime
  Write mtimecmp
  ---- wait for mtip ----
  Write mtimecmp to clear mtip
stoptime
  from core to timer
  stoptime only issues in debug mode

## Slide 38: Clock Gating – Timer (1)
Turns on timer_clk
  BIU receives the mtime/mtimecmp requests
Turns off timer_clk
  mtime/mtimecmp request done
Turns off mtime_clk
  Stoptime asserted
Turns on mtime_clk
  Stoptime de-asserted

## Slide 39: Clock Gating – Debug Module
Backup S0, S1
Read RV_COMMAND
Restore S0, S1
Do abstract command
ebreak
Has new abs_cmd
Do
Resume
Restore S0, S1
+ dret
Y
Y
N
N
Wait State
Restore S0, S1
+ ebreak
debugint taken
PLDM Issues debugint when:
haltreq
resumereq
ABS command
jump to wait state
by ebreak in debug mode
Gate dm_clk here

## Slide 40: Clock Gating – Debug Module
Both DMI and Core interface use dm_clk
Turns on dm_clk
  JTAG FSM active (JTAG leaves IDLE state)
Turns off dm_clk
  Core stays in free run (~halt_mode)
  Core stays in debug wait state (halt_mode & dbg_wait state)
  No JTAG active (JTAG stays in IDLE State)

## Slide 41: Clock Gating – CLIC
In N22, the clic_clk only drives the clic registers
The interrupt handling uses always-on core_clk

## Slide 42: Interface – Bus IF to Internal IF
Signal | Source | Destination | Note
Read Channel |  |  | 
read_req_valid | Bus IF | PIP Core | For Bus IF == AHB, read_req_valid indicates the A-Phase
read_addr | Bus IF | PIP Core | araddr(AXI) / haddr(AHB)
read_data | PIP Core | Bus IF | Flop out
Write Channel |  |  | 
write_req_valid | Bus IF | PIP Core | For Bus IF == AHB, write_req_valid indicates the D-Phase
write_addr | Bus IF | PIP Core | awaddr(AXI) / haddr(AHB)
write_data | Bus IF | PIP Core | wdata(AXI) / hwdata(AHB)
The request from Bus IF to Internal IF is assumed as no wait cycle.
Separate R/W channel may be easier for AXI IF implement. (?)

## Slide 43: Interface – integrated PIP IF
Signal | Source | Destination | Note
biu_pip_req | BIU | PIP | For Bus IF == AHB, read_req_valid indicates the A-Phase
pip_biu_ack | PIP | BIU | bus transfer done
biu_pip_addr | BIU | PIP | axaddr(AXI) / haddr(AHB)
biu_pip_write | BIU | PIP | Indicates a write transfer
biu_pip_wdata | BIU | PIP | wdata(AXI) / hwdata(AHB)
biu_pip_byte_en | BIU | PIP | byte write enable
pip_biu_rdata | PIP | BIU | can’t be flopped out if ACK is same cycle response
pip_biu_resp | PIP | BIU | 0: OK 1: Error  handle as bus error
All R/W request in PIP don’t have wait cycle.
  The bus_ack usually be same cycle response for bus_req
  After the shadow register is removed in TIMER, the wait cycle handling is needed