## Slide 1: Vicuna AE350 SMU Design Specification
Driving Innovations™
Ellis Chen
2019-03-05

## Slide 2: Outline
Feature of ae350_smu_pd
ae350_rstgen
  Add path for reset core 0
ae350_smu
  Old/New hierarchy block diagram
ae350_smu_apbif
  New register for power control
ae350_smu_mpd (Main power domain)
  Remove core clock/power related logic
ae350_smu_pd (Core/L2 power domain)
  Interface
  FSM for power control

## Slide 3: Feature of ae350_smu_pd
Support for a power/clock domain control
  Power source
  Clock source
  Isolation cell
  Retention cell
Support for wakeup event mask
Support for light sleep/deep sleep modes
Support for dynamic voltage frequency scaling (DVFS)

## Slide 4: ae350_rstgen
In ae350_rstgen, core0_resetn is controlled by aresetn_src.
core[1~3]_resetn is controlled by SMU.
Add a path for reset core 0

## Slide 5: Old hierarchy block diagram in AE350
ae350_smu_apbif
ae350_smu_mpd
ae350_smu_aopd_top
ae350_smu_aopd_core
ae350_aopd_pin
ae350_aopd_clkgen
ae350_aopd_rstgen
ae350_aopd_testgen
ae350_smu
Registers
FSM for power mode
Test signal connection
Clock signal with test_mode mux
Reset signal with test_mode mux
IO Pad for aopd_porb/om/jtag_tck/wakeup/rtc_wakeup/mpd_pwr_pff
Synchronizer for RTC signal

## Slide 6: New hierarchy block diagram
ae350_smu_apbif
ae350_smu_mpd
ae350_smu_aopd_core
ae350_aopd_pin
ae350_aopd_clkgen
ae350_aopd_rstgen
ae350_aopd_testgen
ae350_smu(Always-on region)
Registers
Test signal connection
Clock signal with test_mode mux
Reset signal with test_mode mux
IO Pad for aopd_porb/om/jtag_tck/wakeup/rtc_wakeup/mpd_pwr_pff
Synchronizer for RTC signal
ae350_smu_pd
Core 0 and L2/Core 1~3
FSM for power mode

## Slide 7: New global CSR for ae350_smu
Power Mode Cycle Register (PMCR) (0x100)
Name | Bit | Type | Description | Reset
ret_cyc | 15:0 | RW | Cycles for retention state waiting | 1
iso_cyc | 31:16 | RW | Cycles for isolation state waiting | 1
Power Mode Disable Initialization Register (PMDIR) (0x104)
Name | Bit | Type | Description | Reset
disable_init | 31:0 | RW | Control disable init for memories | 0

## Slide 8: New CSR for ae350_smu_pd
Power Status Register (PSR) (0x200)
Name | Bit | Type | Description | Reset
pwr_st | 3:0 | RO | Power status 0:ACTIVE 1:DVFS 2:ISOLATION 3:RETENTION 4:LIGHTSLEEP 5:DEEPSLEEP | 0
Notes: SMU address mapping=0xF0100000~0xF01FFFFF

## Slide 9: New CSR for ae350_smu_pd
Power Control Register (PCR) (0x208)
Name | Bit | Type | Description | Reset
pwr_ctrl_cmd | 3:0 | RW | Power control command 0: No action 1: DVFS 2: Light Sleep 3: Deep Sleep | 0
pwr_ctrl_frq | 7:4 | RO | Reserved for frequency vector | 0
pwr_ctrl_vol | 11:8 | RW | Voltage vector for DVFS | 0
Wakeup Enable Register (WER) (0x204)
Name | Bit | Type | Description | Reset
wakeup_en | 31:0 | RW | Wakeup event enable 0:Disable wakeup event 1:Enable wakeup event | 0xffffffff

## Slide 10: Power mode definition
DVFS
  Change voltage and frequency
Light Sleep
  Core and RAM are clock-gated.
Deep Sleep
  Core and RAM are powered off.

## Slide 11: ae350_smu_mpd
Remove core clock/power related logic
  standby state machine
  smu2core_standby_req
  smu2core_wakeup_ok
  core2smu_wfi_mode

## Slide 12: ae350_smu Interface
Global signal for all power domain
  smu_disable_init[31:0](input): Indicate signal which is asserted by PMDIR
    For icache_disable_init/dcache_disable_init/l2_disable_init

## Slide 13: ae350_smu_pd Interface
Control signal from power domain (with synchronizer)
  pd_ready(input): Indicate this power domain is ready for power change
    Connect to core_wfi_mode that core ready for power change
  pd_wakeup_event[31:0](input): Indicate this power domain should be wakeup
    Connect to msip/meip/mtip/debugint/alm/wi/smu for cores wakeup event
Control signal with ae350_smu_apbif
  smu_wakeup_enable[31:0](input): Indicate pd_wakeup_event is valid for wakeup
  smu_pwr_ctrl_frq[3:0] (input): Indicate frequency vector
  smu_pwr_ctrl_vol[3:0] (input): Indicate voltage vector
  smu_pwr_ctrl_cmd[3:0] (input): Indicate power command
  smu_pwr_st[3:0] (output): Indicate power status

## Slide 14: ae350_smu_pd Interface
Power control signal with voltage/clock source
  pd_pwr_stable(input): Power is stable for the power domain from voltage regulator
  pd_vol_scale_req(output): Voltage scaling vector require to voltage regulator
  pd_vol_scale(output): Voltage scaling vector to voltage regulator
  pd_vol_scale_ack(input): Voltage scaling vector ack from voltage regulator
  pd_frq_scale_req(output): Frequency scaling vector require to clock generator
  pd_frq_scale(output): Frequency scaling vector to clock generator
  pd_frq_scale_ack(input): Frequency scaling vector ack from clock generator
Power control signal for power domain
  pd_iso_en(output): Isolation indicator
  pd_ret_en(output): Retention indicator
  pd_clk_off(output): Clock shut-off indicator
  pd_pwr_off(output): Power region shut-off indicator

## Slide 15: Sample block diagram for power domain
Clock Generator
VRM
Power switch
Power domain
Isolation cell
Retention cell
pd_ready
pd_pwr_off
pd_clk_off
pd_ret_en
pd_iso_en
pd_vol_scale_req
pd_pwr_stable
pd_vol_scale
pd_vol_scale_ack
pd_frq_scale_req
pd_frq_scale
pd_frq_scale_ack
core_clk
vout
SRAM
SMU
PLIC
PLMT
Debug System
Always-on domain
Customer provided
Core domain (cpu_core_top)
Software PLIC
RTC
Platform domain
AXI

## Slide 16: FSM status
0x0:ST_ACTIVE
0x1:ST_DVFS
0x2:ST_ISOLATION
0x3:ST_RETENTION
0x4:ST_LIGHTSLEEP
0x5:ST_DEEPSLEEP

## Slide 17: FSM
ST_ACTIVE
ST_ISOLATION
ST_RETENTION
ST_LIGHTSLEEP
ST_DEEPSLEEP
ST_DVFS
pd_ready==1&&
cmd==DEEPSLEEP
pd_ready==1&&
cmd==DVFS
pd_frq_scale_ack&&
pd_vol_scale_ack
pd_ready==1&&
cmd==LIGHTSLEEP
counter>=ret_cyc&&
cmd==DEEPSLEEP
counter>=iso_cyc
counter>=iso_cyc
counter>=ret_cyc
pd_wakeup_event&&pd_pwr_stable
pd_wakeup_event&&
pd_pwr_stable

## Slide 18: Timing diagram for deep sleep mode
Power off
pd_ready
pd_iso_en
pd_ret_en
pd_pwr_off
pd_clk_offf
ST_ACTIVE
ST_ISOLATION
ST_RETENTION
ST_DEEPSLEEP
ST_RETENTION
ST_ISOLATION
ST_ACTIVE

## Slide 19: Power control signal by FSM
 | pd_iso_en | pd_ret_en | pd_clk_off | pd_pwr_off
ST_NORMAL | 0 | 0 | 0 | 0
ST_DVFS | 0 | 0 | 0 | 0
ST_ISOLATION | 1 | 0 | 0 | 0
ST_RETENTION | 1 | 1 | 0 | 0
ST_LIGHTSLEEP | 1 | 1 | 1 | 0
ST_DEEPSLEEP | 1 | 1 | 1 | 1

## Slide 20: Future work
Power domain inside SMU for ultra-low power
Different frequency between cores and L2

## Slide 21: Thank You!
www.andestech.com

## Slide 22
Thank You!

## Slide 23: Request for L2 design
For DVFS
  Standby command and standby signal
  Wakeup event source
Result
  L2 is bind to hart 0
  Add standby signal to L2

## Slide 24: Original CSR for ae350_smu_apbif
0x00: `AE350_PRODUCT_ID
0x04: `AE350_BOARD_ID
0x10: {21'h0, wrsr_dbg, wrsr_alm, wrsr_extw, 3'h0, wrsr_sw, wrsr_wdt, wrsr_hw, wrsr_mpor, wrsr_apor}
0x1C: {21'h0, wr_mask_reg, 8'h0}
0x20: {21'h0, clock_en_reg}
0x24: {28'h0, clock_ratio_reg}
0x30: userdr0_reg_out[31:0]
0x34: userdr1_reg_out[31:0]
0x40: scratch_reg_out[31:0]
0x44: core_resetn_reg_out
0x50: core0_reset_vector[31:0]
0x54: core1_reset_vector[31:0]
0x58: core2_reset_vector[31:0]
0x5c: core3_reset_vector[31:0]
Notes: Wake-up and Reset Status Register

## Slide 25: Original design in AE210P