## Slide 1: Vicuna AE350 SMU Design Specification
Driving Innovations™
Ellis Chen
2019-03-07

## Slide 2: Outline
Feature of ae350_smu_pd
ae350_rstgen
  Add path for reset core 0
ae350_smu
  Old/New hierarchy block diagram
ae350_smu_apbif
  New register for power control
ae350_smu_mpd (Main power domain)
  Remove core clock/power related logic
ae350_smu_pd (Core/L2 power domain)
  Interface
  FSM for power control

## Slide 3: Feature of ae350_smu_pd
Support for a power/clock domain control
  Power source
  Clock source
  Isolation cell
  Retention cell
Support for wakeup event mask
Support for light sleep/deep sleep modes
Support for dynamic voltage frequency scaling (DVFS)

## Slide 4: Assumption for simplification
Only one clock source and voltage source
  Simplify multi-core DVFS flow
Only core 0 can apply DVFS change
  Add option for power domain control support

## Slide 5: ae350_rstgen
In ae350_rstgen, core0_resetn is controlled by aresetn_src.
core[1~3]_resetn is controlled by SMU.
Add a path for reset core 0

## Slide 6: Old hierarchy block diagram in AE350
ae350_smu_apbif
ae350_smu_mpd
ae350_smu_aopd_top
ae350_smu_aopd_core
ae350_aopd_pin
ae350_aopd_clkgen
ae350_aopd_rstgen
ae350_aopd_testgen
ae350_smu
Registers
FSM for power mode
Test signal connection
Clock signal with test_mode mux
Reset signal with test_mode mux
IO Pad for aopd_porb/om/jtag_tck/wakeup/rtc_wakeup/mpd_pwr_pff
Synchronizer for RTC signal

## Slide 7: New hierarchy block diagram
ae350_smu_apbif
ae350_smu_mpd
ae350_smu_aopd_core
ae350_aopd_pin
ae350_aopd_clkgen
ae350_aopd_rstgen
ae350_aopd_testgen
ae350_smu(Always-on region)
Registers
Test signal connection
Clock signal with test_mode mux
Reset signal with test_mode mux
IO Pad for aopd_porb/om/jtag_tck/wakeup/rtc_wakeup/mpd_pwr_pff
Synchronizer for RTC signal
ae350_smu_pd
Core 0 and L2/Core 1~3
FSM for power mode

## Slide 8: Macro and parameter for ae350_smu
Name | Description | Value
DVFS | DVFS support for this power domain | 1:yes 0:no
NHART | Number of harts | 1~4
CYCLE_WIDTH | Bit width for ret_cyc and iso_cyc | 4
DISALBE_INIT_WIDTH | Bit width for disable_init | Single core: 2 Multi-core: 2*N+1
WAKEUP_WIDTH | Bit width for wakeup_event | 7
Parameter
Marco
Name | Description | Value
NDS_IO_HART1 NDS_IO_HART2 NDS_IO_HART3 | I/O port for multi-cores | none
NDS_FPGA | Hardwired voltage related control to 0 in FPGA flow | none

## Slide 9: New CSR for ae350_smu
Power Mode Cycle Register (PMCR) (0x100)
Name | Bit | Type | Description | Reset
ret_cyc | CYCLE_WIDTH-1:0 | RW | Cycles for retention state waiting *Cycle time is SMU clock | 0
iso_cyc | CYCLE_WIDTH+15:16 | RW | Cycles for isolation state waiting *Cycle time is SMU clock | 0
Power Mode Disable Initialization Register (PMDIR) (0x104)
Name | Bit | Type | Description | Reset
disable_init | DISALBE_INIT_WIDTH-1:0 | RW | Control disable init for memories | 0

## Slide 10: New CSR for ae350_smu
Power Status Register (PSR) (0x204)
Name | Bit | Type | Description | Reset
pwr_st | 3:0 | RO | Power status 0x0:ACTIVE 0x1:DVFS 0x2:ISOLATION 0x3:RETENTION 0x4:LIGHTSLEEP 0x5:DEEPSLEEP | 0
Power Wakeup Record Register (PWRR) (0x208)
Name | Bit | Type | Description | Reset
pwr_wakeup_record | WAKEUP_WIDTH-1:0 | RW | Record pd_wakeup_event with wakeup_en mask when power command is finished | 0x0
Power Domain Select Register (PDSR) (0x200)
Name | Bit | Type | Description | Reset
pwr_index | 1:0 | RW | Select power domain for power command 0x0: Core 0 and L2 0x1: Core 1 0x2: Core 2 0x3: Core 3 | 0x0
Notes: SMU address mapping=0xF0100000~0xF01FFFFF

## Slide 11: New CSR for ae350_smu
Power Control Register (PCR) (0x210)
Name | Bit | Type | Description | Reset
pwr_ctrl_cmd | 3:0 | RW | Power control command 0: No action 1: DVFS 2: Light Sleep 3: Deep Sleep | 0
pwr_ctrl_frq | 7:4 | RW | Frequency vector for DVFS | 0
pwr_ctrl_vol | 11:8 | RO | Reserved for voltage vector for DVFS | 0
Wakeup Enable Register (WER) (0x20C)
Name | Bit | Type | Description | Reset
pwr_wakeup_en | WAKEUP_WIDTH-1:0 | RW | Wakeup event enable 0:Disable wakeup event 1:Enable wakeup event | 0xffffffff

## Slide 12: New CSR for ae350_smu
Power Interrupt Register (PIR) (0x214)
Name | Bit | Type | Description | Reset
pwr_ctrl_int_en | 0 | RW | Assert SMU interrupt for this power domain after power command is done | 0
pwr_ctrl_int_st | 1 | RO | Indicate SMU interrupt | 0
pwr_ctrl_int_clr | 2 | W1C | Clear SMU interrupt | 0

## Slide 13: Power mode definition
DVFS
  Purpose: Dynamic change power for workload requirement
  Function: Change voltage and frequency
  Latency: For voltage/clock source, it might takes ms scale for scaling and stable.
Light Sleep
  Purpose: Fast response for interrupt and save power
  Function: Core and RAM are clock-gated.
  Latency: 1 cycle for enabling clock switch
Deep Sleep
  Purpose: Stop core and save most power
  Function: Core and RAM are powered off.
  Latency: For voltage/clock source, it might takes ms scale for turn-on and stable.

## Slide 14: ae350_smu_mpd
Remove core clock/power related logic
  standby state machine
  smu2core_standby_req
  smu2core_wakeup_ok
  core2smu_wfi_mode

## Slide 15: ae350_smu Interface
Global signal for all power domain
  smu_disable_init[31:0](input): Indicate signal which is asserted by PMDIR
    For icache_disable_init/dcache_disable_init/l2_disable_init
  debugint[NHART-1:0](input): When debugint is asserted, the power domain will be wakeup from light/deep sleep mode.

## Slide 16: ae350_smu_pd Interface
Control signal from power domain (with synchronizer)
  pd_standby(input): Indicate this power domain is ready for power change
    Connect to core_wfi_mode that core ready for power change
  pd_all_lightsleep(input): Indicate all power domains are light sleep mode
  pd_wakeup_event[WAKEUP_WIDTH-1:0](input): Indicate this power domain should be wakeup
    Connect to msip/meip/mtip/rtc_alarm/wi/smu for cores wakeup event
  pd_debugint(input): Indicate this power domain should be wakeup by debugint
    Connect to debugint for cores wakeup event

## Slide 17: ae350_smu_pd Interface
Control signal with ae350_smu_apbif
  smu_ret_cyc_we(input): Indicate smu_ret_cyc is updated
  smu_ret_cyc[CYCLE_WIDTH-1:0](input): Indicate retention cycle
  smu_iso_cyc_we(input): Indicate smu_iso_cyc is updated
  smu_iso_cyc[CYCLE_WIDTH-1:0](input): Indicate isolation cycle
  smu_wakeup_enable_we(input): Indicate smu_wakeup_enable is updated
  smu_wakeup_enable[WAKEUP_WIDTH:0](input): Indicate pd_wakeup_event is valid for wakeup
  smu_pwr_ctrl_cmd_we(input): Indicate smu_pwr_ctrl_* is updated
  smu_pwr_ctrl_cmd[3:0] (input): Indicate power command
  smu_pwr_ctrl_frq[3:0] (input): Indicate frequency vector
  smu_pwr_ctrl_vol[3:0] (input): Indicate voltage vector
  smu_pwr_ctrl_cmd_pending[3:0] (output): Indicate power command pending in ae350_smu_pd
  smu_pwr_status[3:0] (output): Indicate power status

## Slide 18: ae350_smu_pd Interface
Power control signal with voltage/clock source
  pd_vol_stable(input): Voltage is stable for the power domain from voltage regulator
  pd_vol_scale_req(output): Voltage scaling vector require to voltage regulator
  pd_vol_scale(output): Voltage scaling vector to voltage regulator
  pd_vol_scale_ack(input): Voltage scaling vector ack from voltage regulator
  pd_frq_stable(input): Frequency is stable for the power domain from clock generator
  pd_frq_scale_req(output): Frequency scaling vector require to clock generator
  pd_frq_scale(output): Frequency scaling vector to clock generator
  pd_frq_scale_ack(input): Frequency scaling vector ack from clock generator
Power control signal for power domain
  pd_iso_en(output): Isolation indicator
  pd_ret_en(output): Retention indicator
  pd_pwr_off(output): Power region shut-off indicator

## Slide 19: List for wakeup event
RISC-V
  Software PLIC: msip
  PLIC: meip
  PLMT: mtip
  Debug mode: debugint (Not maskable)
Platform
  RTC: rtc_alarm
  SMU: smu
  External event
Notes: PLIC:
11268:assign int_src[1] = rtc_int_period;
11269:assign int_src[2] = rtc_int_alarm;
11270:assign int_src[3] = pit_intr;
11271:assign int_src[4] = spi1_int;
11272:assign int_src[5] = spi2_int;
11273:assign int_src[6] = i2c_int;
11274:assign int_src[7] = gpio_intr;
11275:assign int_src[8] = uart1_int;
11276:assign int_src[9] = uart2_int;
11277:assign int_src[10] = dma_int;
11278:assign int_src[11] = 1'b0;
11279:assign int_src[12] = 1'b0;
11280:assign int_src[13] = 1'b0;
11281:assign int_src[14] = 1'b0;
11282:assign int_src[15] = 1'b0;
11283:assign int_src[16] = 1'b0;
11284:assign int_src[17] = ssp_intr;
11285:assign int_src[18] = sdc_int;
11286:assign int_src[19] = mac_int;
11287:assign int_src[20] = lcd_intr;
11288:assign int_src[21] = 1'b0;
11289:assign int_src[22] = 1'b0;
11290:assign int_src[23] = 1'b0;
11291:assign int_src[24] = 1'b0;
11292:assign int_src[25] = 1'b0;
11293:assign int_src[26] = smu2core_standby_req;
11294:assign int_src[27] = smu2core_wakeup_ok;
11295:assign int_src[28] = 1'b0;
11296:assign int_src[29] = 1'b0;
11297:assign int_src[30] = 1'b0;
11298:assign int_src[31] = 1'b0;

## Slide 20: Sample block diagram for power domain
Clock Generator
VRM
Power switch
Power domain
Isolation cell
Retention cell
pd_standby
pd_pwr_off
pd_ret_en
pd_iso_en
pd_vol_scale_req
pd_vol_stable
pd_vol_scale
pd_vol_scale_ack
pd_frq_scale_req
pd_frq_scale
pd_frq_scale_ack
core_clk
vout
SRAM
SMU
PLIC
PLMT
Debug System
Always-on domain
Customer provided
Core domain (cpu_core_top)
Software PLIC
RTC
Platform domain
AXI
pd_clk_stable
Clock switch
pd_clk_en

## Slide 21: Sample block diagram for power domain
Always-on domain
Customer provided
Core domain
Platform domain

## Slide 22: FSM status
0x0:ST_ACTIVE
0x1:ST_DVFS
0x2:ST_ISOLATION
0x3:ST_RETENTION
0x4:ST_LIGHTSLEEP
0x5:ST_DEEPSLEEP

## Slide 23: FSM
ST_ACTIVE
ST_ISOLATION
ST_RETENTION
ST_LIGHTSLEEP
ST_DEEPSLEEP
ST_DVFS
pd_standby==1&&
cmd==DEEPSLEEP
pd_all_lightsleep==1&&
cmd==DVFS
pd_frq_scale_ack if (new_frq_scale!=old_frq_scale)
pd_vol_scale_ack if (new_vol_scale!=old_vol_scale)
pd_standby==1&&
cmd==LIGHTSLEEP
counter>=ret_cyc
counter>=iso_cyc
counter>=iso_cyc
counter>=ret_cyc
(pd_wakeup_event||pd_debugint)&&
pd_clk_stable
(pd_wakeup_event||pd_debugint)&&
pd_pwr_stable

## Slide 24: FSM with Core control and status
ST_ACTIVE
ST_ISOLATION
ST_RETENTION
ST_LIGHTSLEEP
ST_DEEPSLEEP
ST_DVFS
core_resetn is asserted
cmd is cleared
core is in WFI mode
core is in WFI mode
core is in WFI mode
core_resetn is de-asserted
cmd is cleared
Option: Assert SMU interrupt
pd_pwr_off=1
pd_clk_off=1
pd_iso_en=1
pd_ret_en=1
pd_iso_en=1
pd_iso_en=1
pd_ret_en=1
cmd is cleared
pd_clk_off=1
pd_clk_off=1

## Slide 25: Core self wakeup flow
Core wants to do DVFS by itself
  Core send power command to SMU
  Core 0 setup SMU interrupt enable
  Core executes WFI
  SMU handles power command
  SMU asserts in interrupt to Core
  Core exits WFI mode

## Slide 26: Core to Core wakeup flow
Core 0 asks Core 1 to deep sleep mode
  Core 0 send power command to SMU for Core 1
  Core 0 inform other Core 1 to enter WFI mode
  SMU handles power command
    Core 1 enters deep sleep mode
  Core 1 wakeup by Core 0 by another core

## Slide 27: Multi-Core DVFS flow
Cluster executes frequency change
  Core 0 mask all wakeup event exclude SMU interrupt
  Core 0 send light sleep mode to SMU for other cores
  Core 0 setup SMU interrupt enable
  Core 0 inform other cores to execute WFI
    Other cores enter light sleep mode by SMU
  Core 0 executes WFI
    Core 0 enters DVFS by SMU
  SMU handles power command to all cores
  Core 0 is wakeup by SMU
  Core 0 send SMU interrupt to other cores
  Other cores are wakeup by SMU

## Slide 28: Debug module and SMU interactive
In ST_LIGHTSLEEP and ST_DEEPSLEEP
  Core can be wakeup by SMU which is returning ST_ACTIVE.
ST_ISOLATION and ST_RETENTION
  Core can’t handle debug interrupt because clock is off.
ST_DVFS
  core_clk is off until power change is stable.

## Slide 29: Timing diagram for deep sleep mode
Power off
pd_standby
pd_iso_en
pd_ret_en
pd_pwr_off
pd_clk_off
ST_ACTIVE
ST_ISOLATION
ST_RETENTION
ST_DEEPSLEEP
ST_RETENTION
ST_ISOLATION
ST_ACTIVE
core_resetn

## Slide 30: Power control signal by FSM
 | pd_iso_en | pd_ret_en | pd_clk_off | pd_pwr_off
ST_ACTIVE | 0 | 0 | 0 | 0
ST_DVFS | 0 | 0 | 1 | 0
ST_ISOLATION | 1 | 0 | 0 | 0
ST_RETENTION | 1 | 1 | 0 | 0
ST_LIGHTSLEEP | 1 | 1 | 1 | 0
ST_DEEPSLEEP | 1 | 1 | 1 | 1

## Slide 31: Future work
Core 0 and L2 are de-coupled in power domain.
Power domain inside SMU for ultra-low power
Different frequency between cores and L2