## Slide 1
Power management overview
2021/09/03

## Slide 2
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 3
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 4
Why Power Management?
Why need power management?
  Power/energy saving
  temperature control
application:
  Screen lock
  Hibernate
  CPU frequency reduce

## Slide 5
Power Management Overview
Power management:
  SW (Linux)
    U-mode:
      Linux sysfs command
    S-mode:
      Linux Power management framework
    M-mode:
      architecture depend power management framework
        OpenSBI(RISC-V), PSCI(ARM), ACPI(X86)
  HW
    PMIC (power manage IC)
      SMU (system management unit)
      PMU (power management unit)
sysfs
PM
HSM
SMU
mem
bus
cpu
Peripheral device
sw
hw

## Slide 6
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 7
Power management IC
PMIC (power management IC)
  SMU (system management unit)
  PMU (power management unit)

## Slide 8
Power management IC
PMIC (power manage IC)
  SMU (system management unit)
    Clock setting
    PMU (power management unit)
      Provide different voltage to different devices
        Cpu, camera, usb …..
      Core reset
      Clock frequency adjustment.

## Slide 9
Ax45 SMU Block diagram

## Slide 10
Ax45 SMU Block diagram
HW
  CPU region
    CPU
    L1
    L2
CPU region

## Slide 11
Ax45 SMU Block diagram
HW
  CPU region
    CPU
    L1
    L2
  Debug region
    Debug module
CPU region
Debug region

## Slide 12
Ax45 SMU Block diagram
HW
  CPU region
    CPU
    L1
    L2
  Debug region
    Debug module
  Mem & device & bus region
    Memory subsystem
    AXI/AHB/APB Bus
    Peripheral devices
CPU region
mem & device & bus region
Debug region

## Slide 13
Ax45 SMU Block diagram
HW
  CPU region
    CPU
    L1
    L2
  Debug region
    Debug module
  Mem & device & bus region
    Memory subsystem
    AXI/AHB/APB Bus
    Peripheral devices
  Always on region (AOPD)
    RTC
    WDT
CPU region
Always on region
mem & device & bus region
Always on region
Debug region

## Slide 14
Ax45 SMU Block diagram
HW
  CPU region
    CPU
    L1
    L2
  Debug region
    Debug module
  Mem & device & bus region
    Memory subsystem
    AXI/AHB/APB Bus
    Peripheral devices
  Always on region (AOPD)
    SMU
    RTC
    WDT
CPU region
Always on region
mem & device & bus region
SMU
Always on region
Debug region

## Slide 15
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 16
Ax45 power domain
7 power domains
  PCS (power control slot)
  PCS0~6

## Slide 17
pcs0
Always on region
SMU
Always on region
only AOPD remained

## Slide 18
pcs1
Always on region
SMU
Always on region
AOPD + debug remained
Debug region

## Slide 19
pcs2
Always on region
SMU
Always on region
AOPD +
debug +
Mem
remained
Debug region
mem & device & bus region

## Slide 20
Pcs3~6
Always on region
SMU
Always on region
AOPD +
debug +
Mem +
cpu
remained
Debug region
mem & device & bus region
CPU region

## Slide 21
Ax45 SMU power down sequence
Set smu register
  PCS_CTL
  PCS_WE
  Reset_vector
CPU region
AE350 SMU (Hardware)
  Disable core_clk, lm_clk, dcu_clk
  Activate power clamps (電壓保護)
  Remove power
  Assert core_reset_n

## Slide 22
Ax45 SMU power up sequence
1. Device send irq to SMU
2. SMU wakeup other devices
CPU region
AE350 SMU (Hardware)
  Assert core_reset_n
  Enable core_clk, lm_clk, dcu_clk
  Apply Power (UPF Simulation)
  Disable power clamps (UPF simulation)
  De-assert core_reset_n

## Slide 23
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 24
Ax45 SMU registers
MMIO registers
  AE350 BASE: 0xf0100000 (PA)
Important registers:
  0x50~0x6c: reset_vector
  0x84: PCS_SCRATCH
  0x90: PCS_WE
  0x94: PCS_CTL
  0x98: PCS_STATUS
SMU HW
Pcs1
pcs_cfg
Pcs1
pcs_status
Pcs2
pcs_cfg
…
…
…
systemver
Hart3_reset_vector_hi
ram
Smu mmio registers
0xf0100000
0xf0100080
0xf01000a0

## Slide 25
Ax45 SMU registers
Power Domain Wakeup Event Enable (PCS_WE) (0x90)
  Select wakeup sources

## Slide 26
Ax45 SMU registers
Power Control Slot Control Register (PCS_CTL) (0x94)
  Control per core PCS:
    Enter Light sleep:
      0b00000011 = 0x3
    Enter deep sleep:
      0b00001011 = 0xb
    Wakeup:
      0b00001000 = 0x8
000
00000
PCS_CTL
cmd
param

## Slide 27
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 28
Terminology of power management
AE350 Power management status:
  Normal
  Suspend to idle (freeze)
    wfi()
  Suspend to idle (light sleep) (half PCS3)
    Disabled Core clk
      Disable L1
    L2 still on
  Suspend to ram (deep sleep) (PCS3)
    Core power down
      Disable L1
      All Register reset
    Disabled L2
  Suspend to disk (Not support) (PCS2)
    Disabled Core clk
    Disabled L2
    Disable Memory

## Slide 29
AE350 power up/down sequence
Power down sequence
  User
    echo 0 > /sys/devices/system/cpu/cpu[n]/online
    echo standby > /sys/power/state
    echo mem > /sys/power/state
  Core[n] (Software OpenSBI smu.c)
    Need to be implemented
  AE350 SMU (Hardware)
    Disable core_clk, lm_clk, dcu_clk
    Activate power clamps (UPF simulation)
    Remove power (UPF simulation)
    Assert core_reset_n
Power up sequence
  User
    echo 1 > /sys/devices/system/cpu/cpu[n]/online
    Rtc or uart wakeup
  Core[n] (Software OpenSBI smu.c)
    Need to be implemented
  AE350 SMU (Hardware)
    Assert core_reset_n
    Enable core_clk, lm_clk, dcu_clk
    Apply Power (UPF Simulation)
    Disable power clamps (UPF simulation)
    De-assert core_reset_n
sysfs
PM
HSM
SMU
mem
bus
cpu
Peripheral device
sw
hw

## Slide 30
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 31
OpenSBI HSM
OpenSBI HSM (Hart State Management Extension)
Current Andes OpenSBI has not implemented suspend status.

## Slide 32
OpenSBI SMU Driver
OpenSBI HSM + SMU driver
Trigger hart stop
Enter sleep mode:
  Deep sleep
  Light sleep
  Cpu hotplug with deep sleep
Exit sleep mode:
  Deep sleep
  Light sleep
  Cpu hotplug with deep sleep
SMU hardware
OpenSBI SMU driver

## Slide 33
System overall flow for power management

## Slide 34
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 35
Light sleep Implementation
process
suspend
Driver
suspend
Disable
D$
Write back
D$
Disable CM
Set
PCS_WE
Disable
MIE*
Set 0x3
PCS_CTL
Check
PCS_STATUS
WFI
Disable IRQ
Setup SMU
Wait for other cores ready
Disable Cache
Enter sleep mode
Other cores
main core
Kernel
OpenSBI SMU Driver
Main core
other core
other core
other core
SMU
Light sleep power down
Other hart
sleep
main core
Other cores
PCS_WE:
  Main core: rtc or uart
  Other core: MSIP

## Slide 36
Light sleep Implementation
Enable
MIE*
Enable IRQ
Enable Cache
enable
D$
enable CM
Kernel
OpenSBI SMU Driver
SMU
Light sleep power up
Wakeup event
Send MSIP to wake other cores up
Driver
resume
Other
Cores
wakeup
process
resume
Main
Core
wait
Wait for
other cores
ready
Other cores
main core
other core
other core
other core
Main core

## Slide 37
Light sleep Implementation
Light sleep:
  Wakeup PC is the next instruction after wfi
wakeup here
sleep here

## Slide 38
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 39
Deep sleep Implementation
process
suspend
Driver
suspend
Disable
MIE*
Check
PCS_STATUS
WFI
Disable IRQ
Setup SMU
Wait for other cores ready
Disable
Cache
Disable D$
Write back D$
Disable CM
Enter sleep mode
Kernel
OpenSBI SMU Driver
Main core
other core
other core
other core
SMU
deep sleep power down
Other hart
sleep
main core
Other cores
PCS_WE:
  Main core: rtc or uart
  Other core: MSIP
Store
sp address
to
PCS_SCRATCH
Deep sleep only
Set
PCS_WE
Set 0xb
PCS_CTL
Set
Reset_vec
Other cores
main core
Store
Registers
Disable L2
Check L2 status
Store regs

## Slide 40
Deep sleep Implementation
HW SMU
CORE0_
PCS_SCRATCH
CORE1_
PCS_SCRATCH
L1
mcache_ctl
x0
x31
…
…
pmpaddr15
…
satp
…
sp
L2
RAM
mcache_ctl
x0
x31
…
…
pmpaddr15
…
satp
…
mcache_ctl
x0
x31
…
…
pmpaddr15
…
satp
…
L1_cctl_wb
L2_cctl_wb
Deep sleep:
  Backup CSR to sp
    X0~X31
    Floating CSR (Not implemented)
    Machine mode CSR
    Supervisor mode CSR
    Andes Custom CSR
    PMP CSR
  Save “sp” to PCS_SCRATCH
  Set reset vector
    Hart “PC” will be reset
    Need to set return PC in HART0_RESET_VECTOR_LO
  Disable D-cache & wb
    Write back L1 to L2
  Disable CM
  Disable L2 & wb
    Write back L2 to RAM
  WFI
  L1 & L2 will be reset 0 after deep sleep
L1
HW SMU
CORE0_
PCS_SCRATCH
CORE1_
PCS_SCRATCH
L2
RAM
mcache_ctl
x0
x31
…
…
pmpaddr15
…
satp
…
L1
mcache_ctl
x0
x31
…
…
pmpaddr15
…
satp
…
sp
L1
Deep Sleep

## Slide 41
Deep sleep Implementation
Deep sleep:
  Enable CM
  Enable I/D Cache
  Enable L2
  restore “sp” from PCS_SCRATCH
  Restore CSR
    X0~X31
    Floating CSR (Not implemented)
    Machine mode CSR
    Supervisor mode CSR
    Andes Custom CSR
    PMP CSR
HW SMU
CORE0_
PCS_SCRATCH
CORE1_
PCS_SCRATCH
L1
mcache_ctl
x0
x31
…
…
pmpaddr15
…
satp
…
sp
L2
RAM
mcache_ctl
x0
x31
…
…
pmpaddr15
…
satp
…
L1
mcache_ctl
x0
x31
…
…
pmpaddr15
…
satp
…
sp
wakeup
L1
HW SMU
CORE0_
PCS_SCRATCH
CORE1_
PCS_SCRATCH
L2
RAM
mcache_ctl
x0
x31
…
…
pmpaddr15
…
satp
…
L1
  L1 & L2 do not have the data and will fetch the data from ram.

## Slide 42
Deep sleep Implementation
Enable
MIE*
Enable IRQ
Kernel
OpenSBI SMU Driver
SMU
Deep sleep power up
Wakeup event
Send MSIP to wake other cores up
Driver
resume
Other
Cores
wakeup
process
resume
Main
Core
wait
Wait for
other cores
ready
Other cores
main core
other core
other core
other core
Main core
enable
D$/I$
enable
CM
restore
Registers
from ram
(sp address)
Restore regs
Deep sleep only
Get “sp”
address
From
PCS_SCRATCH
enable
L2
Enable
Cache

## Slide 43
Deep sleep Implementation
Deep sleep:
  Wakeup PC is the not the next instruction after wfi, it will jump to HART0_RESET_VECTOR_LO.
    Set HART0_RESET_VECTOR_LO=cpu_resume()
    deep sleep (wfi)
    First instruction will be cpu_resume()
      Csrr t0, CSR_MCAUSE
sleep here
wakeup here:
HART0_RESET_VECTOR_LO

## Slide 44
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 45
CPU Hotplug Deep sleep Implementation
process
suspend
Driver
suspend
Disable
MIE*
Check
PCS_STATUS
WFI
Wait for other cores ready
Disable
Cache
Disable D$
Write back D$
Disable CM
Enter sleep mode
Kernel
OpenSBI SMU Driver
Main core
SMU
CPU hotplug deep sleep power down
Other hart
sleep
main core
PCS_WE:
  core: 0
    Should not be waken up by any wakeup event
Store
sp address
to
PCS_SCRATCH
No need in CPU hotplug Deep sleep
Set
PCS_WE
Set 0xb
PCS_CTL
Set
Reset_vec
Store
Registers
Disable L2
Check L2 status
Store regs
Disable IRQ
Setup SMU

## Slide 46
CPU Hotplug Deep sleep Implementation
Enable
MIE*
Enable IRQ
Kernel
OpenSBI SMU Driver
SMU
Deep sleep power up
Other core write
wakeup signal(0x8) to
HART[n]_PCS_CTL
Driver
resume
Other
Cores
wakeup
process
resume
Main
Core
wait
Wait for
other cores
ready
core
enable
D$/I$
enable
CM
restore
Registers
from ram
(sp address)
Restore regs
Get “sp”
address
From
PCS_SCRATCH
enable
L2
Enable
Cache

## Slide 47
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 48
Power management interface
ACPI
  Intel x86
PSCI
  arm
OpenSBI
  RISC-V
sysfs
PM
PM
interface
SMU
mem
bus
cpu
Peripheral device
sw
hw

## Slide 49
Power management interface
ACPI (Advanced Configuration and Power Interface)

## Slide 50
Power management interface
ACPI (Advanced Configuration and Power Interface)

## Slide 51
Power management interface
PSCI (The Power State Coordination Interface)

## Slide 52
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 53
Linux Power management framework
Linux power management framework
  Core status management
    Idle, cpu_up, cpu_die …
  CPU hotplug management
  System suspend/resume management
    Peripheral device suspend/resume
    Console suspend/resume
    Process suspend/resume
  CPU frequency management
sysfs
PM
PM
interface
SMU
mem
bus
cpu
Peripheral device
sw
hw

## Slide 54
Linux Power management framework
Linux power management framework

## Slide 55
Linux Power management framework
Generic
pm driver
platform
pm driver
Disable other CPUs:
Other cores jump to M-mode
Main core:
Move these functions to OpenSBI SMU driver

## Slide 56
Linux Power management framework
Generic
pm driver
platform
pm driver
freezing of tasks
  Freeze work_queue
    set max_active=0
  Freeze user process & kthread

## Slide 57
Linux Power management framework
Generic
pm driver
platform
pm driver
Suspend console
  Redirect console to kmsg
  Lock console in kernel/printk.c
Resume console
  Unlock console in kernel/printk.c
  Redirect console to original console

## Slide 58
Linux Power management framework
Generic
pm driver
platform
pm driver
Suspend/resume peripheral devices driver
  If not suspend peripherals may cause unexpected bus hang.
  Peripheral data loss ??
Bus hanged occurs when MAC or LCD keep sending signal to bus after deep sleep.
Bus wants to connect with L2, but L2 is powered down.

## Slide 59
Outline
Power management overview
Power management (HW)
  Ax45 power domain
  Ax45 SMU registers
Power management (SW)
  OpenSBI SMU Driver
    Light sleep implementation
    Deep sleep implementation
    CPU hotplug implementation
  Power management interface
  Linux Power management framework
  User space power management command

## Slide 60
User space command
CPU Hotplug with deep sleep
  offline
    echo 0 > /sys/devices/system/cpu/cpu[X]/online
  online
    echo 1 > /sys/devices/system/cpu/cpu[X]/online
Deep/Light sleep
  Setup wakeup source
    echo enabled > /sys/devices/platform/soc/f0300000.serial/tty/ttyS0/power/wakeup
  Sleep
    Deep sleep:
      echo mem > /sys/power/state
    Light sleep:
      echo standby > /sys/power/state
  Wakeup
    Press any key on keyboard
sysfs
PM
PM
interface
SMU
mem
bus
cpu
Peripheral device
sw
hw

## Slide 61
User space command
Deep sleep
light sleep
Cpu hotplug with deep sleep