## Slide 1: Verify Arbiter
Driving Innovations™
Jack Chang
2018-03-02

## Slide 2: Arbiter
Fair arbiter
  Pointer-Based Round-Robin
Strict priority arbiter
Weighted priority arbiter
Dynamic priority arbiter
  FIFO-Based Priority
  Credit-Based Priority

## Slide 3: Pointer-Based Round-Robin
if port 0 was given a grant on the previous arbitration cycle, then port 1 will be designated the highest priority port for the next arbitration cycle
For any port request service, that particular port should receive a grant within N arbitration cycles

## Slide 4: Fairness Round-Robin Requirements

## Slide 5: Strict Priority Arbiter
Always issues a grant to a requesting, higher-priority port before it issues a grant to a lower-priority port.
Assigns the highest priority to the lowest-numbered port
If there is a pending request on Port0, then it must be serviced before all other ports

## Slide 6: Strict Priority Arbiter Requirements

## Slide 7: Weighted Priority Arbiter
A round-robin priority arbiter gives ports 0 through 3 twice as much bandwidth as ports 4 through 15
Requirements:
  When Port0 to Port3 issue a request, they should get a grant before getting 10 other transfers.
  When Port4 to Port15 issue a request, they should get a grant before getting 20 other transfers.
  The number of transfers (grants) for a weighted priority requirements scheme can be generalized to total_weight/weight_of_port.

## Slide 8: Weighted Priority Arbiter Requirements
weight_p1!=3’b0
-1’b1
-1’b1

## Slide 9: Dynamic Priority Arbiter
The priority is changed dynamically.
  FIFO-Based
  Credit-Based
Priority arbiter requirements:
  If there is only one port with high priority, it will always get the grant.
  If there is more than one port with high priority, those ports will follow the round-robin fairness requirement.
  If there is no port with high priority, all normal-priority ports will follow the round-robin fairness requirement.

## Slide 10: FIFO-Based Priority Arbiter
All ports are initially put into the normal-priority bracket and arbitrated using the round-robin scheme.
When the input FIFO for Port0 reaches the high-water mark, it sends a signal to elevate Port0 to the high-priority bracket.
The ports in the high-priority bracket have strict priority over the ones in the normal-priority bracket. After Port0 gets a grant, it will be placed back in the normal-priority bracket.

## Slide 11: Credit-Based Priority Arbiter
If credit is available, each grant will decrement the credit by one.
If a credit refill condition occurs, the credit will be initialized.
  All ports reach zero
  All non-zero credit ports do not have a request

## Slide 12: Dynamic Priority Arbiter Requirements

## Slide 13: Dynamic Priority Arbiter Constraint

## Slide 14: FIFO-Based Priority Requirements

## Slide 15: Credit-Based Priority Requirements

## Slide 16
Thank You!

## Slide 17: Reference
  T:\vendors\Cadence\JasperGold\application_notes\
    an_arbiter_fairness.pdf
    an_arbiter_strict.pdf
    an_arbiter_weighted.pdf
    an_arbiter_dynamic.pdf
Notes: 17