## Slide 1: Verilog Design Coding Style
Driving Innovations™
Osban
2017/2/24

## Slide 2: RTL Coding Style (v1.0)
The code will be used for 10 years or longer
  Readability
  Maintainability
  Extensibility
Notes: 2

## Slide 3: Module
One module per file
  Use function to name the module
Section
  Include
  Parameter
  IO declaration
  Wire and register declaration
  Function

## Slide 4: Naming Rule
The parameter/macro name should be all upper cases
  `define NDS_DCACHE_SUPPORT
  localparam NDS_DCACHE_REQ_NUM = 8;
Macro prefix
  NDS_XXX_YYY
The net and register name should be all lower cases
  wire dfb_data2_valid_set;
Signal name should be meaningful.
  reg [MSB:0] reg0;
  reg [MSB:0] tmpX;

## Slide 5: Naming Rule (2)
Interface signals
  Source_Desti_Name_Stage
    iiu_ieu_p1_current_pc_ex
  Single meaning
    mtlb_itlb_asstribute
    mtlb_itlb_c, mtlb_itlb_m …
Pipeline signals
  Name_Stage
  Name_Stage_nx

## Slide 6: Naming Rule (3)
Global system register signals
  Named by mnemonics_name and field_name defined in SPA
  reg_(Mnemonics)_(field) or reg_(field)
    EX: reg_psw_dt, reg_psw_cpl

## Slide 7: Constant
Declare parameter for meaningful constant
  System register value

## Slide 8: Always Block
5 kinds of always block
There is NO equation and `ifdef in the always block

## Slide 9: Example: Set/clr Flip Flop

## Slide 10: Example

## Slide 11: Unknown Propagation
Use “assign” instead of “always … if“
Set unknown in the default case

## Slide 12: State Machine
2 always block
Parameter for all states
Unknown for the default state

## Slide 13: Assignment
Do not
  `ifdef in the assignment
  Different assignment equations in different features

## Slide 14: Alignment
Indent
  Tab Or 8 spaces ?
Align the
  “=“, “<=“
  “? “, “:“, “; “
  “&“, “|“

## Slide 15: Alignment (2)

## Slide 16: Vperl
Generate ports
Connection in the top module
Generate similar code

## Slide 17: Generate
Add a label after the “begin”

## Slide 18: Comments in the `else and `endif
`else and `endif
  With comment from which `define

## Slide 19: Thank You!
www.andestech.com

## Slide 20
Thank You!