## Slide 1: RTL Codes for High Speed and Management
2017/09/13
Alex

## Slide 2: Outline
High Speed
  Using valid and ready
  Using sum of product
  Separating control and data path
  Fast Address Comparator
    (A+B)[m:n] == K[m:n]
Management
  Avoid duplicated codes of different configurations
  Avoid casez

## Slide 3: Using valid and ready (1)
ready
req
grant
ready
valid
req/grant
req_valid/
req_ready
200ps
100ps
210ps
410ps
100ps
200ps
300ps
+200ps
+200ps

## Slide 4: Using valid and ready (2)
req/grant
  Has longer path, because grant should be qualified with req
  NOT recommended in new design
valid/ready
  ready should NOT be qualified with valid
  valid should NOT be qualified with ready

## Slide 5: Using sum of product
assign ex_src1 = ex_reg_src1
| ({XLEN{ex_src1_bypass[0]}} & wb_wdata)
| ({XLEN{ex_src1_bypass[1]}} & mm_wdata)
| ({XLEN{ex_src1_bypass[2]}} & lsu_ipipe_wb_bypass_data)
;
assign fetch_pc = ({VALEN{retire_ptr[0]}} & fq0_pc)
| ({VALEN{retire_ptr[1]}} & fq1_pc)
| ({VALEN{retire_ptr[2]}} & fq2_pc)
;
Using sum of product when control signals are one-hot
Changing control signals to one-hot and using sum of product
assign ex_src1 = ex_src1_bypass[0] ? wb_wdata :
ex_src1_bypass[1] ? mm_wdata :
ex_src1_bypass[2] ? lsu_ipipe_wb_bypass_data :
ex_reg_src1;
assign fetch_pc = (retire_ptr==2’d0) ? fq0_pc :
(retire_ptr==2’d1) ? fq1_pc :
fq2_pc ;
Priority
Encoder
Sun of
Product

## Slide 6: Separating Control and Data Path (1)
Control
Data Path
clk
Control
Separated
Contro/Data Path
Not Separated
500ps
500ps
500ps
Data Path 1
(+300ps)
800ps
Data Path 2
(+300ps)

## Slide 7: Separating Control and Data Path (2)
Typically,
  Data path has more fan-outs
  Control signal has worse timing
When control signal is propagated to data path, synthesizer need to optimize more paths.
always @(posedge core_clk) begin
if (reg0_en) // reg0_en is control signal
reg0 <= reg0_nx; // reg0_nx is data path
end
assign reg0_en = (state == PRE )
| (state == EXE )
| (state == POST)
| (mdu_req_valid & mdu_req_ready)
;
assign reg0_nx = ({(2*XLEN+1){(state == PRE )}} & reg0_pre_nx )
| ({(2*XLEN+1){(state == EXE )}} & reg0_exe_nx )
| ({(2*XLEN+1){(state == POST)}} & reg0_post_nx)
| ({(2*XLEN+1){(state == IDLE)}} & reg0_req_nx )
;
wire mdu_req_in = mdu_req_valid & mdu_req_ready & ~mdu_kill;
assign mdu_req_ready = state == IDLE;
always @(posedge core_clk) begin
if (mdu_req_in)
reg0 <= reg0_req_nx;
else if (state == PRE)
reg0 <= reg0_pre_nx;
else if (state == EXE)
reg0 <= reg0_exe_nx;
else if (state == POST)
reg0 <= reg0_post_nx;
end

## Slide 8: Separating Control and Data Path (3)
assign rf_we = ~wb_stall & ( (wb_valid & wb_reg_rf_we & ~wb_abort) |
(mdu_resp_valid & mdu_write_enable) |
init_rf
);
assign rs1_rf_rdata = (wb_valid & wb_reg_rf_we && (wb_rd == ii_rs1)) ? rf_wdata : rf_rdata1;
assign rs2_rf_rdata = (wb_valid & wb_reg_rf_we && (wb_rd == ii_rs2)) ? rf_wdata : rf_rdata2;
Control
rf_we is real write enable signal, but the timing is worse
Data Path
wb_reg_rf_we has better timing

## Slide 9: Fast Address Comparator (A+B)[m:n] == K[m:n]
wire [VALEN-1:ILM_AMSB+1] csa_c;
wire [VALEN-1:ILM_AMSB+1] csa_s;
wire [ILM_AMSB:0] s;
wire c;
genvar i;
// carry save
for (i=ILM_AMSB+1; i<VALEN; i=i+1) begin
assign {csa_c[i], csa_s[i]} = {1'b0, ex_src1[i]} + {1'b0, ex_ag_op1[i]} + {1'b0, ~ILM_BASE[i]};
end
assign {c, s} = {1'b0, ex_src1[ILM_AMSB:0]} + {1'b0, ex_ag_op1[ILM_AMSB:0]};
assign ex_hit_ilm = ~csa_s[VALEN-1:ILM_AMSB+1] == {csa_c[VALEN-2:ILM_AMSB+1], c};
// Fast Address Compare
// Let {AH, AL} = {A[m:n], A[n-1:0]}
// Let {BH, BL} = {B[m:n], B[n-1:0]}
// Let {KH, KL} = {K[m:n], K[n-1:0]}
// Let {C, Partial Sum} = AL + BL
//
// (A+B)[m:n] == K[m:n]
// => AH + BH + C == KH
// => AH + BH - KH + C == 0
// => AH + BH + ~KH + 1 + C == 0
//
// Let {CSA_C, 1'b0} + CAS_S = AH + BH + ~KH
// => {CSA_C, 1'b0} + CSA_S + 1 + C == 0
// => {CSA_C, 1'b0} + 1 + C == -CSA_S
// => {CSA_C, 1'b0} + 1 + C == ~CSA_S + 1
// => {CSA_C, 1'b0} + C == ~CSA_S
// => {CSA_C, C} == ~CSA_S
FA
A[2]
B[2]
K[2]
CSA_C[2]
CSA_S[2]
FA
A[1]
B[1]
K[1]
CSA_C[1]
CSA_S[1]
FA
A[0]
B[0]
K[0]
CSA_C[0]
CSA_S[0]
Fast address comparator can be used for comparing ILM/DLM base, MPU/TLB entries

## Slide 10: Avoid duplicated codes of different configurations
generate
if (BTB_SIZE != 0 && RVC_SUPPORT == "yes") begin : gen_branch_control_with_isa_c
….
assign ex_btb_update_alloc = (ex_btb_alloc & (!ex_pred_hit)) & ex_taken;
assign ex_btb_update_invalidate = ((!ex_btb_alloc) & ex_pred_hit) & ex_pred_taken;
assign ex_btb_update_revise = ex_btb_alloc & ex_pred_hit & ex_pred_taken & ex_taken & (ex_ag_result != ex_pred_npc);
assign ex_btb_update_extend = ex_btb_alloc &
(ex_ag_result[VALEN-1:TARGET_ADDRESS_BIT_NUMBER+1] != ex_pc[VALEN-1:TARGET_ADDRESS_BIT_NUMBER+1]);
…
end
else if (BTB_SIZE != 0 && RVC_SUPPORT == "no") begin
assign ex_btb_update_alloc = (ex_btb_alloc & (!ex_pred_hit)) & ex_taken;
assign ex_btb_update_invalidate = ((!ex_btb_alloc) & ex_pred_hit) & ex_pred_taken;
assign ex_btb_update_revise = ex_btb_alloc & ex_pred_hit & ex_pred_taken & ex_taken & (ex_ag_result != ex_pred_npc);
assign ex_btb_update_extend = ex_btb_alloc &
(ex_ag_result[VALEN-1:TARGET_ADDRESS_BIT_NUMBER+1] != ex_pc[VALEN-1:TARGET_ADDRESS_BIT_NUMBER+1]);
end
endgenerate
Writing codes for superset
(32b & 16b) ISA is superset of 32b ISA

## Slide 11: Avoid casez
assign kill_retire_ptr_en = ( fq_ready[2:0] != 3'b111 )
& ({fq_ready[2:0], resp_valid} != 4'b1101)
& ({fq_ready[2:0], resp_valid} != 4'b1011)
& ({fq_ready[2:0], resp_valid} != 4'b0111)
& ({fq_ready[2:0], resp_valid} != 4'b0000);
assign kill_retire_ptr_nx = ({3{retire_ptr[0] & ~fq_ready[0] & resp_valid}} & 3'b010)
| ({3{retire_ptr[0] & fq_ready[0] & ~fq_ready[1] & ~resp_valid}} & 3'b010)
| ({3{retire_ptr[0] & fq_ready[0] & ~fq_ready[1] & resp_valid}} & 3'b100)
| ({3{retire_ptr[0] & fq_ready[0] & fq_ready[1] & ~fq_ready[2] & ~resp_valid}} & 3'b100)
| ({3{retire_ptr[1] & ~fq_ready[1] & resp_valid}} & 3'b100)
| ({3{retire_ptr[1] & fq_ready[1] & ~fq_ready[2] & ~resp_valid}} & 3'b100)
| ({3{retire_ptr[1] & fq_ready[1] & ~fq_ready[2] & resp_valid}} & 3'b001)
| ({3{retire_ptr[1] & fq_ready[1] & fq_ready[2] & ~fq_ready[0] & ~resp_valid}} & 3'b001)
| ({3{retire_ptr[2] & ~fq_ready[2] & resp_valid}} & 3'b001)
| ({3{retire_ptr[2] & fq_ready[2] & ~fq_ready[0] & ~resp_valid}} & 3'b001)
| ({3{retire_ptr[2] & fq_ready[2] & ~fq_ready[0] & resp_valid}} & 3'b010)
| ({3{retire_ptr[2] & fq_ready[2] & fq_ready[0] & ~fq_ready[1] & ~resp_valid}} & 3'b010);
always @* begin
casez ({retire_ptr, fq_ready, resp_valid})
7'b??1_??0_0: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b0_xxx;
7'b??1_??0_1: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b1_010;
7'b??1_?01_0: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b1_010;
7'b??1_?01_1: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b1_100;
7'b??1_011_0: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b1_100;
7'b??1_011_1: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b0_xxx;
7'b??1_111_?: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b0_xxx;
….
7'b1??_0??_0: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b0_xxx;
7'b1??_0??_1: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b1_001;
7'b1??_1?0_0: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b1_001;
7'b1??_1?0_1: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b1_010;
7'b1??_101_0: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b1_010;
7'b1??_101_1: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b0_xxx;
7'b1??_111_?: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'b0_xxx;
default: {kill_retire_ptr_en, kill_retire_ptr_nx} = 4'bx_xxx;
endcase
end
Readability
Several outputs are don’t care