## Slide 1: [Alpaca]: FPU DSU Revision
Driving Innovations™
Eric
2020/5/29

## Slide 2: DSU Pipeline Instructions
Single width instruction only
Divide instructions
  Floating-point divide
    vfdiv.vv vd, vs2, vs1, vm # vector-vector, vm: mask
    vfdiv.vf vd, vs2, rs1, vm # vector-scalar
  Reverse floating-point divide vector = scalar / vector
    vfrdiv.vf vd, vs2, rs1, vm # scalar-vector, vd[i] = f[rs1]/vs2[i]
Square root instruction
  Floating-point square root
    vfsqrt.v vd, vs2, vm # vector-vector square root

## Slide 3: Previous Design
Fast migrated from tightly coupled N25 FPU
F1 stage is dedicated for subnormal to normal conversion
Divide/Square-root operands are unpacked at F2
SRT iterations loops at F3 stage
  At Sticky Generation state, remainder from Carry-Save Adder are added for result selection at next cycle
  At Done state, the result is chosen (Q-1 if remainder is negative, else Q) and is right shift if result is subnormal
Rounding is done at F4 stage
  Using Y0/Y1/z algorithm (z: LSB 4-bit add with round bit)

## Slide 4: Previous Design (DIV Pipeline)
div_op1
div_op2
VF1
op1
op2
V2
Subnormal normalization
Subnormal detection
Subnormal normalization
Subnormal detection
div_op2
div_op1
result1
result0
op2
op1
VF1
VF2
V2
Vector
Register
file
VF3
Divider
Subnormal detection & normalization
FSM

## Slide 5: Previous Design (DIV Pipeline)
quotient1
quotient0
remainder1
quotient_sel
exp
remainder0
result
rounding mode
VF3
VF4
Result+1
Round Decision
special value
detection
VF2
Subnormal Shifter
>>
adder & stick Gen.
Round & Stick
Special Value Detection

## Slide 6: Detail Rounding Scheme of Previous DSU
Result
St1
Sum
ovf
inc
rounding mode
sign
St1
VF3
VF4
Right Shifter
MSBs Dual-adder
LSB
Carry and stick Calc.
4-bit low part adder
Round Decision
5-bit adder
5-bit adder
LSB Correction & special value detection
VF2
Subnorm?
1

## Slide 7: Improvement Opportunity
Only one div/sqrt will be executed in DSU pipe
  Four stages (3 groups of staging flop) are used
    Use one group of staging flops to flop instruction at F2 stage
Special input values are detected at F2 stage
  F1 stage is dedicated for I/P conversion, need to pipe original inputs to F2 stage
    Detect special I/P at F1: only need to flop converted inputs
Rounding scheme Y0/Y1/Z is complicated
  Used in DP MAC, for 161-bit CSA addition (107 sticky bits)
    DSU DP result has only 58-bit (53 fraction, 1 round, 4 sticky bits)
  Two 5-bit adders and a MUX for LZA prediction error
    No LZA is needed for DSU result generation

## Slide 8: Revision Items
One group of staging flop for 4 calculation state
Move special value detection from F2 to F1
Simplify rounding scheme to a simple 54-bit adder
Support Double Precision FPU divide/square root
  Add DP subnormal I/P to normal RTL

## Slide 9: DSU uArch
Operand 1 Subnormal Input Normalization
Operand 2 Subnormal Input Normalization
F2 state
DSU
Radix-4
SRT
F3 state
Sticky Gen/
Subnormal
Right shift
F4 state
Result
Rounding
F3 state
Exception/ Subnormal
Prediction
F4 state
Exception
Detection
F4 state
Normal
Result Generation
F4 state
Special Value
Generation
Reg
Reg
FP1
FP2
Special Value Detection
Exponent Calculation
Calculation state (SP:13 DP:27 cycles)
Sticky Gen state (CS form remainder)
Done state (Result, Result-1)

## Slide 10: Subnormal Input Normalization
Subnormal
Detection
Leading Zero Counter
Normalization Barrel
Shifter
msb
lsb
…
operand
Normalized fraction
msb
lsb
…
Exponent
Adjustment
Normalized exponent

## Slide 11: Rounding
DS result MSBs
54-bit round adder (DP)
Round digit gen
Remainder sticky
rounding_mode
Round result
DS result LSBs

## Slide 12
Thank You!