## Slide 1: FP DIV/SQRT uArch
202101
Larry

## Slide 2: Agenda
List of abbreviation
Overview
Configuration
uArch Overview
FP DIV/SQRT Instructions
FP Estimation Instructions
Round digit generation
Underflow Flag Detection
Enhancements
Merge IDIV and FDIV methods
Interface
Instruction list

## Slide 3: TODO list
Redraw final datapath and clarify FFs
Add a abstract functional block/datapath
Show result and after rounding difference

## Slide 4: List of abbreviation (1/)
Abbreviation | Definition
DSU | Divider and Square Root Unit
LZD | Leading zero detection
LZC | Leading zero count

## Slide 5: List of parameter (1/)
Abbreviation | Definition
XLEN | The current width of an x register in bits (32 for RV32 or 64 for RV64)
FLEN | The current width of a f register in bits (32 for SP, 64 for DP)

## Slide 6: Overview (1/)
2-stage pipeline
Supported data types
Instruction handling
  FP DIV/SQRT instruction using radix-4 SRT algorithm
  FP estimation instruction using look-up table
Precision | Width | Sign | Expo | Mant
HP | 16 | 1 | 5 | 10
SP | 32 | 1 | 8 | 23
DP | 64 | 1 | 11 | 52

## Slide 7: Overview (2/)
Instruction latency
*DIV/SQRT instruction can not be dispatch to function unit back-to-back and the instructions reduce 1 cycle.
x is not supported
Instruction | Latency |  |  | 
 | Scalar |  | Vector | 
DIV/SQRT | HP | 13* | HP | 13*
 | SP | 20* | SP | 20*
 | DP | 34* | DP | 34*
VFRECE7 | x | x | 3 | 
VFRSQRTE7 | x | x | 3 | 

## Slide 8: Configurability
Feature | Options
XLEN | 64
FLEN* | 16/32/64
VLEN | 512/256/128
SIMD_WIDTH | 512/256/128
ELEN* | 32/64
*If RVV = 0, FLEN can be configured to 32/64
*If RVV = 1, FLEN is equivalent to ELEN

## Slide 9: uArch overview

## Slide 10: VPU stage
Frontend
Function unit

## Slide 11: Function Unit Lane Hierarchy
src_gen is for source data selection
  Select data for read port 0/ 1/ 2/ 3 or scalar register
  Describe detail according to Chevy’s latest spec or v0/v1 decode table
ELEN=32
ELEN=64

## Slide 12: FDIV uArch (1/)
The original datapath
  Generate sticky 3 times
  Reduce staging FFs
  Rounding method
  Reduce 2-level adder to 1-level

## Slide 13: FDIV uArch (2/)
The modified datapath
  Generate sticky 3  2 times
  Rounding method

## Slide 14: FDIV uArch (3/)
Div instruction datapath
  Step 1: Normalize source value
  Step 2: Compute result by DSU
  Step 3: Calculate sticky
  Step 4: Shift right for subnormal
  Step 5: Do rounding
Sqrt instruction datapath
  Step 1: normalize source value
  Step 2: Compute result by DSU
  Step 3: Calculate sticky
  Step 4: Shift right for subnormal
  Step 5: Do rounding

## Slide 15: FDIV uArch (4/)
Vector estimation instruction

## Slide 16: FDIV uArch (5/)
DSU Datapath
For 2’sc

## Slide 17: FDIV uArch (5/)
DSU Datapath
For 2’sc

## Slide 18: FP Div/SQRT Instructions

## Slide 19: FP Div/SQRT Instructions datapath
Div instruction datapath
  Step 1: Normalize source value
  Step 2: Compute result by DSU
  Step 3: Calculate sticky
  Step 4: Shift right for subnormal
  Step 5: Do rounding
Sqrt instruction datapath
  Step 1: normalize source value
  Step 2: Compute result by DSU
  Step 3: Calculate sticky
  Step 4: Shift right for subnormal
  Step 5: Do rounding

## Slide 20: FP Div/SQRT Instructions (1/)
DSU dataflow
  Unpack source data
  Normalize significand and increase exponent
  Use DSU to compute result of div/sqrt
  Generate partial sticky
  Shift right significand and generate partial sticky if exponent value is subnormal
  Generate round digit
  Do rounding
Enhancements
  Reducing look-up table
  Reduce instruction latency (1 cycle)
  Reduce sticky generation times
  Modified rounding method
  Reduce 2 level adder to 1 level
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 21: FP Div/SQRT Instructions (2/)
Algorithm
    SRT algorithm
    DIV/SQRT look-up table
Recursive equation
  Div 
    is in the range [1.0, 2)
    is normalize divisor
    is in the range [-2/3d, 2/3d)
    is in the range [1.0, 2)
    Digit set () is [-2, -1, 0, 1, 2]
  Sqrt 
    is in the range [0.25, 1)
    is in the range [, )
    is in the range [0.5, 1)
    Digit set () is [-2, -1, 0, 1, 2]
    1st round of is 1.0
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 22: FP Div/SQRT Instructions (3/)
FSM behavior
  ST_IDLE is no activity
  ST_INIT is for sqrt instruction to initialize root (1.00) and do (z-1)*4
    The counter is enabled in ST_INIT and ST_CALC states
  ST_CALC is to calculate partial quotient/root/remainder
    The counter is enabled in ST_INIT and ST_CALC states
    The counter count up from 0 to the corresponding last loop value
    The last round return partial remainder by carry save form.
  ST_DONE is to return quotient and (quotient – 1)
Precision | Last loop
HP | 7
SP | 14
DP | 28
1st round is for hidden 1 and other round are for mantissa, round bit and sticky MSB | 
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 23: FP Estimation Instructions

## Slide 24: FP Estimation Instructions (1/)
Instruction dataflow
  Unpack input data
  Normalize data, compute exponent and detect special value in parallel
  Look-up vfrece7/vfesqrte7 table and do exception detection
  Calculate result exponent
  Shift right significand value if exponent is subnormal
  Produce special value according to the corresponding exception if detected
F1 stage works
  Normalize data
  Compute exponent
  Detect special value
F2 stage works
  Look-up vfrece7/vfesqrte7 table
  Do exception detection
  Shift right significand value if exponent is subnormal
  Produce special value according to the corresponding exception if detected
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 25: FP Estimation Instructions (2/)
Produce special value, exception flag according to the corresponding table in vector-spec
vfrsqrte7.v
vfrece7.v
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 26: Round digit generation & Twice Rounding Detection

## Slide 27: Round digit generation (1/)
Generate rounding carry according to rounding modes
Rounding modes
  RNE (Round to Nearest, ties to Even)
    Rounding carry is 1 if the value is greater than tie
    The value is round to even if the value is tie
  RTZ (Round Towards Zero)
    Truncate
  RDN (Round DowN)
    Truncate if the value is positive
    Rounding carry is 1 if the value is negative
  RUP (Round UP)
    Rounding carry is 1 if the value is positive
    Truncate if the value is negative
  RMM (Round to nearest, ties to Max Magnitude)
    Rounding carry is 1 if the value is greater than and equal tie
  ROD (Round towards ODd)
    Rounding carry is 1 if LSB is 0

## Slide 28: Round digit generation (2/)
1. Do rounding only
  A + increment (1 bit) (A has not round bit)
Abbreviation
  L is LSB/ R is round bit / S is sticky bit / Tie is (R & ~S)
Rounding mode | Rounding inc
RNE (Round to Nearest, ties to Even) | R & (L ¦ S)
RTZ (Round Towards Zero) | 0
RDN (Round DowN) | ~sign & (R ¦ S)
RUP (Round UP) | sign & (R ¦ S)
RMM (Round to nearest, ties to Max Magnitude) | R
ROD (Round towards ODd) | ~L

## Slide 29: Underflow Flag Detection

## Slide 30: Underflow Flag Detection – Special Case (1/)
Tininess is detected after rounding.
The exponent range are unbounded and the significand is not bounded to the corresponding format and keep normal format.
The above unbounded value is in subnormal range when exponent is unbounded. The bounded value will round to min normal value and it is not in subnormal range and underflow flag is not asserted because of rounding to min normal value. Thus, this special case should be detected.
 | Significand (HP) | Exponent
Unbounded | 01.1111_1111_11xxx | -15
bounded | 00.1111_1111_111xx | -14

## Slide 31: Underflow Flag Detection – Special Case (2/)
The Fig. show result format, L, R, S, Sm and St field.
The bit pattern is all-one mantissa and the next slide show underflow special case detection.
RM | Underflow special case
RNE | BP & R & ~Sm
RTZ | 0
RDN | BP & sign & (R^S)
RUP | BP & ~sign & (R^S)
RMM | BP & R & ~Sm
ROD | 0

## Slide 32: Underflow Flag Detection – Normal Case (4/)
The underflow just qualify bit pattern, rounding carry (round digit) and other signals.
The bit pattern is the same with the special case

## Slide 33: Enhancements

## Slide 34: Enhancements (1/)
Reduce 2-level adder
  Produce Exp and Exp – 1 (without bias)
  ExpA and ExpB have bias
  Method 1: Generate (Exp) first then calcule (Exp – 1)
  Method 2: Generate (Exp – 1) first then calcule (Exp)
  Method 3: Generate (Exp) and (Exp – 1) in parallel
 | HP | SP | DP
Bias | b0_0000_0000_1111 | b0_0000_0111_1111 | b0_0011_1111_1111
~Bias - 1 | b1_1111_1110_1111 | b1_1111_0111_1111 | b1_1011_1111_1111
Instruction | Exp | Exp - 1
DIV | ExpA – ExpB | ExpA + ~ExpB
SQRT | (ExpA – Bias) >> 1 | (ExpA + (~Bias – 1)) >> 1
Notes: Method 3: Generate (Exp) and (Exp – 1) in parallel
DIV Exp = ExpA – ExpB
DIV Exp – 1 = ExpA – ExpB – 1 = ExpA + (~ExpB + 1) – 1 = ExpA + ~ExpB
SQRT Exp = (ExpA – Bias) >> 1
SQRT Exp – 1 = (ExpA – Bias) >> 1 – 1 = (ExpA – Bias - 2) >> 1 = (ExpA + (~Bias – 1)) >> 1
Bias = 15
15 => b0_0000_0000_1111
~15 => b1_1111_1111_0000
~15-1 => b1_1111_1110_1111
Bias = 127
127 => b0_0000_0111_1111
~127 => b1_1111_1000_0000
~127-1 => b1_1111_0111_1111
Bias = 1023
1023 => b0_0011_1111_1111
~1023 => b1_1100_0000_0000
~1023-1 => b1_1011_1111_1111

## Slide 35: Enhancements (2/)
Compare 3 methods
The following reports are VFDIV64 PPA under different method and Freq.
Methods | Result | DIV | SQRT | EXP | EXP - 1
Exp first (origin) | Exp | ExpA – ExpB | (ExpA – Bias)>>1 |  | 
 | Exp – 1 |  |  |  | Exp - 1
Exp_m1 first | Exp |  |  | (Exp – 1) + 1 | 
 | Exp – 1 | ExpA + ~ExpB | (ExpA – (Bias+2)) >> 1 |  | 
Parallel | Exp | ExpA - ExpB | (ExpA – Bias)>>1 |  | 
 | Exp – 1 | ExpA + ~ExpB | (ExpA + (~Bias-1)) >> 1 |  | 
Methods | FLEN | Lib | Freq. | Area | Note
Exp first (original) | 64 | 28HPC+ | 1.00GHz | 27.47kgates | 
Exp_m1 first | 64 | 28HPC+ | 1.00GHz | 27.69kgates | 
Parallel | 64 | 28HPC+ | 1.00GHz | 27.52kgates | Arithmetic right shift for SQRT
Exp first (original) | 64 | 28HPC+ | 1.25GHz | 31.24kgates | 
Parallel | 64 | 28HPC+ | 1.25GHz | 30.39kgates | Arithmetic right shift for SQRT
Notes: Bias = 15
15 => b0_0000_0000_1111
~15 => b1_1111_1111_0000
~15-1 => b1_1111_1110_1111
Bias = 127
127 => b0_0000_0111_1111
~127 => b1_1111_1000_0000
~127-1 => b1_1111_0111_1111
Bias = 1023
1023 => b0_0011_1111_1111
~1023 => b1_1100_0000_0000
~1023-1 => b1_1011_1111_1111

## Slide 36: Merge IDIV and FDIV methods

## Slide 37: Merge IDIV and FDIV methods (1/)
Two methods to merge/fuse IDIV and FDIV function units.
  Merge two function units
    Reuse staging FFs and return result according to instruction type
  Fuse two function units
    Support 64-bit data in and widen related logics
    Do 2’sc for input and output if negative
    Support 8 bit div
    Reuse radix-4 SRT look-up table
    Extend quotient handling logics
    Add Left shifting logic to handle integer result
    Hard to implement remainder instruction using SRT
Merge 2 function units
Fuse 2 function units

## Slide 38: Merge IDIV and FDIV methods (2/)
Why hard to implement remainder instruction
  Apply radix-4 algorithm so 2-bit partial quotient is generated in each iteration
  The extra fraction bit should recover to partial remainder
  Remainder (Integer) = Remainder (fraction) x divisor
    Method 1: 10/3 = 3.333…  3 * 0.333… = 1
    Method 2: 10/3 = 3.333…  10 - 3 * 3 = 1
Conclusion
  Keep the current design
Integer | iteration | Extra fraction bit
INT8 | 1+4 | 1 bits
INT16 | 1+8 | 1 bits
INT32 | 1+16 | 1 bits
INT64 | 1+32 | 1 bits
1 is for hidden one

## Slide 39: Interface

## Slide 40: VPU Hierarchy

## Slide 41: Lane Interface (1/)
Module name is vc_lane_vfmis.v
Hierarchy diagram

## Slide 42: Lane Interface (2/)
Block connection diagram

## Slide 43: Lane Interface (3/)
Signal name | Type | Description
core_clk | Input | Clock
core_reset_n | Input | Negative Edge Reset
lane_id | Input | Lane ID and it indicate lane0 for scalar floating-point logics
vfdiv_vtype_sew | Input | Apply vsew to execute instruction
vfdiv_csr_ediv | Input | Apply vediv to execute instruction
vfdiv_vtype_lmul | Input | Apply vlmul to execute instruction
vfdiv_rmode | Input | Apply frm to execute instruction
vfdiv_valid | Input | Instruction valid signal
vfmis_uop_cnt | Input | Micro-op counter start from 0
vfdiv_uop_first | Input | Indicate the 1st micro-op
vfdiv_msk_bits | Input | The source data valid signal
vfdiv_ex_ctrl | Input | Instruction encoding and please see Instruction encoding slide
vfdiv_op_wide | Input | Indicate 2x width destination or source
vfdiv_sign | Input | Indicate sign data (XRF)

## Slide 44: Lane Interface (4/)
Signal name | Type | Description
vrf_data[0/1/2/3]_in | Input | The data is from VRF read port 0/1/2/3
frf_data[0/1/2]_out | Input | The data is from FRF read port 0/1/2/3
fdiv_scalar_valid | Input | Indicate that the scalar data is valid
vfdiv_[vs1/vs2/vs3]_valid | Input | The corresponding source data is valid
vfdiv_[vs1/vs2/vs3]_select | Input | The corresponding source is from read port
vfdiv_[rs1/rs2]_valid | Input | The corresponding source data is valid
vfdiv_rs_data | Input | Indicate the scalar source data of vector instruction
vfdiv_data | Output | Result VRF data
vfdiv_mask | Output | Result byte-write enable
vfdiv_vfcsr_flag_set | Output | Result exception flag

## Slide 45: Pipe Interface (1/)
Module name is vc_vfp_fdiv.v
Supported FLENs are 16/32/64 and XLEN is the same with FLEN
Hierarchy diagram

## Slide 46: Pipe Interface (2/)
Signal name | Type | Description
core_clk | Input | Clock
core_reset_n | Input | Negative Edge Reset
f1_valid | Input | Valid signal
f1_ex_ctrl | Input | Control signal for encoding. More info in instruction encoding slide.
f1_sew | Input | Indicate element width
f1_ediv | Input | Un-used
f1_round_mode | Input | Round mode
f1_op1_data | Input | Source oprand1
f1_op2_data | Input | Source oprand2

## Slide 47: Pipe Interface (3/)
Signal name | Type | Description
f4_result_type | Output | Result data type 3’b111  DP 3’b110  SP 3’b101  HP 3’b100  Bfloat16 3’b011  Double-word 3’b010  Word 3’b001  Half-word 3’b000  Byte
f4_wdata_en | Output | Write enable for F1 retired instruction (Instruction latency is 1)
f4_wdata | Output | Result data for F1 retired instruction (Instruction latency is 1)
f4_flag_set | Output | Result exception flag

## Slide 48: Instruction list

## Slide 49: Instruction list
The fdiv function unit encoding

## Slide 50: Backup

## Slide 51: Radix-2 Algorithm (1/)
Radix-2 have
  Restoring algorithm
  Non-restoring algorithm
  SRT algorithm (also non-restoring algorithm)

## Slide 52: Radix-2 Algorithm (2/)
Restoring algorithm
  Quotient digit set is {0, 1}

## Slide 53: Radix-2 Algorithm (3/)
Non-restoring algorithm
  Quotient digit set is {-1, 0, 1}

## Slide 54: Radix-2 divider using SRT (1/)
SRT named for its creators (Sweeney, Robertson, and Tocher) and it is non-restoring algorithm
Generate 1-bit partial remainder in 1 iteration
Quotient

## Slide 55: Radix-2 divider using SRT (2/)
Shifted partial remainder is in the range [-d, d)
Digit set
  -1  subtract -d
  0  subtract 0
  1  subtract d

## Slide 56: Radix-2 divider using SRT & CSA(1/)
Shifted partial remainder () is in the range [-2d, 2d)
Digit set
  -1  [-2d, -1/2)
  0  [-1/2, 0)
  1  [0, 2d)

## Slide 57: Radix-2 divider using SRT & CSA(2/)
Let and
Add the most significant 4 bits of u and v, t result may have 1 bit error (’b0.01 = 0.25) because of carry from low part. The threshold gap is greater than 0.25.
XXXX XXXX
XXXX XXXX
X
carry

## Slide 58: Radix-2 divider using SRT & CSA(3/)
The following Fig. is radix-2 divider datapath
Use sum of partial carry and sum string to select
BACK

## Slide 59: Radix-4 divider using SRT (1/)
SRT named for its creators (Sweeney, Robertson, and Tocher) and it is non-restoring algorithm
Generate 2-bit partial remainder in 1 iteration
Shifted partial remainder () is in the range [-4d, 4d)
Digit set

## Slide 60: Radix-4 divider using SRT (2/)
p is shifted partial remainder and d is divisor
(3 * divisor) is complex so we want to restrict the quotient digits to [−2, 2] from [-3, 3].

## Slide 61: Radix-4 divider using SRT (3/)
Restrict the quotient digits to [−2, 2] from [-3, 3]
  is in the range [-hd, hd)
  is in the range [-4hd, 4hd)
  We should be able to bring the worst-case values to within [-hd, hd) by adding ±2d to it
   

## Slide 62: Radix-4 divider using SRT (4/)
quotient digits to [−2, -1, 0, 1, 2] from [-3, -2, -1, 0, 1, 2, 3]
  is in the range [-d, d)
quotient digits is [−2, -1, 0, 1, 2]
  is in the range [-2/3d, 2/3d)

## Slide 63: Radix-4 SRT - Quotient Handling (1/)
Generate 2-bit partial quotient in each iteration and the corresponding value is {-2, -1, 0, 1, 2}. The final quotient like as 1. 1 -2 1 -1 1 2 (sign digit) but it can not use directly and the correct result is 1.020312 (radix-4).
The following will describe how to handle negative partial quotient.
  In each iteration, we should keep (partial quotient, ) and (partial quotient -1, )
  The next round can select (partial quotient -1) if the partial quotient is negative.
Example:
BACK
 |  |  | select |  | 
 |  | -2() |  |  | 
 |  | 0() |  |  | 
 |  | 1() |  |  | 
 |  |  | select |  | 

## Slide 64: Radix-2 SQRT - Example
The example is non-restoring algorithm

## Slide 65: Radix-4 DIV and SQRT
DIV
  is in the range [-2/3d, 2/3d)
  Digit set () is [-2, -1, 0, 1, 2]
  is in the range [1.0, 2)
  is dividend
  dividend is in the range [1.0, 2)
SQRT
  is in the range [-2/3, 2/3) [-4/3, 4/3)
  Digit set () is [-2, -1, 0, 1, 2]
    Digit set adjustment is for reducing look-up table
  is in the range [0.5, 1)
  is ((radicand >> 1) – 1)
  radicand is in the range [0.25, 1)
2 | 3’b010 | 
1 | 3’b001 | 
0 | 3’b000 | 
-1 | 3’b111 | 
-2 | 3’b110 | 
2 | 3’b010 | 
1 | 3’b001 | 
0 | 3’b000 | 
-1 | 3’b111 | 
-2 | 3’b110 | 

## Slide 66: Radix-4 SRT Look-up Table (1/)
The Fig is DIV SRT look-up table.
Quotient of DIV is in [1, 2)
BACK
The Fig is SQRT SRT look-up table.
Quotient of SQRT is in [0.5, 1)

## Slide 67: How to subtract 1/adjust data for SQRT (1/)
  The significand do *2 if exponent is odd and the radicand is in the range [0.25, 1)
  The following value is in the range [0.5, 2) and the value(din0) is 2x radicand
Notes: The sqrt result of each values
0.9375 => 0.9682458365518542212948163499456 0.1111
0.875 => 0.93541434669348534639593718307914 0.1110
0.8125 => 0.90138781886599732327980531686762 0.1110
0.75 => 0.86602540378443864676372317075294 0.1101
0.6875 => 0.82915619758884996227873318416767 0.1101
0.625 => 0.79056941504209483299972338610818 0.1100
0.5625 => 0.75 0.1100
0.5 => 0.70710678118654752440084436210485 0.1011

## Slide 68: How to subtract 1/adjust data for SQRT (2/)
  For SQRT initialization, (Z-1)
  Shift left and 1 extension for SQRT instruction
    4((radicand >> 1) – 1)  2radicand - 4
DS_DIN | Shift left 1 bit | 1 extension
0001.1111 | 0011.111 (3.875) | 1111.111 (-0.125)
0001.1110 | 0011.110 (3.75) | 1111.110 (-0.25)
0001.1101 | 0011.101 (3.625) | 1111.101 (-0.375)
0001.1100 | 0011.100 (3.5) | 1111.100 (-0.5)
0001.1011 | 0011.011 (3.375) | 1111.011 (-0.625)
0001.1010 | 0011.010 (3.25) | 1111.010 (-0.75)
0001.1001 | 0011.001 (3.125) | 1111.001 (-0.875)
0001.1000 | 0011.000 (3) | 1111.000 (-1)
DS_DIN | Shift left 1 bit | 1 extension
0000.1111 | 0001.111 (1.875) | 1101.111 (-2.125)
0000.1110 | 0001.110 (1.75) | 1101.110 (-2.25)
0000.1101 | 0001.101 (1.625) | 1101.101 (-2.375)
0000.1100 | 0001.100 (1.5) | 1101.100 (-2.5)
0000.1011 | 0001.011 (1.375) | 1101.011 (-2.625)
0000.1010 | 0001.010 (1.25) | 1101.010 (-2.75)
0000.1001 | 0001.001 (1.125) | 1101.001 (-2.875)
0000.1000 | 0001.000 (1) | 1101.000 (-3)
Notes: The sqrt result of each values
0.9375 => 0.9682458365518542212948163499456 0.1111
0.875 => 0.93541434669348534639593718307914 0.1110
0.8125 => 0.90138781886599732327980531686762 0.1110
0.75 => 0.86602540378443864676372317075294 0.1101
0.6875 => 0.82915619758884996227873318416767 0.1101
0.625 => 0.79056941504209483299972338610818 0.1100
0.5625 => 0.75 0.1100
0.5 => 0.70710678118654752440084436210485 0.1011

## Slide 69: 1st Round Root selection for SQRT (1/)
Root digit selection rule cannot be used for all iterations because root is unknown in early iterations. SQRT instruction will use high-order root (0.1xxx) to generate 2-bit root in each iteration.
To find the 1st round root value and the steps like as below diagram
1.0000
(Z-1) * 4
Lookup table
1.0000
0.1100
0.1000
-2/-1/0
+
-2
-1
0
0.1110
0.1101
0.1100
0.1011
0.1010
-1
-2
-0
1
2
Initial value
Lookup table
-2/-1/0/1/2
+
2nd partial remainder
3rd partial remainder
The corresponding 2nd round root is illegal if partial remainder is unbounded
1st round root
The corresponding 3rd round root is illegal if partial remainder is unbounded
The corresponding root is illegal if unbounded
‘b100
2nd round root
3rd round root
1st partial remainder
<<2
Notes: The sqrt result of each values
0.9375 => 0.9682458365518542212948163499456 0.1111
0.875 => 0.93541434669348534639593718307914 0.1110
0.8125 => 0.90138781886599732327980531686762 0.1110
0.75 => 0.86602540378443864676372317075294 0.1101
0.6875 => 0.82915619758884996227873318416767 0.1101
0.625 => 0.79056941504209483299972338610818 0.1100
0.5625 => 0.75 0.1100
0.5 => 0.70710678118654752440084436210485 0.1011
0.4375 => 0.66143782776614764762540393840982 0.1010
0.375 => 0.61237243569579452454932101867647 0.1001
0.3125 => 0.55901699437494742410229341718282 0.1000
0.25 => 0.5 0.1000

## Slide 70: 1st Round Root selection for SQRT (2/)
The Fig. show value according to digit set and the corresponding bounded value are (1 * 4/3) , (0.75 * 4/3) and (0.5 * 4/3)
  0 1.00
  -10.11
  -20.10
Root is 1.00
Root is 0.11
Root is 0.10
Notes: The sqrt result of each values
0.9375 => 0.9682458365518542212948163499456 0.1111
0.875 => 0.93541434669348534639593718307914 0.1110
0.8125 => 0.90138781886599732327980531686762 0.1110
0.75 => 0.86602540378443864676372317075294 0.1101
0.6875 => 0.82915619758884996227873318416767 0.1101
0.625 => 0.79056941504209483299972338610818 0.1100
0.5625 => 0.75 0.1100
0.5 => 0.70710678118654752440084436210485 0.1011
0.4375 => 0.66143782776614764762540393840982 0.1010
0.375 => 0.61237243569579452454932101867647 0.1001
0.3125 => 0.55901699437494742410229341718282 0.1000
0.25 => 0.5 0.1000

## Slide 71: 1st Round Root selection for SQRT (3/)
The first round pick up the corresponding root value we can calculate the corresponding partial remainder according to input value.
Several root will produce unbounded partial remainder like as white field.
The three green color will produce 3 roots (1.00, 0.11 and 0.10) in 1st iteration then the next round use it to calculate new partial remainder.
Then All values in red rectangle are 4x and then check the 2nd round will not produce unbounded value or illegal root.
Root is 1.00
Root is 0.11
Root is 0.10

## Slide 72: 1st Round Root selection for SQRT (4/)
The second iteration use previous 3 roots (1.00, 0.11 and 0.10) to select partial root and calculate partial remainder.
Partial root selection
  Partial Root 1.00 will select -2, -1, 0 partial root because partial remainders are in range [-4, -0.5].
  Partial Root 0.11 will select -2, -1, 0, 1, 2 partial root because partial remainder are in range [-3.5, 2.5].
  Partial Root 0.10 will select -2, -1, 0, 1, 2 partial root because partial remainder are in [-2, 2.5]
We can find 2nd round partial root according to right Figs and calculate the 2nd round partial remainder.
Partial Root 0.10
Partial Root 0.11
Partial Root 1.00

## Slide 73: 1st Round Root selection for SQRT (5/)
The right Fig. is produced according to partial root selection table and the corresponding 1st round partial root.
The root is in range [0.5, 1] so 0.0111 and 0.0110 are illegal. Thus, 0.1010 and 0.1011 cannot be applied as 1st round root.

## Slide 74: 1st Round Root selection for SQRT (6/)
Check the partial remainders are bounded [-2r/3, 2r/3)
According to 2nd partial remainder table, all partial remainder values are in the corresponding boundary. Thus, we can apply 0.1100 and 0.1101 as 1st round root.
The current design apply 0.1101 as 1st round root.
Notes: The sqrt result of each values
0.9375 => 0.9682458365518542212948163499456 0.1111
0.875 => 0.93541434669348534639593718307914 0.1110
0.8125 => 0.90138781886599732327980531686762 0.1110
0.75 => 0.86602540378443864676372317075294 0.1101
0.6875 => 0.82915619758884996227873318416767 0.1101
0.625 => 0.79056941504209483299972338610818 0.1100
0.5625 => 0.75 0.1100
0.5 => 0.70710678118654752440084436210485 0.1011
0.4375 => 0.66143782776614764762540393840982 0.1010
0.375 => 0.61237243569579452454932101867647 0.1001
0.3125 => 0.55901699437494742410229341718282 0.1000
0.25 => 0.5 0.1000

## Slide 75: Merge DIV and SQRT Look-up Table (1/)
Merge 2 look-up tables to reduce area.
The red rectangles are different with SQRT look-up table.
The sum of high-order partial remainder may be actually sum or sum without carry.
Check that red rectangles are replaceable
DIV Look-up table
SQRT Look-up table
+1
Sum with carry=0
Sum with carry=1

## Slide 76: Merge DIV and SQRT Look-up Table (2/)
+2
+1/+2
+1

## Slide 77: Merge DIV and SQRT Look-up Table (3/)
+1
+0/+1
+0

## Slide 78: Merge DIV and SQRT Look-up Table (4/)
+0
+0/-1
-1

## Slide 79: Merge DIV and SQRT Look-up Table (5/)
-1
-1/-2
-2

## Slide 80: Merge DIV and SQRT Look-up Table (6/)
Merge div & sqrt look-up
  Merge the look-up tables (use only one table and it is original SQRT look-up table)
VFDIV64
Lib | Feq. | FLEN | Original | Modified | 
28HPC+ | 1.00Ghz | 32 | 21.3kgates | 21.2kgates | 0.5%
28HPC+ | 1.25Ghz | 32 | 22.7kgates | 22.5kgates | 0.9%
28HPC+ | 1.00Ghz | 64 | 27.5kgates | 27.3kgates | 0.7%
28HPC+ | 1.25Ghz | 64 | 31.2kgates | 30.1kgates | 3.6%
DIV Look-up table
SQRT Look-up table

## Slide 81: Round digit generation (1/)
Generate rounding increment according to rounding modes
Rounding modes
  RNE (Round to Nearest, ties to Even)
  RTZ (Round Towards Zero)
  RDN (Round DowN)
  RUP (Round UP)
  RMM (Round to nearest, ties to Max Magnitude)
  ROD (Round towards ODd)
Sign | L | R | S |  | RNE | RTZ | RDN | RUP | RMM | ROD
0 | 0 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +1
0 | 0 | 0 | 1 |  | +0 | +0 | +0 | +1 | +0 | +1
0 | 0 | 1 | 0 |  | +0 | +0 | +0 | +1 | +1 | +1
0 | 0 | 1 | 1 |  | +1 | +0 | +0 | +1 | +1 | +1
0 | 1 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +0
0 | 1 | 0 | 1 |  | +0 | +0 | +0 | +1 | +0 | +0
0 | 1 | 1 | 0 |  | +1 | +0 | +0 | +1 | +1 | +0
0 | 1 | 1 | 1 |  | +1 | +0 | +0 | +1 | +1 | +0
1 | 0 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +1
1 | 0 | 0 | 1 |  | +0 | +0 | +1 | +0 | +0 | +1
1 | 0 | 1 | 0 |  | +0 | +0 | +1 | +0 | +1 | +1
1 | 0 | 1 | 1 |  | +1 | +0 | +1 | +0 | +1 | +1
1 | 1 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +0
1 | 1 | 0 | 1 |  | +0 | +0 | +1 | +0 | +0 | +0
1 | 1 | 1 | 0 |  | +1 | +0 | +1 | +0 | +1 | +0
1 | 1 | 1 | 1 |  | +1 | +0 | +1 | +0 | +1 | +0

## Slide 82: Underflow Flag Detection – Special Case (1/)
Format
The table show all cases of asserting underflow under twice rounding case.
  Left V  subnormal to normal
  Right V  Assert underflow flag
  Assert special underflow flag if the condition have 2V.
  R: round bit
  Sm: MSB of sticky field
  St: other sticky field
  S = (Sm | St)
Sign | R | Sm | St |  | RNE |  | RTZ |  | RDN |  | RUP |  | RMM |  | ROD | 
0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 1 |  |  | V |  | V |  | V | V | V |  | V |  | V
0 | 0 | 1 | 0 |  |  | V |  | V |  | V | V | V |  | V |  | V
0 | 0 | 1 | 1 |  |  | V |  | V |  | V | V | V |  | V |  | V
0 | 1 | 0 | 0 |  | V | V |  | V |  | V | V | V | V | V |  | V
0 | 1 | 0 | 1 |  | V | V |  | V |  | V | V |  | V | V |  | V
0 | 1 | 1 | 0 |  | V |  |  | V |  | V | V |  | V |  |  | V
0 | 1 | 1 | 1 |  | V |  |  | V |  | V | V |  | V |  |  | V
1 | 0 | 0 | 0 |  |  |  |  |  |  |  |  |  |  |  |  | V
1 | 0 | 0 | 1 |  |  | V |  | V | V | V |  | V |  | V |  | V
1 | 0 | 1 | 0 |  |  | V |  | V | V | V |  | V |  | V |  | V
1 | 0 | 1 | 1 |  |  | V |  | V | V | V |  | V |  | V |  | V
1 | 1 | 0 | 0 |  | V | V |  | V | V | V |  | V | V | V |  | V
1 | 1 | 0 | 1 |  | V | V |  | V | V |  |  | V | V | V |  | V
1 | 1 | 1 | 0 |  | V |  |  | V | V |  |  | V | V |  |  | V
1 | 1 | 1 | 1 |  | V |  |  | V | V |  |  | V | V |  |  | V

## Slide 83: Underflow Flag Detection – Special Case (2/)
The condition should qualify bit pattern (BP) and the following condition under different rounding mode
BP | Sign | R | Sm | St |  | RNE | RTZ | RDN | RUP | RMM | ROD
Match | 0 | 0 | 0 | 0 |  |  |  |  |  |  | 
Match | 0 | 0 | 0 | 1 |  |  |  |  | A |  | 
Match | 0 | 0 | 1 | 0 |  |  |  |  | A |  | 
Match | 0 | 0 | 1 | 1 |  |  |  |  | A |  | 
Match | 0 | 1 | 0 | 0 |  | A |  |  | A | A | 
Match | 0 | 1 | 0 | 1 |  | A |  |  |  | A | 
Match | 0 | 1 | 1 | 0 |  |  |  |  |  |  | 
Match | 0 | 1 | 1 | 1 |  |  |  |  |  |  | 
Match | 1 | 0 | 0 | 0 |  |  |  |  |  |  | 
Match | 1 | 0 | 0 | 1 |  |  |  | A |  |  | 
Match | 1 | 0 | 1 | 0 |  |  |  | A |  |  | 
Match | 1 | 0 | 1 | 1 |  |  |  | A |  |  | 
Match | 1 | 1 | 0 | 0 |  | A |  | A |  | A | 
Match | 1 | 1 | 0 | 1 |  | A |  |  |  | A | 
Match | 1 | 1 | 1 | 0 |  |  |  |  |  |  | 
Match | 1 | 1 | 1 | 1 |  |  |  |  |  |  | 
RM | Underflow
RNE | BP & R & ~Sm
RTZ | 0
RDN | BP & sign & (R^S)
RUP | BP & ~sign & (R^S)
RMM | BP & R & ~Sm
ROD | 0

## Slide 84: VFDIV64 PPA (1/)
The following RTL SHA-1 are
  Original: master branch 30d18f15f
  V1: master branch c261b5975
  V2: master branch 5c4668b24
  V3: master branch 01cd85b79
Synthesis tool: DC v2019.03-sp3
Tech_lib: tcbn28hpcplusbwp30p140ssg0p81vm40c
The following reports has output delay
  Flag output delay is 50ps, outputs in F1 are 100ps and outputs in F2 are 200ps, and then FMIS F2 stage just have 340ps@1.25GHz and 500ps@1.00GHz
Feq. | XLEN/FLEN | Original (Kgates/ ps) | V1 (Kgates/ ps/ %) | V2 (Kgates/ ps/ %) | V3 (Kgates/ ps/ %)
1.00GHz | 64/32 | 21.59 / MET | 20.53 / MET / -4.91 | 20.29 / MET / -6.02 | 20.19 / MET / -6.48
 | 64/64 | 27.77 / MET | 26.20 / MET / -5.65 | 25.80 / MET / -7.09 | 25.65 / MET / -7.63
1.25GHz | 64/32 | 24.89 / MET | 22.61 / MET / -9.16 | 22.79 / MET / -8.44 | 22.52 / MET / -9.52
 | 64/64 | 33.32 / MET | 29.37 / MET / -11.85 | 29.37 / MET / -12.82 | 29.09 / MET / -12.70
Notes: set input_delay_ratio 0.3
set_input_delay [expr $clk_period * $input_delay_ratio] -clock CORE_CLK [all_inputs]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfdiv_data64]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfdiv_mask8]
set_output_delay [expr 0.05] -clock CORE_CLK [get_ports vfdiv_vfcsr_flag_set]

## Slide 85: VFDIV64 PPA – ORI vs V1 (2/)
Feq. | XLEN/FLEN | Module | Original | V1 | V2 | V3
1.00GHz | 64/32 | vc_vfdiv64 fdiv_pipe0 fdiv_pipe1 fdiv_pipe2 fdiv_pipe3 | 8149.4279 2459.898 1387.512 2406.6 1387.26 | 7756.0559 / -4.83% 2337.5520 / -4.97% 1293.7680 / -6.76% 2322.4320 / -3.50% 1301.2020 / -6.20% | 7664.8319 / -5.95% 2313.4860 / -5.95% 1275.4980 / -8.07% 2295.4680 / -4.62% 1277.8920 / -7.88% | 7624.6379 / -6.44% 2273.7960 / -7.57% 1284.0660 / -7.46% 2280.0960 / -5.26% 1288.9800 / -7.08%
 | 64/64 | vc_vfdiv64 fdiv_pipe0 fdiv_pipe1 fdiv_pipe2 fdiv_pipe3 | 10496.4299 4780.6919 1384.11 2417.058 1390.536 | 9901.9619 / -5.66% 4479.1740 / -6.31% 1306.2420 / -5.63% 2315.3760 / -4.21% 1290.6180 / -7.19% | 9748.3679 / -7.13% 4382.5320 / -8.33% 1279.9080 / -7.53% 2294.5860 / -5.07% 1281.9240 / -7.81% | 9694.9439 / -7.64% 4340.8260 / -9.20% 1282.8060 / -7.32% 2276.0640 / -5.83% 1283.3100 / -7.71%
1.25GHz | 64/32 | vc_vfdiv64 fdiv_pipe0 fdiv_pipe1 fdiv_pipe2 fdiv_pipe3 | 9400.6079 2889.18 1511.118 2830.842 1541.61 | 8542.4219 / -9.13% 2581.6140 / -10.65% 1405.1520 / -7.01% 2571.0300 / -9.18% 1415.4840 / -8.18% | 8613.2339 / -8.38% 2674.3500 / -7.44% 1388.3940 / -8.12% 2567.6280 / -9.30% 1396.3320 / -9.42% | 8506.7639 / -9.51% 2559.8160 / -11.40% 1411.0740 / -6.62% 2543.0580 / -10.17% 1412.4600 / -8.38%
 | 64/64 | vc_vfdiv64 fdiv_pipe0 fdiv_pipe1 fdiv_pipe2 fdiv_pipe3 | 12590.4239 6055.9379 1527.246 2780.946 1560.258 | 11098.0799 / -11.85% 5131.6020 / -15.26% 1384.6140 / -9.34% 2575.0620 / -7.40% 1401.1200 / -10.20% | 10977.7499 / -12.81% 5020.5960 / -17.10% 1377.5580 / -9.80% 2583.1260 / -7.11% 1404.5220 / -9.98% | 10993.8779 / -12.68% 5047.6860 / -16.65% 1400.4900 / -8.30% 2523.1500 / -9.27% 1414.4760 / -9.34%

## Slide 86: VFDIV64 PPA comparing (1/)
The following RTL SHA-1 are
  Original: master branch 30d18f15f
  V1: master branch c261b5975
  V2: master branch 5c4668b24
  V3: master branch 01cd85b79
FLEN | Feq. | Ori | V1 | V2 | V3
32 | 1000 (1.00ns) | 21.59 kagtes / MET | 20.53 kagtes / MET | 20.29 kagtes / MET | 20.19 kagtes / MET
32 | 1250 (0.80ns) | 24.89 kagtes / MET | 22.61 kagtes / MET | 22.79 kagtes / MET | 22.52 kagtes / MET
32 | 1333 (0.75ns) |  | 24.42 kagtes / MET | 24.65 kagtes / MET | 23.95 kgates / MET
32 | 1429 (0.70ns) |  | 27.31 kagtes / MET | 27.81 kagtes / MET | 28.27 kagtes / MET
32 | 1667 (0.60ns) |  | 32.67 kagtes / -75ps |  | 
64 | 1000 (1.00ns) | 27.77 kgates / MET | 26.20 kgates / MET | 25.80 kgates / MET | 25.65 kgates / MET
64 | 1250 (0.80ns) | 33.32 kgates / MET | 29.37 kgates / MET | 29.05 kgates / MET | 29.09 kgates / MET
64 | 1333 (0.70ns) | 36.59 kgates / -31ps | 31.88 kgates / MET | 31.46 kgates / MET | 31.29 kgates / MET
64 | 1429 (0.65ns) | 38.36 kgates / -68ps | 36.22 kgates / -30ps |  | 34.73 kgates / -14ps
64 | 1667 (0.60ns) |  | 37.63 kgates / -49ps |  |