## Slide 1: FP MISC uArch
202012
Larry

## Slide 2: Agenda
List of abbreviation/parameter
Overview
Configuration
uArch overview
Conversion Instructions
Round digit/2’sc inc generation
Comparing & Others instructions
Cross Lane Forwarding Path
Enhancements
Instruction list

## Slide 3: List of abbreviation (1/)
Abbreviation | Definition
F2I/F2F/I2F | F: Floating-point, I: integer
ABS | Alignment barrel shift
NBS | Normalization barrel shift
2’sc | 2’s complement
LZD | Leading zero detection
LZC | Leading zero count
mant_width_max | max of mantissa width of supported precisions
mant_width_min | min of mantissa width of supported precisions
dst_mant_width | Destination mantissa width
src_mant_width | Source mantissa width

## Slide 4: List of parameter (1/)
Abbreviation | Definition
XLEN | The current width of an x register in bits (32 for RV32 or 64 for RV64)
FLEN | The current width of a f register in bits (32 for SP, 64 for DP)
VLEN | Vector length
ELEN | Element width

## Slide 5: Overview (1/)
2-stage pipeline
Supported data types
  BFloat16/HP/SP/DP
  Int8/Int16/Int32/Int64
The followings are supported instructions and the corresponding latency
  Conversion (I2F, F2F, F2I)
  Comparing/min/max
  Sign injection/classify/move
Precision | Width | Sign | Expo | Mant
HP | 16 | 1 | 5 | 10
Bfloat16 | 16 | 1 | 8 | 7
SP | 32 | 1 | 8 | 23
DP | 64 | 1 | 11 | 52

## Slide 6: Overview (2/)
Instruction latency
Instruction | Latency |  | 
 | Scalar | Vector | 
Conversion | 2 | Widening | 2
 |  | Narrowing | 3
Sign injection | 2 | 2 | 
Min/max | 2 | 2 | 
Comparing | 1 | 2 | 
Classify | 1 | 2 | 
Move | 1 | 2 | 

## Slide 7: Configurability
Feature | Options
XLEN | 64
FLEN* | 16/32/64
VLEN | 512/256/128
SIMD_WIDTH | 512/256/128
ELEN* | 32/64
*FLEN can be configured to 32/64 when RVV==0
*ELEN is equivalent to FLEN when RVV==1

## Slide 8: uArch overview

## Slide 9: VPU stage
Frontend
Function unit
Main pipe

## Slide 10: Function Unit Lane Hierarchy
Src_gen is for source data selection
FSM is for reduction instructions to generate control signals
Lane_carry_control handle data forwarding between each lane
ELEN=32
ELEN=64

## Slide 11: FMIS uArch (1/)

## Slide 12: FMIS uArch (2/)
INT to FP

## Slide 13: FMIS uArch (3/)
FP to INT (exp < 52)
FP to INT (52 <= exp)

## Slide 14: FMIS uArch (4/)
FP narrowing to widening
FP widening to narrowing

## Slide 15: FMIS uArch (5/)
Comparing instructions
Others instructions

## Slide 16: Conversion instructions

## Slide 17: Integer to FP Datapath
Conversion datapath
  INT to FP

## Slide 18: Integer to FP (1/)
Integer to floating-point dataflow
  2’sc for negative integer
  All integer source types are aligned at XLEN-bit
  Do 3 things in parallel
    Count leading zero
    Normalize aligned data
    Generate sticky bit
  Pack to significand format according destination precision
  Do rounding
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 19: Integer to FP (2/)
Normalization
  Calculate leading zero number
    rd_exp = type_expo – LZC
  Apply structuralized or network to calculate LZC
  Apply barrel shift to normalize source data
  Apply structuralized or network to generate sticky bit
  The above shifter and or network can work in parallel and reduce latency
Rounding
  According to round mode and sticky, add 1 on LSB or on Round bit
  Increase exponent by 1 and set mantissa to zero if carry bit is set
Source type | Type_expo
DWORD | 63
WORD | 31
HWORD | 15
BYTE | 7

## Slide 20: FP to Integer Datapath
Conversion datapath
  FP to INT (exp < 52)
  FP to INT (52 <= exp)

## Slide 21: FP to integer (1/)
Floating to integer dataflow
  Data packing
  Right shift by sh_amount (subnormal don’t care)
    Expo < 52
      Exponent: (52 – expo)
      Rounding: rounded by 54-bit adder
    52 <= expo <= 63
      Exponent: (63 – expo)
      Rounding: no rounding
  Do rounding
  2’s complement if source value is negative
Round digit/2’sc inc generation merge rounding and 2’sc steps

## Slide 22: FP to integer (2/)
Exponent
  Expo < 52
    Exponent: (52 – expo)
    Rounding: rounded by 54-bit adder
  52 <= expo <= 63
    Exponent: (63 – expo)
    Rounding: no rounding
Rounding (SP to long)
  Expo < 52
    Right shift (52 – expo) bits because leading 12 bits are 0
    Need to round (at least 1bit shifted to bit[10:0])
    Result is {12’b0, bit[62:11]}
  52 <= Expo <= 63
    Right shift (63 – expo)
    No need to round
    Result is {bit[63:0]}
  64 <= Expo
    Source value is greater than max integer value
LRS
12’d0
Result
63 11 10 0
For rounding
Expo < 52
Result
63 11 10 0
No rounding
52<= Expo <= 63

## Slide 23: FP to FP Datapath
FP narrowing to FP widening
FP widening to narrowing

## Slide 24: FP to FP (1/)
The F2F conversion is dividend into two parts.
  Wider to narrow
  Narrow to wider
Floating-point to floating-point methodology
  Wider to narrow (abs)
    Calculate exponent directly
    Shift amount
      Result > subnormal
        (src_expo – (src_mant_width – dst_mant_width))
      Result <= subnormal
        (~src_expo - dst_bias + (src_mant_width – dst_mant_width) + 1)
    Rounding
  Narrow to wider (nbs)
    Use NBS (left shift) for normal or subnormal input
    No Rounding is needed
1 for subnormal

## Slide 25: Round digit/2’sc inc generation

## Slide 26: Round digit/2’sc inc generation (1/)

## Slide 27: Round digit/2’sc inc generation (2/)
Do rounding and 2’sc at the same time or one of those
Merge rounding and 2’sc steps to improve critical path
No inclement LSB Inclement LSB0 Inclement LSB1
If rounding no inclement LSB => set inc=1
If rounding inclement LSB => set inc=0
If RNE tie clear LSB and LSB was 1 => set inc=1
  Round-bit=1 & round_digit=01 & LSB = 1
    should inclement LSB, but LSB will be cleared, so set inc=1
  No Round-to-odd in F2I instruction
3 round to 3
0011 -> 0011
2’s c: inv+1
1100
+ 1
-------- ---------
1101 1101
-3 -3
4 round to 5
0100 -> 0101
2’s c: inv+0
1011 1010
+ 1 + 1
-------- ---------
1100 1011
-4 -5
3 round to 4
0011 -> 0100
2’s c: inv+0
1100 1011
+ 1 + 1
-------- ---------
1101 1100
-3 -4
Notes: A is value after rounding
R is rounding inclement
B = A+R
Result = B’+1 = (A+R)’+1
R = 0, Result = A’+1
R = 1, Result = A’-1+1 = A’

## Slide 28: comparing & others instructions

## Slide 29: Comparing & Others Instructions
Comparing instructions
Others instructions

## Slide 30: Comparing & Others Instructions
Comparing & others instruction block diagram detail
bf2s: bfloat16 to single

## Slide 31: Comparing Instructions
Comparing instructions
  Scalar: return 0/1
  Vector: Write the comparison result to a mask register
Min/Max instructions
  The rm field indicates MIN/MAX
  FMIN: Write the smaller of rs1 and rs2 to rd
  FMAX: Write the larger of rs2 and rs2 to rd
  The value −0.0 is considered to be less than the value +0.0.
  Both inputs are NaNs, the result is the canonical NaN.
  Only one operand is a NaN, the result is the non-NaN operand.
  Signaling NaN inputs raise the invalid operation exception, even when the result is not NaN.

## Slide 32: Others Instructions
Sign-injection instructions
  The result takes all bits except the sign bit form the vector vs2 operands.
  The rm (rounding mode) field indicates J[N]/JX
Classify instructions
  The 10-bit mask produced by this instruction is placed in the LSB of the result elements.
  This instruction is only defined for SEW=16b above, so the result will always fit in the destination elements.
Rd bit | Meaning
0 | rs1 is -inf
1 | rs1 is a -normal number
2 | rs1 is a -subnormal number
3 | rs1 is -0
4 | rs1 is +0
5 | rs1 is a +subnormal number
6 | rs1 is a +normal number
7 | rs1 is +inf
8 | rs1 is a signaling NaN
9 | rs1 is a quiet NaN

## Slide 33: Cross Lane forwarding path

## Slide 34: Narrowing & Mask Instruction Forwarding Path
Narrowing and mask instruction format is special and those instruction result will go through to lower lane. (e.g. Lane 1 Lane 0)
The following instruction need to shift to narrowing format
  Lane produce result and pack result
  Lane_Carry_control pack result and duplicated

## Slide 35: Reduction instructions Forwarding Path
Reduction instruction data flow
  Do the corresponding operator to deal with each vector datas
  Merge elements in lane first then merge remain results
VLEN=256, SIMD=256, LMUL=2, SEW=16, VL=VLMAX

## Slide 36: Enhancements

## Slide 37: Enhancement list (1/)
Enhance sticky generation path (st1)
Leading zero detection before 2’sc
  Early detection for leading zero
  1bit error correction
Reduce integer value mux
Merge 64bit and 54bit adder (?)
Merge non-conversion result path

## Slide 38: Sticky generation for normalization (1/)
LZC logic

## Slide 39: Sticky generation for normalization (2/)
LZC = 5d’13 = 5’b01101
LZC[4] = 0, L4_sticky = |bit[15:0]
LZC[3] = 1, L3_sticky = L4_sticky | 1’b0
LZC[2] = 1, L2_sticky = L3_sticky | 1’b0
LZC[1] = 0, L1_sticky = L2_sticky | bit[17:16]
LZC[0] = 1, L0_sticky = L1_sticky | (LZC[0]) ? bit[18] : |bit[19:18];
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0
0
1
1
0
1
Notes: l5_sticky = 1’b0
l4_sticky = (f1_s_lz_num[5] == 1’b1) ? l5_sticky :|bit[15:0]
L3_sticky = (f1_s_lz_num[5:4] == 2’b11) ? l4_sticky :
l4_sticky | (| bit[27:24])

## Slide 40: Sticky generation for normalization (3/)
Notes: l5_sticky = 1’b0
l4_sticky = (f1_s_lz_num[5] == 1’b1) ? l5_sticky :|bit[15:0]
L3_sticky = (f1_s_lz_num[5:4] == 2’b11) ? l4_sticky :
l4_sticky | (| bit[27:24])

## Slide 41: Leading zero detection before 2’sc (1/)
Extra logics to handle LZD 1 bit error
  Bit pattern detection (1+0*)
    8bit example  11110000
  LZC correction
  Clear st1
  Set nbs dat

## Slide 42: Leading zero detection before 2’sc (2/)
Bit pattern detection logic
LZD error bit patterns
  Example
    A  8’b11110000 (neg int)
    A 1’sc  8’b00001111  LZC = 4, sticky = 1, nds_dat = 8’b00000000
    A 2’sc  8’b00010000  LZC = 3, sticky = 0, nds_dat = 8’b10000000
  Hit bit pattern
    LZC = LZC -1
    Sticky = 0
    nds_dat = 8’b10000000

## Slide 43: Reduce integer value mux (1/)
Modify integer value alignment from 63-bit to 0-bit
  Reduce data type selection

## Slide 44: Merge 64bit and 54bit adder (1/)
Use 65-bit adder to do 64-bit 2’sc and 54-bit rounding (lsb is round bit)
For 64-bit 2’sc, just add 1 at round bit.

## Slide 45: Instruction List

## Slide 46: Supported scalar fp instruction list (1/)
Sign-injection instruction
  fsgnj.[hsd]
  fsgnjn.[hsd]
  fsgnjx.[hsd]
Compare instruction
  feq.[hsd]
  flt.[hsd]
  fle.[hsd]
Classify instruction
  fclass.[hsd]
Move instruction
  fmv.x.[hwd]
  fmv.[hwd].x

## Slide 47: Supported scalar fp instruction list (2/)
Conversion between int and fp
Conversion between fp and fp
Int width\fp_width | F16(HP) | F32(SP) | F64(DP)
I32 | fcvt.w.h fcvt.wu.h fcvt.h.w fcvt.h.wu | fcvt.w.s fcvt.wu.s fcvt.s.w fcvt.s.wu | fcvt.w.d fcvt.wu.d fcvt.d.w fcvt.d.wu
I64 | fcvt.l.h fcvt.lu.h fcvt.h.l fcvt.h.lu | fcvt.l.s fcvt.lu.s fcvt.s.l fcvt.s.lu | fcvt.l.d fcvt.lu.d fcvt.d.l fcvt.d.lu
SRC \ DST | F16(HP) | Bfloat16 | F32(SP) | F64(DP)
F16(HP) | X | X | fcvt.s.h | fcvt.d.h
Bfloat16 | X | X | fcvt.s.bf16 | X
F32(SP) | fcvt.h.s | fcvt.bf16.s | X | fcvt.d.s
F64(DP) | fcvt.h.d | X | fcvt.s.d | X

## Slide 48: Supported vector fp instruction list (1/)
14.11. Vector Floating-Point MIN/MAX Instructions
  Floating-point minimum
    vfmin.vv vd, vs2, vs1, vm # Vector-vector
    vfmin.vf vd, vs2, rs1, vm # Vector-scalar
  Floating-point maximum
    vfmax.vv vd, vs2, vs1, vm # Vector-vector
    vfmax.vf vd, vs2, rs1, vm # Vector-scalar
14.12. Vector Floating-Point Sign-Injection Instructions
  For vfsgnj, the result’s sign bit is v/rs1’s sign bit.
    vfsgnj.vv vd, vs2, vs1, vm # Vector-vector
    vfsgnj.vf vd, vs2, rs1, vm # Vector-scalar
  For vfsgjn, the result’s sign bit is the opposite of v/rs1’s sign bit.
    vfsgnjn.vv vd, vs2, vs1, vm # Vector-vector
    vfsgnjn.vf vd, vs2, rs1, vm # Vector-scalar
  For vfsgnjx, the sign bit is the XOR of the sign bits of v/rs1 and vs2.
    vfsgnjx.vv vd, vs2, vs1, vm # Vector-vector
    vfsgnjx.vf vd, vs2, rs1, vm # Vector-scalar

## Slide 49: Supported vector fp instruction list (2/)
14.13. Vector Floating-Point Compare Instructions
  Compare equal
    vmfeq.vv vd, vs2, vs1, vm # Vector-vector
    vmfeq.vf vd, vs2, rs1, vm # Vector-scalar
  Compare not equal
    vmfne.vv vd, vs2, vs1, vm # Vector-vector
    vmfne.vf vd, vs2, rs1, vm # Vector-scalar
  Compare less than
    vmflt.vv vd, vs2, vs1, vm # Vector-vector
    vmflt.vf vd, vs2, rs1, vm # Vector-scalar
  Compare less than or equal
    vmfle.vv vd, vs2, vs1, vm # Vector-vector
    vmfle.vf vd, vs2, rs1, vm # Vector-scalar
  Compare greater than
    vmfgt.vf vd, vs2, rs1, vm # Vector-scalar
  Compare greater than or equal
    vmfge.vf vd, vs2, rs1, vm # Vector-scalar

## Slide 50: Supported vector fp instruction list (3/)
14.14. Vector Floating-Point Classify Instruction
  vfclass.v vd, vs2, vm # Vector-vector
14.15. Vector Floating-Point Merge Instruction
  vfmerge.vfm vd, vs2, rs1, v0 # vd[i] = v0.mask[i] ? f[rs1] : vs2[i]
14.16. Vector Floating-Point Move Instruction
  vfmv.v.f vd, rs1 # vd[i] = f[rs1]
14.17. Single-Width Floating-Point/Integer Type-Convert Instructions
  vfcvt.xu.f.v vd, vs2, vm # Convert float to unsigned integer.
  vfcvt.x.f.v vd, vs2, vm # Convert float to signed integer.
  vfcvt.rtz.xu.f.v vd, vs2, vm # Convert float to unsigned integer, truncating.
  vfcvt.rtz.x.f.v vd, vs2, vm # Convert float to signed integer, truncating.
  vfcvt.f.xu.v vd, vs2, vm # Convert unsigned integer to float.
  vfcvt.f.x.v vd, vs2, vm # Convert signed integer to float.

## Slide 51: Supported vector fp instruction list (4/)
14.18. Widening Floating-Point/Integer Type-Convert Instructions
  vfwcvt.xu.f.v vd, vs2, vm # Convert float to double-width unsigned integer.
  vfwcvt.x.f.v vd, vs2, vm # Convert float to double-width signed integer.
  vfwcvt.rtz.xu.f.v vd, vs2, vm # Convert float to double-width unsigned integer truncating.
  vfwcvt.rtz.x.f.v vd, vs2, vm # Convert float to double-width signed integer truncating.
  vfwcvt.f.xu.v vd, vs2, vm # Convert unsigned integer to double-width float.
  vfwcvt.f.x.v vd, vs2, vm # Convert signed integer to double-width float.
  vfwcvt.f.f.v vd, vs2, vm # Convert single-width float to double-width float.
14.19. Narrowing Floating-Point/Integer Type-Convert Instructions
  vfncvt.xu.f.w vd, vs2, vm # Convert double-width float to unsigned integer.
  vfncvt.x.f.w vd, vs2, vm # Convert double-width float to signed integer.
  vfncvt.rtz.xu.f.w vd, vs2, vm # Convert double-width float to unsigned integer truncating.
  vfncvt.rtz.x.f.w vd, vs2, vm # Convert double-width float to signed integer truncating.
  vfncvt.f.xu.w vd, vs2, vm # Convert double-width unsigned integer to float.
  vfncvt.f.x.w vd, vs2, vm # Convert double-width signed integer to float.
  vfncvt.f.f.w vd, vs2, vm # Convert double-width float to single-width float.
  vfncvt.rod.f.f.w vd, vs2, vm # Convert double-width float to single-width float rounding towards odd.

## Slide 52: Supported vector fp instruction list (5/)
15.3. Vector Single-Width Floating-Point Reduction Instructions
  vfredmax.vs vd, vs2, vs1, vm # Maximum value
  vfredmin.vs vd, vs2, vs1, vm # Minimum value
Custom instruction
  vfwcvt.s.bf16 vd, vs2, vm
  vfncvt.bf16.s vd, vs2, vm

## Slide 53: Backup

## Slide 54: Rounding mode (1/)
Alternative rounding options are also available. IEEE 754 specifies the following rounding modes:
  round to nearest
    where ties round to the nearest even digit in the required position (the default and by far the most common mode)
  round to nearest
    where ties round away from zero (optional for binary floating-point and commonly used in decimal)
  round up (toward +∞;)
    negative results thus round toward zero
  round down (toward −∞)
    negative results thus round away from zero
  round toward zero (truncation)
    it is similar to the common behavior of float-to-integer conversions, which convert −3.9 to −3 and 3.9 to 3

## Slide 55: Rounding mode (2/)
Sign,LSB,round,stick | RNE | RTZ | RDN | RUP | RMM
0_000 | +0 | +0 |  |  | 
0_001 | +0 | +0 |  |  | 
0_010 | +0 | +0 |  |  | 
0_011 | +1 | +0 |  |  | 
0_100 | +0 | +0 |  |  | 
0_101 | +0 | +0 |  |  | 
0_110 | +1 | +0 |  |  | 
0_111 | +1 | +0 |  |  | 
1_000 | +0 | +0 |  |  | 
1_001 | +0 | +0 |  |  | 
1_010 | +0 | +0 |  |  | 
1_011 | +1 | +0 |  |  | 
1_100 | +0 | +0 |  |  | 
1_101 | +0 | +0 |  |  | 
1_110 | +1 | +0 |  |  | 
1_111 | +1 | +0 |  |  |