## Slide 1: FP MISC uArch
202012
Larry

## Slide 2: Agenda
List of abbreviation/parameter
Overview
Configuration
uArch overview
Conversion Instructions
Round digit/2’sc inc generation
Underflow Flag Detection
Comparing & Others instructions
Cross Lane Forwarding Path
Conversion from nibble/byte to HP/SP
Enhancements
Interface
Instruction encoding

## Slide 3: List of abbreviation (1/)
Abbreviation | Definition
F2I/F2F/I2F | F: Floating-point, I: integer
ABS | Alignment barrel shift
NBS | Normalization barrel shift
2’sc | 2’s complement
LZD | Leading zero detection
LZC | Leading zero count

## Slide 4: List of parameter (1/)
Abbreviation | Definition
XLEN | The current width of an x register in bits (32 for RV32 or 64 for RV64)
FLEN | The current width of a f register in bits (32 for SP, 64 for DP)
VLEN | Vector length
ELEN | Element width

## Slide 5: Overview (1/)
2-stage pipeline
Supported data types
  BFloat16/HP/SP/DP
  Int8/Int16/Int32/Int64
The followings are supported instructions and the corresponding latency
  Conversion (I2F, F2F, F2I)
  Comparing/min/max
  Sign injection/classify/move
Precision | Width | Sign | Expo | Mant
HP | 16 | 1 | 5 | 10
Bfloat16 | 16 | 1 | 8 | 7
SP | 32 | 1 | 8 | 23
DP | 64 | 1 | 11 | 52

## Slide 6: Overview (2/)
Instruction latency
Instruction | Latency |  |  | 
 | Scalar |  | Vector | 
Conversion | 2 |  | Widening | 2
 |  |  | Narrowing | 3
Sign injection | 2 |  | 2 | 
Min/max | 2 |  | 2 | 
Comparing | 1 |  | 2 | 
Classify | 1 |  | 2 | 
Move | toFRF | 2 | 2 | 
 | toXRF | 1 |  | 

## Slide 7: Configurability
Feature | Options
XLEN | 64
FLEN* | 16/32/64
VLEN | 512/256/128
SIMD_WIDTH | 512/256/128
ELEN* | 32/64
*If RVV = 0, FLEN can be configured to 32/64
*If RVV = 1, FLEN is equivalent to ELEN

## Slide 8: uArch overview

## Slide 9: VPU stage
Frontend
Function unit

## Slide 10: Function Unit Lane Hierarchy
src_gen is for source data selection
  Select data for read port 0/ 1/ 2/ 3 or scalar register
FSM is for reduction instructions to generate control signals
Lane_carry_control handle data forwarding between each lane
ELEN=32
ELEN=64

## Slide 11: FMIS uArch (1/)

## Slide 12: FMIS uArch (2/)
INT to FP

## Slide 13: FMIS uArch (3/)
FP to INT

## Slide 14: FMIS uArch (4/)
FP widening
FP narrowing
Bfloat16 to SP
SP to Bfloat16

## Slide 15: FMIS uArch (5/)
Comparing instructions
Others instructions
Scalar fp result (XRF

## Slide 16: Conversion instructions

## Slide 17: Integer to FP Datapath
INT to FP

## Slide 18: Integer to FP (1/)
Integer to floating-point dataflow
  Data packing
  Do 3 things in parallel
    Do 2’sc for negative integer
    Generate LZC
    Find bit pattern for correction
  Normalize data and generate sticky bit
  Pack to significand format according destination precision
  Do rounding
Enhancements
  Detect Leading zero before 2’sc
  Structuralized OR network
  Structuralized AND network
  Rearrange data alignment for I2F
    Reduce selection multiplexers
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 19: Integer to FP (2/)
Data packing
  Reduce selection mux
  Reduce shift amount computation
    52/63 – LZC  63 – LZC = ~LZC & mask (‘d63)
Notes: Bit width is (1+FLEN_MAX) - (1+FLEN_MIN) + XLEN

## Slide 20: Integer to FP (3/)
Normalization
  Calculate leading zero number
    Generate string for LZC
  Exponent calculation
    Rearrange data alignment for reducing selection mux
    Result expo = (XLEN – 1) – LZC (expo hasn’t bias)
  Apply structuralized OR network to calculate LZC, sticky bit and propagation bit
  Apply barrel shift to normalize source data
Rounding
  Generate round digit according to round mode, sticky bit and propagation bit
  Select (exponent) or (exponent+1) according to carry bit

## Slide 21: FP to Integer Datapath
FP to INT

## Slide 22: FP to integer (1/)
Floating to integer dataflow
  Data packing
  Right shift packed data according to difference of exponent
  Generate round digit
  Do rounding and 2’sc at the same time
Enhancements
  Rearrange data alignment for F2I
  Merge 64bit and 54bit adder

## Slide 23: FP to integer (2/)
Unpack and align data
  Align all precision source value at (XLEN - 1) bit like as following fig
Shift amount (exponent hasn’t bias)
  ABS should support 65 shift amount value when XLEN is 64
    ABS_amount == 64
      aligned data LSB is hidden one
      Sticky is (|abs_in[62:11]) / (|abs_in[62:0])
    ABS_amount >= 65
      aligned data LSB is zero
      Sticky is set
    Shift all significand to sticky field
  Apply 64-bit adder to handle (exponent < 64)
    Shift amount: (XLEN – 1) – exponent (exponent hasn’t bias)
      XLEN=64  63–exponent  ~exponent & ‘d63
      XLEN=32  31–exponent  ~exponent & ‘d31
Round digit/2’sc inc generation merge rounding and 2’sc steps

## Slide 24: FP to FP Datapath
FP widening
FP narrowing
Bfloat16 to SP
SP to Bfloat16

## Slide 25: FP to FP – Widening FP (1/)
Widening instruction dataflow
  Calculate LZC for subnormal value and do normalization
  No Rounding is needed
  No subnormal result
Data packing
  Align hidden one and calculate LZC
    Subnormal input will be shifted to normal fp format
  Packing data according to destination precision

## Slide 26: FP to FP – Narrowing FP (2/)
Narrowing instruction dataflow
  Calculate subnormal result flag
  Use subnormal result flag to select shift amount (shift to normal/subnormal)
  Calculate exponent without bias
  Generate shifted value and round digit
  Do rounding
Enhancement
  Rearrangement data alignment for narrowing FP
    Because 64-bit and 54-bit adders are merged.

## Slide 27: FP to FP – Narrowing FP (3/)
Calculate subnormal result flag
  Use exponent to detect that result may be subnormal value (exponent has bias)
    DP to SP subnormal (exponent - 1023 <= -127, exponent < 897)
    DP to HP subnormal (exponent - 1023 <= -15, exponent < 1009)
    SP to HP subnormal (exponent - 127 <= -15, exponent < 113)

## Slide 28: FP to FP – Narrowing FP (4/)
Shift amount
  If normal result, ABS shift input value to normal format
    DP to SP: 40
    DP to HP: 53
    SP to HP: 53
    SP to Bfloat16: 56
  If subnormal result, ABS shift input value to subnormal format
    DP to SP: – (exponent – 1023) – 127 + 40 + 1 = ~exponent + 1 + 937 = ~exponent + 938
    DP to HP: – (exponent – 1023) – 15 + 53 + 1 = ~exponent + 1 + 1062 = ~exponent + 1062
    SP to HP: – (exponent – 127) – 15 + 53 + 1 = ~exponent + 1 + 166 = ~exponent + 167
exponent has bias

## Slide 29: Round digit/2’sc inc generation

## Slide 30: Round digit/2’sc inc generation (1/)

## Slide 31: Round digit/2’sc inc generation (2/)
Merge the following steps to reduce dummy adder
  increment 1 of 2’sc
  rounding
The round digit support the following features
  Rounding
    Positive integer to floating-point
    Floating-point to floating-point
  Increment 1 then rounding
    Negative integer to floating-point
  Rounding then increment 1
    Floating-point to negative integer

## Slide 32: Round digit/2’sc inc generation (3/)
Rounding increment under different rounding mode
Sign | L | R | S |  | RNE | RTZ | RDN | RUP | RMM | ROD
0 | 0 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +1
0 | 0 | 0 | 1 |  | +0 | +0 | +0 | +1 | +0 | +1
0 | 0 | 1 | 0 |  | +0 | +0 | +0 | +1 | +1 | +1
0 | 0 | 1 | 1 |  | +1 | +0 | +0 | +1 | +1 | +1
0 | 1 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +0
0 | 1 | 0 | 1 |  | +0 | +0 | +0 | +1 | +0 | +0
0 | 1 | 1 | 0 |  | +1 | +0 | +0 | +1 | +1 | +0
0 | 1 | 1 | 1 |  | +1 | +0 | +0 | +1 | +1 | +0
1 | 0 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +1
1 | 0 | 0 | 1 |  | +0 | +0 | +1 | +0 | +0 | +1
1 | 0 | 1 | 0 |  | +0 | +0 | +1 | +0 | +1 | +1
1 | 0 | 1 | 1 |  | +1 | +0 | +1 | +0 | +1 | +1
1 | 1 | 0 | 0 |  | +0 | +0 | +0 | +0 | +0 | +0
1 | 1 | 0 | 1 |  | +0 | +0 | +1 | +0 | +0 | +0
1 | 1 | 1 | 0 |  | +1 | +0 | +1 | +0 | +1 | +0
1 | 1 | 1 | 1 |  | +1 | +0 | +1 | +0 | +1 | +0

## Slide 33: Round digit/2’sc inc generation (4/)
1. Do rounding only
  A + increment (1 bit) (A has not round bit)
Abbreviation
  L is LSB/ R is round bit / S is sticky bit / Tie is (R & ~S)
Rounding mode | Rounding inc
RNE (Round to Nearest, ties to Even) | 1. R then clear sum LSB if tie/ 2. R & (L ¦ S)
RTZ (Round Towards Zero) | 0
RDN (Round DowN) | sign & (R ¦ S)
RUP (Round UP) | ~sign & (R ¦ S)
RMM (Round to nearest, ties to Max Magnitude) | R
ROD (Round towards ODd) | 1. Set LSB when R or S is set 2. ~L & (R ¦ S)

## Slide 34: Round digit/2’sc inc generation (5/)
2. Increment 1 then rounding
Abbreviation
  L is LSB
  R is round bit
  S is sticky bit
  P is propagation bit
  L, R, S is from 1’sc source value
Propagation bit
  P is 1 if sticky field are all-one
  P is 1 if the source LSB is moved to sticky MSB or higher.
* Unreachable

## Slide 35: Round digit/2’sc inc generation (6/)
2. Increment 1 then rounding
Correction logic
  Correction_S = (~2sc_inc & S) | (~(2sc_inc | (S & P)))
  {Correction_L , Correction_R} = {L,R} + 2sc_inc & S & P
Round digit[1] is 2sc_inc & R & S & P
2’sc inc | S | P |  | Correct S | Carry
0 | 0 | 0 |  | 0 | 0
0 | 0 | 1 |  | 0 | 0
0 | 1 | 0 |  | 1 | 0
0 | 1 | 1 |  | 1 | 0
1 | 0 | 0 |  | 1 | 0
1 | 0 | 1 |  | 1 | 0
1 | 1 | 0 |  | 1 | 0
1 | 1 | 1 |  | 0 | 1
* Unreachable
Notes:   Correction_S
  = (~2sc_inc & S) | (2sc_inc & (~S | ~P))
  = (~2sc_inc & S) | (2sc_inc & ~(S & P))
  = (~2sc_inc & S) | (~(2sc_inc | (S & P)))

## Slide 36: Round digit/2’sc inc generation (7/)
3.Rounding then increment 1
Proof
  B = A + r (A is before rounding, B is after rounding)
  ~A + inc = ~B + 1 = ~(A + r) + 1
  R = 0  ~A + inc = ~(A + 0) + 1  inc = 1
  R = 1  ~A + inc = ~(A + 1) + 1 = ~A – 1 + 1  inc = 0
    -1  A = 8’b11111111
      ~ (A + 1) = 8’b11111111
      ~A = 8’b00000000, ~A – 1 = 8’b11111111
    -128  A = 8’b10000000
      ~ (A + 1) = 8’b01111110
      ~A = 8’b01111111, ~A – 1 = 8’b01111110
Summary
  inc is 0 if rounding increment is 1
  inc is 1 if rounding increment is 0
Correction logic
  neg_int_result ^ rounding inc
Notes: A is value after rounding
R is rounding inclement
B = A+R
Result = B’+1 = (A+R)’+1
R = 0, Result = A’+1
R = 1, Result = A’-1+1 = A’

## Slide 37: Round digit/2’sc inc generation (8/)
Abbreviation
  r_inc is rounding increment
  c_inc is 2’sc increment
  neg_int_src is negative integer source
  neg_int_res is negative integer result
Round digit
  Round digit[1] is neg_int_src & c_inc
  Round digit[0] is neg_int_res ^ r_inc
  Then the sum of Round_digit[1], Round digit[0] and shifted data is the result
Notes: A is value after rounding
R is rounding inclement
B = A+R
Result = B’+1 = (A+R)’+1
R = 0, Result = A’+1
R = 1, Result = A’-1+1 = A’

## Slide 38: Underflow Flag Detection

## Slide 39: Underflow Flag Detection – Special Case (1/)
Tininess is detected after rounding.
The exponent range are unbounded and the significand is not bounded to the corresponding format and keep normal format.
The above unbounded value is in subnormal range when exponent is unbounded. The bounded value will round to min normal value and it is not in subnormal range and underflow flag is not asserted because of rounding to min normal value. Thus, this special case should be detected.
 | Significand (HP) | Exponent
Unbounded | 01.1111_1111_11xxx | -15
bounded | 00.1111_1111_111xx | -14

## Slide 40: Underflow Flag Detection – Special Case (2/)
The Fig. show result format, L, R, S, Sm and St field.
The bit pattern is all-one mantissa and the next slide show underflow special case detection.
RM | Underflow special case
RNE | BP & R & ~Sm
RTZ | 0
RDN | BP & sign & (R^S)
RUP | BP & ~sign & (R^S)
RMM | BP & R & ~Sm
ROD | 0

## Slide 41: Underflow Flag Detection – Normal Case (4/)
The underflow just qualify bit pattern, rounding carry (round digit) and other signals.
The bit pattern is the same with the special case

## Slide 42: comparing & others instructions

## Slide 43: Comparing & Others Instructions Datapath
Comparing instructions
Others instructions
Scalar fp result (XRF

## Slide 44: Comparing & Others Instructions
Comparing & others instruction block diagram detail
bf2s: bfloat16 to single

## Slide 45: Comparing Instructions
Comparing instructions
  Scalar: return 0/1
  Vector: Write the comparison result to a mask register
Min/Max instructions
  The rm field indicates MIN/MAX
  FMIN: Write the smaller of rs1 and rs2 to rd
  FMAX: Write the larger of rs2 and rs2 to rd
  The value −0.0 is considered to be less than the value +0.0.
  Both inputs are NaNs, the result is the canonical NaN.
  Only one operand is a NaN, the result is the non-NaN operand.
  Signaling NaN inputs raise the invalid operation exception, even when the result is not NaN.

## Slide 46: Others Instructions
Sign-injection instructions
  The result takes all bits except the sign bit form the vector vs2 operands.
  The rm (rounding mode) field indicates J[N]/JX
Classify instructions
  The 10-bit mask produced by this instruction is placed in the LSB of the result elements.
  This instruction is only defined for SEW=16b above, so the result will always fit in the destination elements.
Rd bit | Meaning
0 | rs1 is -inf
1 | rs1 is a -normal number
2 | rs1 is a -subnormal number
3 | rs1 is -0
4 | rs1 is +0
5 | rs1 is a +subnormal number
6 | rs1 is a +normal number
7 | rs1 is +inf
8 | rs1 is a signaling NaN
9 | rs1 is a quiet NaN

## Slide 47: Cross Lane datapath

## Slide 48: Narrowing & Mask Instruction Datapath
Narrowing and mask instruction format is special and those instruction result will go through to lower lane. (e.g. Lane 1 Lane 0)
The following instruction need to shift to narrowing format
  Lane produce result and pack result
  Lane_Carry_control pack result and duplicated

## Slide 49: Reduction Instructions (1/)
Reduction instruction data flow
  Do the corresponding operator to deal with each vector element
  Merge elements in lane first then merge remain results
Lane0
Lane1
Lane2
Lane3
LANE 2TO1
LANE 4TO2

## Slide 50: Reduction Instructions (2/)
Lane0 -64-bit
lane1
lane2
lane3
lane4
lane5
lane6
lane7
Inter lanes, op1 mux
pipe0
pipe1
pipe2
pipe3
Ordered reduction
Unordered reduction
Dot-product, VD accumulation
Intra lane, op3 mux
pipe0
pipe1
pipe2
pipe3
Intra lane, op1 mux
VLEN=512, 4*2 lanes * 64-bit

## Slide 51: Reduction Instructions (3/)
FSM
VLEN | SIMD Ratio | Lane Count
512 | 1:1 | 8
256 | 1:1 | 4
128 | 1:1 | 2
512 | 2:1 | 4
256 | 2:1 | 2
128 | 2:1 | 1
REDUCT_SCLR
REDUCT_VEC
PIPE_4TO2
PIPE_2TO1
LANE_8TO4
LANE_4TO2
LANE_2TO1
OREDUCT_VEC
sew16
sew64
sew32
uop_cnt != 0
uop_cnt != 0
lane_cnt = 8
lane_cnt = 4
lane_cnt = 2
State | Action
REDUCT_SCLR | also the idle state accumulate the scalar element
REDUCT_VEC | accumulate elements to its corresponded tree leaf node
PIPE_4TO2 | merge 4 pipe results in each lane to 2 p0 = p0 + p1, p2 = p2 + p3
PIPE_2TO1 | merge 2 pipe results in each lane to 1 p0 = p0 + p2
LANE_8TO4 | merge 8 lane results to 4
LANE_4TO2 | merge 4 lane results to 2
LANE_2TO1 | merge 2 lane result to 1, it’s the final result
DOTPROD_ACC | 

## Slide 52: Reduction Instructions (4/)
VLEN=256, SIMD=256, LMUL=2, SEW=16, VL=VLMAX
REDUCT_SCLR
REDUCT_VEC
PIPE_4TO2
PIPE_2TO1
LANE_8TO4
LANE_4TO2
LANE_2TO1
OREDUCT_VEC
sew16
sew64
sew32
uop_cnt != 0
uop_cnt != 0
lane_cnt = 8
lane_cnt = 4
lane_cnt = 2
PIPE_2TO1
PIPE_4TO2
LANE_4TO2
LANE_2TO1
REDUCT_VEC
REDUCT_VEC

## Slide 53: Conversion from nibble/byte to HP/SP (1/)
The design support conversion from nibble/byte to floating-point
The supported precisions are half-precision and single-precision
Interface
Signal name | Width | Description
sew | 3 | Indicate result fp type. 3’b010 indicates SP and others indicate HP
sign | 1 | 0 is unsigned and 1 is signed
data | 8 | 8-bit integer value
wdata | FLEN (16/32) | Result data. Do nan-boxing for hp result when result type is HP and FLEN is 32.

## Slide 54: Conversion from nibble/byte to HP/SP (2/)
The following figures are the corresponding datapath
FLEN 32
FLEN 16

## Slide 55: Conversion from nibble/byte to HP/SP (3/)
Data alignment
Do extension for nibble value according to signed or unsigned
  Signed  signed extension
  Unsigned  zero extension

## Slide 56: Enhancements

## Slide 57: Enhancement list (1/)
Enhance sticky generation path (st1)
Detect Leading zero before 2’sc
Rearrange data alignment for I2F
Rearrange data alignment for F2I
Rearrange data alignment for narrowing FP
Merge 64bit and 54bit adder and non-conversion data path
MISC
Move Bfloat16 to SP to fmv datapath

## Slide 58: Structuralized OR network (1/)
LZC logic

## Slide 59: Structuralized OR network (2/)
LZC = 5d’13 = 5’b01101
LZC[4] = 0, L4_sticky = |bit[15:0]
LZC[3] = 1, L3_sticky = L4_sticky | 1’b0
LZC[2] = 1, L2_sticky = L3_sticky | 1’b0
LZC[1] = 0, L1_sticky = L2_sticky | bit[17:16]
LZC[0] = 1, L0_sticky = L1_sticky | (LZC[0]) ? bit[18] : |bit[19:18];
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0
0
1
1
0
1
or
or
Notes: l5_sticky = 1’b0
l4_sticky = (f1_s_lz_num[5] == 1’b1) ? l5_sticky :|bit[15:0]
L3_sticky = (f1_s_lz_num[5:4] == 2’b11) ? l4_sticky :
l4_sticky | (| bit[27:24])

## Slide 60: Structuralized OR network (3/)
BACK
Notes: l5_sticky = 1’b0
l4_sticky = (f1_s_lz_num[5] == 1’b1) ? l5_sticky :|bit[15:0]
L3_sticky = (f1_s_lz_num[5:4] == 2’b11) ? l4_sticky :
l4_sticky | (| bit[27:24])

## Slide 61: Structuralized OR network (4/)
LZC = 5d’13 = 5’b01101
LZC[4] = 0, L4_sticky = |bit[15:0]
LZC[3] = 1, L3_sticky = L4_sticky | 1’b0
LZC[2] = 1, L2_sticky = L3_sticky | 1’b0
LZC[1] = 0, L1_sticky = L2_sticky | bit[17:16]
LZC[0] = 1, L0_sticky = L1_sticky | (LZC[0]) ? bit[18] : |bit[19:18];
63 | 62 | 61 | 60 | 59 | 58 | 57 | 56 | 55 | 54 | 53 | 52 | 51 | 50 | 49 | 48 | 47 | 46 | 45 | 44 | 43 | 42 | 41 | 40 | 39 | 38 | 37 | 36 | 35 | 34 | 33 | 32 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
Notes: l5_sticky = 1’b0
l4_sticky = (f1_s_lz_num[5] == 1’b1) ? l5_sticky :|bit[15:0]
L3_sticky = (f1_s_lz_num[5:4] == 2’b11) ? l4_sticky :
l4_sticky | (| bit[27:24])

## Slide 62: Structuralized OR network - ABS(1/)
Generate sticky
  Do OR with the shifted sticky field
Notes: l5_sticky = 1’b0
l4_sticky = LZC[4] & (|bit[16:31])
L3_mux_sticky = (LZC[4:3] == 2’b00) ? (|bit[16:31])

## Slide 63: Structuralized OR network - ABS(2/)
LZC = 5d’13 = 5’b01101
LZC[4] = 0, L4_sticky = LZC[4] & (|bit[16:31])
LZC[3] = 1, L3_sticky = LZC[3] & (|bit[24:31])
LZC[2] = 1, L2_sticky = LZC[2] & (|bit[20:23])
LZC[1] = 0, L1_sticky = LZC[1] & (|bit[18:19])
LZC[0] = 1, L0_sticky = LZC[0] & bit[19]
Sticky = L4_sticky | L3_sticky | L2_sticky | L1_sticky | L0_sticky;
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0
LZC[4]=0
LZC[3]= 1
LZC[2]= 1
LZC[1]= 0
LZC[0]= 1
or
or
LZC[4]=0
LZC[4:3]=01
LZC[4:1]=0110
Notes: l5_sticky = 1’b0
l4_sticky = LZC[4] & (|bit[16:31])
L3_mux_sticky = (LZC[4:3] == 2’b00) ? (|bit[16:31])

## Slide 64: Structuralized OR network - ABS(3/)
Notes: l5_sticky = 1’b0
l4_sticky = LZC[4] & (|bit[16:31])
L3_mux_sticky = (LZC[4:3] == 2’b00) ? (|bit[16:31])

## Slide 65: Structuralized AND network (1/)
Structuralized AND network is similar to OR network
Do AND(&) operation on field and increase normalized value for increasing of 2’sc
Notes: l5_sticky = 1’b0
l4_sticky = (f1_s_lz_num[5] == 1’b1) ? l5_sticky :|bit[15:0]
L3_sticky = (f1_s_lz_num[5:4] == 2’b11) ? l4_sticky :
l4_sticky | (| bit[27:24])

## Slide 66: Structuralized AND network (2/)
BACK
Notes: l5_sticky = 1’b0
l4_sticky = (f1_s_lz_num[5] == 1’b1) ? l5_sticky :|bit[15:0]
L3_sticky = (f1_s_lz_num[5:4] == 2’b11) ? l4_sticky :
l4_sticky | (| bit[27:24])

## Slide 67: Leading zero detection before 2’sc (1/)
Generate LZC early
  What’s input string?

## Slide 68: Leading zero detection before 2’sc (2/)
Merge increment of 2’sc (for negative integer source) to round digit generation and
Add structuralized AND network to deal with carry (from sticky part) because of 2’sc increment
If (1’sc + 1) raise carry bit then exp_inc can select correct exponent
  Negative integer is 16’b1111_1000_0000_0000
  1’sc 16’b0000_0111_1111_1111
  Pack to HP format  01.1111_1111_11 and increment 1 for 2’sc
  Result  10.0000_0000_00 and carry is set then exponent increase 1

## Slide 69: Leading zero detection before 2’sc (3/)
The tail pack 1 string for carry when the integer LSB are shifted in significand field
Example
If (1’sc + 1) raise carry bit then exp_inc can select correct exponent
  Negative integer is 16’b1111_1111_0000_0000
  1’sc 16’b0000_0000_1111_1111_111
  Pack to HP format  01.1111_1111_11 and increment 1 for 2’sc
  Result  10.0000_0000_00 and carry is set then exponent increase 1

## Slide 70: Rearrange data alignment for I2F (1/)
Modify integer value alignment from 63-bit to 0-bit
  Reduce data type selection
For FLEN 32 (pipe0, pipe2)
  Just force lz_num[5] to 1’b1
For FLEN 16 (pipe1, pipe3)
  Just force lz_num[5:4] to 2’b11
lz_num is leading zero count
After 2’sc

## Slide 71: Rearrange data alignment for I2F (2/)
The following show reduced multiplexers
BACK

## Slide 72: Rearrange data alignment for F2I (1/)
Apply a 64-bit adder
BACK

## Slide 73: Rearrange data alignment for narrowing FP (1/)
This rearrangement is for merging two adders
All destination result types are aligned at LSB
  ABS should support 65-bit right shift
BACK

## Slide 74: Merge 64bit and 54bit adder (1/)
Use 64-bit adder to do 64-bit 2’sc and 54-bit rounding
  LSB of 64-bit is for round bit
Rearrange data alignment for all conversion instructions
Adjust shift amount according to changing alignment
BACK

## Slide 75: MISC (1/)
Generate exp_inc in F1 stage
  Bit pattern detection
Move exponent computation to F1 stage
Reduce 1 gate delay
  Source data before clear
  Use frd_is_zero to control mask

## Slide 76: MISC (2/)
Compute F1_fp2hp_abs_amout with op1_exp
  f1_exp_op1_no_bias = {2‘d0, f1_op1_exp_dp} – 13’d1023 if frs is DP
  f1_exp_op1_no_bias = {5‘d0, f1_op1_exp_sp} – 13’d127 if frs is SP
Do not care subnormal source and special value will handle subnormal exponent
Modified shift amount
  f1_dp2hp_abs_amount = (f1_dp2hp_subnorm) ? {2‘b11, ~f1_op1_exp_dp} + 13'd1052 : 13'd42;
  f1_sp2hp_abs_amount = (f1_sp2hp_subnorm) ? {5‘b11111, ~f1_op1_exp_sp} + 13’d156 : 13'd42;
  f1_dp2sp_abs_amount = (f1_dp2hp_subnorm) ? {2‘b11, ~f1_op1_exp_dp} + 13’d927 : 13'd29;

## Slide 77: Interface

## Slide 78: VPU Hierarchy

## Slide 79: Lane Interface (1/)
Module name is vc_lane_vfmis.v
Hierarchy diagram

## Slide 80: Lane Interface (2/)
Block connection diagram

## Slide 81: Lane Interface (3/)
Signal name | Type | Description
core_clk | Input | Clock
core_reset_n | Input | Negative Edge Reset
lane_id | Input | Lane ID and it indicate lane0 for scalar floating-point logics
vfmis_vtype_sew | Input | Apply vsew to execute instruction
vfmis_csr_ediv | Input | Apply vediv to execute instruction
vfmis_vtype_lmul | Input | Apply vlmul to execute instruction
vfmis_rmode | Input | Apply frm to execute instruction
vfmis_valid | Input | Instruction valid signal
vfmis_uop_cnt | Input | Micro-op counter start from 0
vfmis_uop_first | Input | Indicate the 1st micro-op
vfmis_uop_last | Input | Indicate the last micro-op
vfmis_msk_bits | Input | The source data valid signal
vfmis_ex_ctrl | Input | Instruction encoding and please see Instruction encoding slide
vfmis_op_wide | Input | Indicate 2x width destination or source
vfmis_sign | Input | Indicate sign data (XRF)
vfmis_tail_bits | Input | Indicate the tail elements and the value is inversion of vfmis_msk_bits

## Slide 82: Lane Interface (4/)
Signal name | Type | Description
vrf_data[0/1/2/3]_in | Input | The data is from VRF read port 0/1/2/3
frf_data[0/1/2]_out | Input | The data is from FRF read port 0/1/2/3
fmis_scalar_valid | Input | Indicate that the scalar data is valid
vfmis_[vs1/vs2/vs3]_valid | Input | The corresponding source data is valid
vfmis_[vs1/vs2/vs3]_select | Input | The corresponding source is from read port
vfmis_[rs1/rs2]_valid | Input | The corresponding source data is valid
vfmis_rs_data | Input | Indicate the scalar source data of vector instruction

## Slide 83: Lane Interface (5/)
Signal name | Type | Description
vfmis_lane_carryin0_data64 | Input | The data is from other lanes and this port is for reduction instruction
vfmis_lane_carryin1_data64 | Input | The data is from other lanes and this port is for reduction instruction
vfmis_lane_carryout_data64 | Output | This is reduction instruction result and it will go to other lane
vfmis_lci_cmp_data | Input | Get permuted result from vc_lane_carry_control
vfmis_lci_cmp_mask | Input | Get permuted byte-write enable from vc_lane_carry_control
vfmis_lco_cmp_data | Output | This is comparing instruction result and the data will be permuted in vc_lane_carry_control
vfmis_lco_cmp_mask | Output | This is narrowing instruction byte-write enable and it will be permuted in vc_lane_carry_control
vfmis_lci_narr_data | Input | Get permuted result from vc_lane_carry_control
vfmis_lci_narr_mask | Input | Get permuted byte-write enable from vc_lane_carry_control
vfmis_lco_narr_data | Output | This is narrowing instruction result and the data will be permuted in vc_lane_carry_control
vfmis_lco_narr_mask | Output | This is narrowing instruction byte-write enable and it will be permuted in vc_lane_carry_control

## Slide 84: Lane Interface (6/)
Signal name | Type | Description
vfmis_data | Output | Result VRF data
vfmis_frf_data | Output | Result FRF data
vfmis_xrf_data | Output | Result XRF data
vfmis_mask | Output | Result byte-write enable
vfmis_vfcsr_flag_set | Output | Result exception flag

## Slide 85: Pipe Interface (1/)
Module name is vc_vfp_fmis.v
Supported FLENs are 16/32/64 and XLEN is the same with FLEN
Hierarchy diagram

## Slide 86: Pipe Interface (2/)
Signal name | Type | Description
core_clk | Input | Clock
core_reset_n | Input | Negative Edge Reset
lane_pipe_id_0 | Input | Indicate Pipe 0 in Lane 0
f1_valid | Input | Valid signal
f1_fmis_scalar_valid | Input | Indicate scalar instruction
f1_ex_ctrl | Input | Control signal for encoding. More info in instruction encoding slide.
f1_sew | Input | Indicate element width
f1_ediv | Input | Un-used
f1_round_mode | Input | Round mode
f1_widen | Input | Widening instruction for vector instruction
f1_narrow | Input | Narrowing instruction for vector instruction
f1_sign | Input | Indicate signed integer source or decode instruction
f1_vmask | Input | The corresponding element v0.t value

## Slide 87: Pipe Interface (3/)
Signal name | Type | Description
f1_op1_invalid | Input | Invalid oprand1
f1_op2_invalid | Input | Invalid oprand2
f1_op1_data | Input | Source oprand1
f1_op2_data | Input | Source oprand2
f1_cmp_inv_op | Output | Set invalid operation exception flag for scalar fp instruction (destination is XRF)
f1_wdata_en | Output | Write enable for F1 retired instruction (Instruction latency is 1)
f1_wdata | Output | Result data for F1 retired instruction (Instruction latency is 1)

## Slide 88: Pipe Interface (4/)
Signal name | Type | Description
f2_result_type | Output | Result data type 3’b111  DP 3’b110  SP 3’b101  HP 3’b100  Bfloat16 3’b011  Double-word 3’b010  Word 3’b001  Half-word 3’b000  Byte
f2_cmp_result | Output | Partial compare result and upper module need to merging and shifting data.
f2_narr_wdata | Output | Partial narrowing result and upper module need to merging and shifting data.
f2_wdata_en | Output | Write enable for non F1 retired instruction (Instruction latency is 2 or 3)
f2_wdata | Output | Result data for non F1 retired instruction (Instruction latency is 2 or 3)
f2_flag_set | Output | Result exception flag

## Slide 89: Instruction Encoding

## Slide 90: Instruction encoding (1/)

## Slide 91: Backup

## Slide 92: Underflow Flag Detection – All cases
The condition should qualify bit pattern (BP) and the following condition under different rounding mode
BP | Sign | R | Sm | St |  | RNE | RTZ | RDN | RUP | RMM | ROD
Match | 0 | 0 | 0 | 0 |  |  |  |  |  |  | 
Match | 0 | 0 | 0 | 1 |  |  |  |  | A |  | 
Match | 0 | 0 | 1 | 0 |  |  |  |  | A |  | 
Match | 0 | 0 | 1 | 1 |  |  |  |  | A |  | 
Match | 0 | 1 | 0 | 0 |  | A |  |  | A | A | 
Match | 0 | 1 | 0 | 1 |  | A |  |  |  | A | 
Match | 0 | 1 | 1 | 0 |  |  |  |  |  |  | 
Match | 0 | 1 | 1 | 1 |  |  |  |  |  |  | 
Match | 1 | 0 | 0 | 0 |  |  |  |  |  |  | 
Match | 1 | 0 | 0 | 1 |  |  |  | A |  |  | 
Match | 1 | 0 | 1 | 0 |  |  |  | A |  |  | 
Match | 1 | 0 | 1 | 1 |  |  |  | A |  |  | 
Match | 1 | 1 | 0 | 0 |  | A |  | A |  | A | 
Match | 1 | 1 | 0 | 1 |  | A |  |  |  | A | 
Match | 1 | 1 | 1 | 0 |  |  |  |  |  |  | 
Match | 1 | 1 | 1 | 1 |  |  |  |  |  |  | 
RM | Underflow
RNE | BP & R & ~Sm
RTZ | 0
RDN | BP & sign & (R^S)
RUP | BP & ~sign & (R^S)
RMM | BP & R & ~Sm
ROD | 0

## Slide 93: FMIS uArch – v0.1

## Slide 94: FMIS uArch – v0.2

## Slide 95: FMIS uArch – v0.3

## Slide 96: FMIS uArch – v0.4

## Slide 97: VFMIS64 PPA (1/)
The following RTL SHA-1 are
  Original: master branch b81cf640d
  V1: master branch 96a7f05b8
  V2: master branch 4b13089c3
Synthesis tool: DC v2019.03-sp3
Tech_lib: tcbn28hpcplusbwp30p140ssg0p81vm40c
The following reports has output delay
  Flag output delay is 50ps, outputs in F1 are 100ps and outputs in F2 are 200ps, and then FMIS F2 stage just have 340ps@1.25GHz and 500ps@1.00GHz
Feq. | XLEN/FLEN | Original (kgates/ps) | V1 (kgates/ps/ %) | V2 (kgates/ps / %)
1.00GHz | 64/32 | 23.32 / MET | 19.09 / MET / -18.14 | 18.17 / MET / -22.08
 | 64/64 | 26.82 / MET | 22.40 / MET / -16.48 | 21.17 / MET / -21.17
1.25GHz | 64/32 | 33.20 / -75ps | 26.66 / -40ps / -19.70 | 25.81 / -7ps / -22.26
 | 64/64 | 35.41 / -105ps | 32.39 / -50ps / -8.53 | 31.56 / -31ps / -10.87
Notes: set input_delay_ratio 0.3
set_input_delay [expr $clk_period * $input_delay_ratio] -clock CORE_CLK [all_inputs]
set_output_delay [expr 0.1] -clock CORE_CLK [get_ports f1_wdata*]
set_output_delay [expr 0.1] -clock CORE_CLK [get_ports f1_cmp_inv_op]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_data64]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_narr_data64]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_mask8]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_cmp_data4]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_vd_is_mr_mask8]
set_output_delay [expr 0.05] -clock CORE_CLK [get_ports vfmis_vfcsr_flag_set]

## Slide 98: VFMIS64 PPA (2/)
Feq. | XLEN/FLEN | Module | Original | V1 | V2
1.00GHz | 64/32 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 8813.9520 2821.0140 789.7680 2551.6260 786.4920 | 7211.1059 / -18.19% 2440.872 / -13.48% 660.24 / -16.40% 1709.568 / -33.00% 666.288 / -15.28% | 6852.3840 / -22.26% 2412.3960 / -14.48% 615.1320 / -22.11% 1602.7200 / -37.19% 610.5960 / -22.36%
 | 64/64 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 10138.7160 3912.4260 786.6180 2643.9840 779.3100 | 8460.2699 / -16.55% 3500.7840 / -10.52% 676.1160 / -14.05% 1725.8220 / -34.73% 676.6200 / -13.18% | 7999.6139 / -21.10% 3393.8100 / -13.26% 607.9500 / -22.71% 1603.4760 / -39.35% 609.5880 / -21.78%
1.25GHz | 64/32 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 12544.8119 4448.5560 921.9420 3786.5520 902.2860 | 10071.306 / -19.72% 3575.502 / -19.63% 832.608 / -9.69% 2394.378 / -36.77% 874.314 / -3.10% | 9753.2820 / -22.25% 3553.5780 / -20.12% 815.9760 / -11.49% 2291.9400 / -39.47% 817.4880 / -9.40%
 | 64/64 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 13386.4919 5844.8880 859.9500 3352.2300 880.3620 | 12243.9239 / -8.54% 5645.304 / -3.41% 851.256 / -1.01% 2435.454 / -27.35% 877.338 / -0.34% | 11927.0339 / -10.90% 5768.6580 / -1.30% 776.1600 / -9.74% 2235.2400 / -33.32% 834.4980 / -5.21%

## Slide 99: VFMIS64 PPA (3/)
The following RTL SHA-1 are
  Original: master branch b81cf640d
  V1: master branch 96a7f05b8
  V2: master branch 4b13089c3
  V3: separate data FFs for conversion and non-conversion instruction
Synthesis tool: DC v2019.03-sp3
Tech_lib: tcbn28hpcplusbwp30p140ssg0p81vm40c
The following reports has output delay
  Flag output delay is 50ps, outputs in F1 are 100ps and outputs in F2 are 200ps, and then FMIS F2 stage just have 340ps@1.25GHz and 500ps@1.00GHz
Feq. | XLEN/FLEN | Original (kgates/ps) | V1 (kgates/ps/ %) | V2 (kgates/ps / %) | V3 (kgates/ps / %)
1.00GHz | 64/32 | 23.32 / MET | 19.09 / MET / -18.14 | 18.17 / MET / -22.08 | 19.26 / MET / -17.41
 | 64/64 | 26.82 / MET | 22.40 / MET / -16.48 | 21.17 / MET / -21.17 | 22.06 / MET / -17.75
1.25GHz | 64/32 | 33.20 / -75ps | 26.66 / -40ps / -19.70 | 25.81 / -7ps / -22.26 | 27.08 / -17ps / -18.34
 | 64/64 | 35.41 / -105ps | 32.39 / -50ps / -8.53 | 31.56 / -31ps / -10.87 | 31.54 / -23ps / -10.92
Notes: set input_delay_ratio 0.3
set_input_delay [expr $clk_period * $input_delay_ratio] -clock CORE_CLK [all_inputs]
set_output_delay [expr 0.1] -clock CORE_CLK [get_ports f1_wdata*]
set_output_delay [expr 0.1] -clock CORE_CLK [get_ports f1_cmp_inv_op]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_data64]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_narr_data64]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_mask8]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_cmp_data4]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_vd_is_mr_mask8]
set_output_delay [expr 0.05] -clock CORE_CLK [get_ports vfmis_vfcsr_flag_set]

## Slide 100: VFMIS64 PPA (4/)
Feq. | XLEN/FLEN | Module | Original | V1 | V2 | V3
1.00GHz | 64/32 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 8813.9520 2821.0140 789.7680 2551.6260 786.4920 | 7211.1059 / -18.19% 2440.872 / -13.48% 660.24 / -16.40% 1709.568 / -33.00% 666.288 / -15.28% | 6852.3840 / -22.26% 2412.3960 / -14.48% 615.1320 / -22.11% 1602.7200 / -37.19% 610.5960 / -22.36% | 7273.2239 / -17.48% 2551.2480 / -9.56% 621.6840 / -21.28% 1622.2500 / -36.42% 629.6220 / -19.95%
 | 64/64 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 10138.7160 3912.4260 786.6180 2643.9840 779.3100 | 8460.2699 / -16.55% 3500.7840 / -10.52% 676.1160 / -14.05% 1725.8220 / -34.73% 676.6200 / -13.18% | 7999.6139 / -21.10% 3393.8100 / -13.26% 607.9500 / -22.71% 1603.4760 / -39.35% 609.5880 / -21.78% | 8329.9860 / -17.84% 3467.1420 / -11.38% 624.7080 / -20.58% 1619.6040 / -38.74% 627.8580 / -19.43%
1.25GHz | 64/32 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 12544.8119 4448.5560 921.9420 3786.5520 902.2860 | 10071.306 / -19.72% 3575.502 / -19.63% 832.608 / -9.69% 2394.378 / -36.77% 874.314 / -3.10% | 9753.2820 / -22.25% 3553.5780 / -20.12% 815.9760 / -11.49% 2291.9400 / -39.47% 817.4880 / -9.40% | 10233.2159 / -18.43% 3743.5860 / -15.85% 832.7340 / -9.68% 2296.8540 / -39.34% 823.6620 / -8.71%
 | 64/64 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 13386.4919 5844.8880 859.9500 3352.2300 880.3620 | 12243.9239 / -8.54% 5645.304 / -3.41% 851.256 / -1.01% 2435.454 / -27.35% 877.338 / -0.34% | 11927.0339 / -10.90% 5768.6580 / -1.30% 776.1600 / -9.74% 2235.2400 / -33.32% 834.4980 / -5.21% | 11913.2999 / -11.01% 5494.3560 / -6.00% 763.5600 / -11.21% 2245.0680 / -33.03% 790.1460 / -10.25%

## Slide 101: VFMIS64 PPA (5/)
The following RTL SHA-1 are
  Original: master branch b81cf640d
  V3-1: master branch af2d1076d
  V3-2: master branch af2d1076d with FMIS_PWR_REDUCTION macro
Synthesis tool: DC v2019.03-sp3
Tech_lib: tcbn28hpcplusbwp30p140ssg0p81vm40c
The following reports has output delay
  Flag output delay is 50ps, outputs in F1 are 100ps and outputs in F2 are 200ps, and then FMIS F2 stage just have 340ps@1.25GHz and 500ps@1.00GHz
Feq. | XLEN/FLEN | Original (kgates/ps) | V3-1 (kgates/ps / %) | V3-2 (kgates/ps / %)
1.00GHz | 64/32 | 23.32 / MET | 17.67 / MET / -24.23% | 19.26 / MET / -17.41%
 | 64/64 | 26.82 / MET | 20.33 / MET / -24.20% | 22.06 / MET / -17.75%
1.25GHz | 64/32 | 33.20 / -75ps | 24.93 / -19ps / -24.91% | 27.08 / -17ps / -18.34%
 | 64/64 | 35.41 / -105ps | 29.69 / -33ps / -16.15% | 31.54 / -23ps / -10.92%
Notes: set input_delay_ratio 0.3
set_input_delay [expr $clk_period * $input_delay_ratio] -clock CORE_CLK [all_inputs]
set_output_delay [expr 0.1] -clock CORE_CLK [get_ports f1_wdata*]
set_output_delay [expr 0.1] -clock CORE_CLK [get_ports f1_cmp_inv_op]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_data64]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_narr_data64]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_mask8]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_cmp_data4]
set_output_delay [expr 0.2] -clock CORE_CLK [get_ports vfmis_vd_is_mr_mask8]
set_output_delay [expr 0.05] -clock CORE_CLK [get_ports vfmis_vfcsr_flag_set]

## Slide 102: VFMIS64 PPA (6/)
Feq. | XLEN/FLEN | Module | Original | V3-1 | V3-2
1.00GHz | 64/32 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 8813.9520 2821.0140 789.7680 2551.6260 786.4920 | 6668.5500 / -24.34% 2430.5400 / -13.84% 619.7940 / -21.52% 1641.0240 / -35.69% 622.5660 / -20.84% | 7273.2239 / -17.48% 2551.2480 / -9.56% 621.6840 / -21.28% 1622.2500 / -36.42% 629.6220 / -19.95%
 | 64/64 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 10138.7160 3912.4260 786.6180 2643.9840 779.3100 | 7677.0540 / -24.28% 3386.5020 / -13.44% 610.0920 / -22.44% 1610.9100 / -39.07% 619.2900 / -20.53% | 8329.9860 / -17.84% 3467.1420 / -11.38% 624.7080 / -20.58% 1619.6040 / -38.74% 627.8580 / -19.43%
1.25GHz | 64/32 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 12544.8119 4448.5560 921.9420 3786.5520 902.2860 | 9424.4220 / -24.87% 3465.3780 / -22.10% 771.8760 / -16.28% 2397.0240 / -36.70% 802.7460 / -11.03% | 10233.2159 / -18.43% 3743.5860 / -15.85% 832.7340 / -9.68% 2296.8540 / -39.34% 823.6620 / -8.71%
 | 64/64 | vc_vfmis64 fmis_pipe0 fmis_pipe1 fmis_pipe2 fmis_pipe3 | 13386.4919 5844.8880 859.9500 3352.2300 880.3620 | 11220.0479 / -16.18% 5520.4380 / -5.55% 760.5360 / -11.56% 2246.0760 / -33.00% 778.0500 / -11.62% | 11913.2999 / -11.01% 5494.3560 / -6.00% 763.5600 / -11.21% 2245.0680 / -33.03% 790.1460 / -10.25%