## Slide 1
Vector FPU
Ruei-Yuan (2019/6/12)

## Slide 2: Vector FPU
  Support 16-bit (half-precision), 32-bit (single-precision) operations
  Support vector/scalar floating-point instructions
  Fix latency for the vector/scalar floating-point instructions

## Slide 3: Vector FPU

## Slide 4: Vector FPU per Lane (64-bit)
32/16-bit FPU pipeline
32/16-bit FPU pipeline
32/16-bit FPU pipeline
32/16-bit FPU pipeline
[31:0] or {16’b0, [15:0]}
[63:32] or {16’b0, [31:16]}
32’b0 or {16’b0, [47:32]}
32’b0 or {16’b0, [63:48]}
32’b0 or {16’b0, [63:48]}
32’b0 or {16’b0, [47:32]}
[63:32] or {16’b0, [31:16]}
[31:0] or {16’b0, [15:0]}

## Slide 5: Vector FPU Pipeline
32
32/16-bit FMAC Pipeline
32/16-bit FPU MISC/CVT Pipeline
32/16-bit FPU DIV/SQRT Pipeline

## Slide 6: Vector FPU Interface
input [`VRF_MASK_RANGE] vfxxx_clr_bits;
input [1:0] vfxxx_csr_ediv;
input [`EX_CTRL_RANGE] vfxxx_ex_ctrl;
input [`MOP_CNT_RANGE] vfxxx_mop_cnt;
input [`VRF_MASK_RANGE] vfxxx_msk_bits;
input [2:0] vfxxx_rmode;
input [`DATA_RANGE] vfxxx_rs1_data;
input vfxxx_rs1_valid;
input vfxxx_valid;
input [`CSR_LMUL_RANGE] vfxxx_vtype_lmul;
input [`SEW_RANGE] vfxxx_vtype_sew;
input vfxxx_wide; // indicate the widening operation
output [`VRF_MASK_RANGE] vfxxx_mask;
output [`VRF_DATA_RANGE] vfxxx_data;
output [4:0] vfxxx_vfcsr_flag_set;
Note: xxx includes: mac, div, mis

## Slide 7: Vector FPU Pipeline
FPU FMAC pipeline:
  ADD/SUB/MUL/MADD/MSUB/REDSUM/DOT instructions
FPU DIV pipeline:
  DIV/SQRT instructions
FPU MISC/CVT pipeline:
  CMP/MERGE/SIGN/MIN/MAX/CLASS/CVT/REDMAX/REDMIN/MV instructions

## Slide 8: FMAC Pipeline
V2
op1
op2
op3
sub
exp1
exp3
exp2
LZA
St1
Carry
Sum
VF1
VF2
SHIFT
Amount
Calc.
VF3
71-bits Alignment Shift
Stick
Calc.
MUL
St1
3:2
CSA
Sign-detection
HA
carry
HA
carry
HA
sum
CLZ pos
CLZ neg
INV
op2
op1
Hidden1
Gen
op3
Hidden1
Gen
unpacked

## Slide 9: FMAC Pipeline
EXP
Result
St1
Sum
Carry
LZA
ovf
inc
rounding mode
sign
St1
VF3
VF4
Normalization Shifter
<<
Dual-adder
LSB-adder
LSB-adder
LSB-adder
Carry and stick Calc.
4-bit low part adder
Round Decision
5-bit adder
5-bit adder
LSB Correction & special value detection
Select
decision
VF2
Subnorm
EXP result
Result

## Slide 10: DIV Pipeline
div_op1
div_op2
VF1
op1
op2
V2
Subnormal normalization
Subnormal detection
Subnormal normalization
Subnormal detection
div_op2
div_op1
result1
result0
op2
op1
VF1
VF2
V2
Vector
Register
file
VF3
Divider
Subnormal detection & normalization
FSM

## Slide 11: DIV Pipeline
quotient1
quotient0
remainder1
quotient_sel
exp
remainder0
result
rounding mode
VF3
VF4
Result+1
Round Decision
special value
detection
VF2
Subnormal Shifter
>>
adder & stick Gen.
Round & Stick
Special Value Detection

## Slide 12: Convert Instructions
Conversion between FP and Integer
  Integer to FP
    16-bit integer to SP/HP
    Word integer to SP/HP
  FP to Integer
    HP to 16-bit/Word integer
    SP to 16-bit/Word integer
  FP to FP
    SP  HP
    HP  SP
    Bfloat  SP

## Slide 13: Integer to FP (1/)
  Perform two’s complement when input is negative
  Source is Word: bit[43:0]={12’b0, int_num[31:0]}
    Word to SP/HP: rd_exp=31
  Source is 16-bit: bit[43:0]={12’b0, int_num[15:0], 16’b0}
    16-bit to SP/HP: rd_exp=15
  Source is 8-bit: bit[43:0]={12’b0, int_num[7:0], 24’b0}
    8-bit to HP: rd_exp=7
43 | 42 | 41 |  |  | … |  |  | 32 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 |  |  |  | … |  |  |  | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0L | R | [ |  |  |  |  |  |  |  | S |  |  |  |  |  | ]
SP
HP
Word operand
16-bit operand
FP format
12-bit
bit
8-bit operand

## Slide 14: Integer to FP (2/)
  Normalization:
    Count leading zero of bit[31:0] (LZD) (rd_exp’=rd_exp- lzd)
    Left shift 12 bits if target is SP
    Left shift bit[43:0] by lz_num[4:0] (5 level mux)
  Rounding: (25-bit adder needed: bit[44:20])
    Detect Sticky bit (st) (| bit[19:0])
    According to round mode and st, add 1 on LSB or on Round bit
    If bit[44](SP)/bit[32](HP)==1  exp+1, fraction=0
43 | 42 | 41 |  |  | … |  |  | 32 | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 |  |  |  | … |  |  |  | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0L | R | [ |  |  |  |  |  |  |  | S |  |  |  |  |  | ]
SP
HP
Word operand
16-bit operand
FP format
12-bit
bit
8-bit operand

## Slide 15: FP to Integer
To use smaller rounding adder (25-bit):
  Exp<23: rsh (23-exp), Leading 8 bits are 0
    need to be rounded (at least 1bit shifted to bit[7:0])
    Result integer = {8’b0, bit[31:8]}
  23 ≦ Exp ≦ 31: right shift (31-exp),
    no need to be rounded
    Result integer = {bit[31:0]}
8 7 0
8’b0
8 7 0
Round bit
No rounding is needed
31
31
result
result

## Slide 16: FP to 32/16/8 Bit Integer
  Right shift by sh_amount
    0<exp<23: sh_amount = 23-exp, then rounding by 25bit adder
      32bit_int[31:0] ={8’b0,bit[31:8]}
      16bit_int[15:0] = bit[23:8]
      8bit_int[7:0] = bit[15:8]
    exp >= 23: sh_amount = 31-exp, no rounding
      32bit_int[31:0]=bit[31:0]
      16bit_int: exception
      8bit_int: exception
31 | 30 | 29 | 28 |  |  |  |  |  |  |  |  | … |  |  |  |  |  |  |  | 9 | 8 | 7 | 6 | 5 | … | 2 | 1 | 0
23 | 22 | 21 |  |  | S | P |  |  |  |  |  |  |  |  |  |  |  | 3 | 2 | 1 | 0 |  |  |  |  |  |  | 
10 | 9 | 8 | 7 | 6 | H | P | 3 | 2 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | L | R | [ |  | S |  |  | ]
bit
To Rounding 25-bit Adder

## Slide 17: Convert Between SP and HP
SP to HP
  Right shift amount:
  (31-18=13) + (-exp-13) if target result is subnorm
  Rounding (i.e. -13>sp_exp>-25)
HP to SP
  bit[31:0] = {hp[10:0],20’b0}
  Use LZD to left shift subnormal input
31 | 30 | 29 |  |  |  |  |  |  | 18 |  |  |  |  |  |  |  |  |  | 8 | 7 | 6 | 5 | … | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 L | R | [ |  | S |  |  | ]
bit
To be Rounded in 25-bit Adder

## Slide 18: Convert Between SP and Bfloat
SP to Bfloat
  Right shift by 31-15=16 bit (do not detect subnormal)
  Rounding
Bfloat to SP
  sp[31:0] = {bfloat[15:0],16’b0}
31 | 30 | 29 |  |  |  |  |  |  |  |  |  | 15 |  |  |  |  |  |  | 8 | 7 | 6 | 5 | … | 2 | 1 | 0
23 | 22 | 21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 L | R | [ |  | S |  |  | ]
bit
To be rounded in 25-bit Adder

## Slide 19: Convert Instructions uArch
Conversion needs Left Shifter
  Integer to FP
  HP to SP
    left shift when subnormal input, otherwise don’t need shifter
Conversion needs Right Shifter
  FP to Integer
  SP to HP
  SP to Bfloat

## Slide 20: uArch of Convert Instructions
2’s comp.
Normalization (Left shifter)
Alignment (Right shifter)
Shift amount
25-bit adder
Round digit gen
st0
st1
rounding_mode
F2I result
I2F/F2F result
sign
FP2Int/FP Path
Int2FP/HP2SP Path
FP1
FP2
2’s complement
no_round
instr_type
LZD
…

## Slide 21: Reduction Sum Operation (Unordered) per Lane (64-bit)
FMAC pipe0
FMAC pipe2
FMAC pipe0
FMAC pipe0
FMAC pipe1
FMAC pipe2
FMAC pipe3
4T
4T
4T
Vs2[0]
Vs2[1]
Vs2[3]
Vs2[2]
Vs1[0]

## Slide 22: Reduction Sum Operation (Unordered) per Lane
Lane0 | Result(T0) | Result(T1) | Result(T2)
pipe0 | Vs1[0]+Vs2[0] | P0_T0+Vs2[1] | P0_T1+P2_T1
Pipe1 | x | x | x
Pipe2 | Vs2[2]+Vs2[3] | Vs2[2]+Vs2[3] (hold the result) | x
Pipe3 | X | x | x
LMUL=1, T= 4 cycles
Operation: vd[0] = sum( vs2[*] , vs1[0] )

## Slide 23: Reduction Sum Operation per Lane (T0)
V2 stage
Vs1[0]
Vs2[0]
Vs2[2]
Vs2[3]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control

## Slide 24: Reduction Sum Operation per Lane (T1)
Vs2[2]
Vs2[3]
Vs2[1]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[3]
Vs2[0]+Vs1[0]

## Slide 25: Reduction Sum Operation per Lane (T2)
Vs2[3]
Vs2[2]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[2]+Vs2[3]
Vs2[1]+Vs2[0]+Vs1[0]

## Slide 26: Reduction Sum Operation per Lane (T3)
Vs2[2]+Vs2[3]
Vs2[1]+Vs2[0]+Vs1[0]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control

## Slide 27: Reduction Sum Operation (Unordered) per Lane
Lane0 | Result(T0) | Result(T1) | Result(T2)
pipe0 | V4[0]+V8[0] | P0_T0+V5[0] | P0_T1+V6[0]
Pipe1 | x | V4[1]+V5[1] | P1_T1+V6[1]
Pipe2 | x | V4[2]+V5[2] | P2_T1+V6[2]
Pipe3 | x | V4[3]+V5[3] | P3_T1+V6[3]
LMUL>1, T= 4 cycles, e.g.: LMUL=4, and Vs2=V4,V5,V6,V7 and Vs1=V8
Operation: vd[0] = sum( vs2[*] , vs1[0] )

## Slide 28: Reduction Sum Operation (Unordered) per Lane
Lane0 | Result(T3) | Result(T4) | Result(T5)
pipe0 | P0_T2+V7[0] | P0_T3+P1_T3 | P0_T4+P1_T4
Pipe1 | P1_T2+V7[1] | x | x
Pipe2 | P2_T2+V7[2] | P2_T3+P3_T3 | x
Pipe3 | P3_T2+V7[3] | x | x
Operation: vd[0] = sum( vs2[*] , vs1[0] )
LMUL>1, T= 4 cycles, e.g.: LMUL=4, and Vs2=V4,V5,V6,V7 and Vs1=V8

## Slide 29: Reduction Sum Operation (Unordered)
4T*LMUL+8T
Vs1[0]
Vs2[1]
4T
4T
4T
Vs2[N]
.
.
.
Vs1[N]

## Slide 30: Reduction Sum Operation (Unordered) for Lane
 | Result(T0) | Result(T1) | Result(T2) | Result(T3)
Lane0 | L0_T0 | L0_T0+L1_T0 | L0_T1+L2_T1 | L0_T2+L4_T2
Lane1 | L1_T0 | x | x | 
Lane2 | L2_T0 | L2_T0+L3_T0 | x | 
Lane3 | L3_T0 | x | x | 
Lane4 | L4_T0 | L4_T0+L5_T0 | L4_T1+L6_T1 | 
Lane5 | L5_T0 | x | x | 
Lane6 | L6_T0 | L6_T0+L7_T0 | x | 
Lane7 | L7_T0 | x | x | 
LMUL>=1, T0= 4*LMUL + 8 cycles, T1, T2, T3 = 4 cycles

## Slide 31: Reduction Sum Operation (Lane Top)

## Slide 32: Reduction Sum Operation (step1 * LMUL)

## Slide 33: Reduction Sum Operation (step 2)

## Slide 34: Reduction Sum Operation (step 3)

## Slide 35: Reduction Sum Operation (step 4)

## Slide 36: Reduction Sum (Unordered) Instructions Latency
Instruction | Latency
Reduction sum (unordered) | ((Log2(elements)*4) + 4)*LMUL 4*LMUL+4*(log2(512/SEW))

## Slide 37: Reduction Sum Operation (Ordered)
Reuse the unordered logic for the reduction sum ordered operation.

## Slide 38: Reduction Sum Operation per Lane
Vs1[0]
Vs2[0]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
Vs2[2]
Vs2[3]

## Slide 39: Reduction Sum Operation per Lane
Vs2[1]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
Vs2[2]
Vs2[3]
Vs1[0] + Vs2[0]

## Slide 40: Reduction Sum Operation per Lane
Vs1[0] + Vs2[0]+Vs2[1]
Vs2[2]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
Vs2[2]
Vs2[3]

## Slide 41: Reduction Sum Operation per Lane
Vs1[0] + Vs2[0]+Vs2[1]+Vs2[2]
Vs2[3]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
Vs2[2]
Vs2[3]

## Slide 42: Reduction Sum Operation per Lane
Vs1[0] + Vs2[0]+Vs2[1]+Vs2[2]+Vs2[3]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
Vs2[2]
Vs2[3]

## Slide 43: Reduction Sum Operation

## Slide 44: Reduction Sum (Ordered) Instructions Latency
Instruction | Latency
Reduction sum (ordered) | 4*(512/SEW)*LMUL

## Slide 45: Widening Operation
Convert the all source operand (e.g. 16-bit) to 32-bit (single precision) for the widening operation.
Case1: 2*SEW = SEW + SEW
Case2: 2*SEW = 2*SWE + SEW

## Slide 46: Dot Product Operation
Reuse the reduction unordered logic to implement dot product operation.

## Slide 47: Dot Product Operation per Lane
Lane0 | Result(T0) | Result(T1)
pipe0 | Vs2[0]*Vs1[0] | P0_T0+Vd[0]
Pipe1 | Vs2[1]*Vs1[1] | P1_T0+Vd[1]
Pipe2 | x | x
Pipe3 | x | x
T= 4 cycles, the latency is 2T = 8
Operation: Vd[i] = vd[i] + vs1[i] * vs2[i], sew=32 and ediv=1
Lane0 | Result(T0) | Result(T1)
pipe0 | Vs2[0]*Vs1[0] | P0_T0+Vd[0]
Pipe1 | Vs2[1]*Vs1[1] | P1_T0+Vd[1]
Pipe2 | Vs2[2]*Vs1[2] | P2_T0+Vd[2]
Pipe3 | Vs2[3]*Vs1[3] | P3_T0+Vd[3]
T= 4 cycles, the latency is 2T = 8
Operation: Vd[i] = vd[i] + vs1[i] * vs2[i], sew=16 and ediv=1

## Slide 48: Dot Product Operation per Lane
Lane0 | Result(T0) | Result(T1) | Result(T2)
pipe0 | Vs2[0][15: 0]*Vs1[0][15: 0] | P0_T0+P1_T0 | P0_T1+Vd[0][31:0]
Pipe1 | Vs2[0][31:16]*Vs1[0][31:16] | x | x
Pipe2 | Vs2[1][15: 0]*Vs1[1][15: 0] | P2_T0+P3_T0 | P2_T1+Vd[0][31:0]
Pipe3 | Vs2[1][31:16]*Vs1[1][31:16] | x | x
T= 4 cycles, the latency is 3T = 12
Operation: Vd[i] = vd[31:0] + (vs1[31:16] * vs2[31:16]) +
(vs1[15: 0] * vs2[15: 0]), sew=32 and ediv=2

## Slide 49: Dot Product Operation per Lane
Vs2[0][15:0]
Vs1[0][31:16]
Vs2[0][31:16]
Vs1[1][15:0]
Vs2[1][15:0]
Vs2[1][31:16]
Vs1[1][31:16]
Vs2[0][15:0]
FMAC pipeline0
FMAC pipeline3
op1
op2
FMAC pipeline1
FMAC pipeline2
op1
op2
op1
op2
op1
op2
Reduction control

## Slide 50: Dot Product Operation per Lane
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1][31:16] * Vs1[1][31:16]
Vs2[1][15:0] * Vs1[1][15:0]
Vs2[0][31:16] * Vs1[0][31:16]
Vs2[0][15:0] * Vs1[0][15:0]

## Slide 51: Dot Product Operation per Lane
Vd[1][31:0]
Vs2[1]
Vd[0][31:0]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
0
(Vs2[1][31:16] * Vs1[1][31:16]) +
(Vs2[1][15:0] * Vs1[1][15:0])
(Vs2[0][31:16] * Vs1[0][31:16]) +
(Vs2[0][15:0] * Vs1[0][15:0])

## Slide 52: Dot Product Operation per Lane
(Vs2[1][31:16] * Vs1[1][31:16]) +
(Vs2[1][15:0] * Vs1[1][15:0])
+ Vd[1][31:0]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
(Vs2[0][31:16] * Vs1[0][31:16]) +
(Vs2[0][15:0] * Vs1[0][15:0])
+ Vd[0][31:0]

## Slide 53: Instructions Latency
Instruction | Latency
ADD/SUB/MUL/MADD/MUSB | 4 + (LMUL-1)
ADD/SUB/MUL/MADD/MUSB (widening) | 4 + (2*LMUL-1) + 1
DIV/SQRT | 17*LMUL (sew=32, single precision) 10*LMUL (sew=16, half precision)
SGN/CMP/CVT/MAX/MIN/MERGE/MV/CLASS | 2 + (LMUL-1)
DOT (sew=16/32, ediv=1) | 8*LMUL
Reduction sum (unordered) | 4*LMUL+4*log2(512/SEW)
Reduction sum (ordered) | 4*(512/SEW)*LMUL
Reduction min/max | 2*LMUL+2*log2(512/SEW)

## Slide 54: Instructions Throughput
Instruction | Throughput
ADD/SUB/MUL/MADD/MUSB | 1
ADD/SUB/MUL/MADD/MUSB (widening) | 1
DIV/SQRT | 17 ->15->14 10 ->8->7
DOT (sew=16/32, ediv=1) | 8
Reduction sum (unordered) | 4*LMUL+4*log2(512/SEW)
Reduction sum (ordered) | 4*(512/SEW)*LMUL
Reduction min/max | 2*LMUL+2*log2(512/SEW)

## Slide 55
Thank You!

## Slide 56: Misc. Pipeline Instructions
Conversion between FP and Integer
  Integer to FP
    16-bit int to SP/HP
    Word to SP/HP
  FP to Integer
    HP to 16-bit int/Word
    SP to 16-bit int/Word
FP Sign Injection
  FSGNJ, FSGNJN, FSGNJX
FCMP
FMIN_MAX
FCLASS
FMV

## Slide 57: Vector Floating-Point Sign-Injection Instructions
The result takes all bits except the sign bit form the vector vs2 operands.
  The rm (rounding mode) field indicates J[N]/JX
For vfsgnj, the result’s sign bit is v/rs1’s sign bit.
Vfsgnj.vv vd, vs2, vs1, vm # Vector-vector vd[i] = {vs1[i].MSB, vs2[i]}
Vfsgnj.vf vd, vs2 , rs1, vm # Vector-scalar vd[i] = {f[rs1].MSB, vs2[i]}
For vfsgjn, the result’s sign bit is the opposite of v/rs1’s sign bit.
Vfsgjn.vv vd, vs2 , vs1, vm # Vector-vector vd[i] = {~vs1[i].MSB, vs2[i]}
Vfsgjn.vf vd, vs2 , rs1, vm # Vector-scalar vd[i] = {~f[rs1].MSB, vs2[i]}
For vfsgnjx, the sign bit is the XOR of the sign bits of v/rs1 and vs2.
Vfsgnjx.vv vd, vs2 , vs1, vm # Vector-vector vd[i] = {vs2[i].MSB ^ vs1[i].MSB, vs2[i]}
Vfsgnjx.vf vd, vs2 , rs1, vm # Vector-vector vd[i] = {vs2[i].MSB ^ f[rs1].MSB, vs2[i]}

## Slide 58: Vector Floating-Point Compare Instructions
Write the comparison result to a mask register (not necessarily V0).
Compare equal
Vfeq.vv vd, vs2, vs1, vm # Vector-vector vd[i] = (vs2[i] == vs1[i])
Vfeq.vf vd, vs2 , rs1, vm # Vector-scalar vd[i] = (vs2[i] == f[rs1])
Compare not equal
Vfne.vv vd, vs2, vs1, vm # Vector-vector vd[i] = (vs2[i] != vs1[i])
Vfne.vf vd, vs2 , rs1, vm # Vector-scalar vd[i] = (vs2[i] != f[rs1])
Compare less than
Vflt.vv vd, vs2, vs1, vm # Vector-vector vd[i] = (vs2[i] < vs1[i])
Vflt.vf vd, vs2 , rs1, vm # Vector-scalar vd[i]. = (vs2[i] < f[rs1])

## Slide 59: Vector Floating-Point Compare Instructions
Compare less than or equal
Vfle.vv vd, vs2, vs1, vm # Vector-vector vd[i].LSB = (vs2[i] <= vs1[i])
Vfle.vf vd, vs2 , rs1, vm # Vector-scalar vd[i].LSB = (vs2[i] <= f[rs1])
Compare greater than
Vfgt.vf vd, vs2 , rs1, vm # Vector-scalar vd[i].LSB = (vs2[i] > vs1[i])
Compare greater than or equal
Vfge.vf vd, vs2 , rs1, vm # Vector-scalar vd[i].LSB = (vs2[i] >= f[rs1])

## Slide 60: Vector Floating-Point Compare Instructions

## Slide 61: Vector Floating-Point Compare Instructions
This feature is removed from RISC-V spec.
To help implement the C99 floating-point comparison functions, a vford instruction is added that sets a mask register if the arguments are ordered.
  One of the source operands is treated as NaNs, result should be 0 (unordered).
Vford.vv vd, vs2, vs1, vm # Vector-vector
Vford.vf vd, vs2, rs1, vm # Vector-scalar

## Slide 62: Vector Floating-Point MIN/MAX Instructions
Floating-point minimum
Vfmin.vv vd, vs2, vs1, vm #Vector-vector vd[i] = min (vs2[i], vs1[i])
Vfmin.vf vd, vs2, rs1, vm # Vector-scalar vd[i] = min (vs2[i], f[rs1])
Floating-point maximum
Vfmax.vv vd, vs2, vs1, vm # Vector-vector vd[i] = max (vs2[i], vs1[i])
Vfmax.vf vd, vs2, rs1, vm # Vector-scalar vd[i] = max (vs2[i], f[rs1])

## Slide 63: FMIN and FMAX Instructions
FMIN-MAX
  The rm field indicates MIN/MAX
  FMIN: Write the smaller of rs1 and rs2 to rd
  FMAX: Write the larger of rs2 and rs2 to rd
  The value −0.0 is considered to be less than the value +0.0.
  Both inputs are NaNs, the result is the canonical NaN.
  Only one operand is a NaN, the result is the non-NaN operand.
  Signaling NaN inputs raise the invalid operation exception, even when the result is not NaN.

## Slide 64: Vector Floating-Point Classify Instruction
Vfclass.v vd, vs2, vm # Vector-vector vd[i] = classify(vs2[i])
The 10-bit mask produced by this instruction is placed in the LSB of the result elements.
This instruction is only defined for SEW=16b above, so the result will always fit in the destination elements.

## Slide 65: Vector Floating-Point Merge Instruction
Mask (vm=0):
  Vfmerge.vf vd, vs2, rs1, v0.t # vd[i] = v0[i].LSB ? f[rs1] : vs2[i]
  All elements should be written back
Unmask (vm=1)
  Vfmerge.vf vd, v0, rs1 # vd[i] = f[rs1]
    The instruction must have the vs2 field set to v0, with all other values for vs2 reserved.
    Pseudo instruction vmv.v.f vd, rs1 which expands to vfmerge.vf vd, v0, rs1

## Slide 66: Floating-Point Scalar Move Instructions
The floating-point scalar read/write instructions transfer a single value between a scalar f register and element 0 of as vector register. The instructions ignore LMUL and vector register groups.
Vfmv.f.s rd, vs2 # rd = vs2[0] (rs1=0)
If SEW > FLEN, the least-significant FLEN bits are transferred and the upper SEW-FLEN bits are ignored. If SEW < FLEN, the value is NaN-boxed (1-extended) to FLEN bits.
Vfmv.s.f vd, rs1 # vd[0] = rs1 (vs2=0)
If SEW < FLEN, the least-significant bits are copied and the upper XLEN-SEW bits are ignored. If SEW > FLEN, the value is NaN-boxed (1-extended) to SEW bits.
The other elements in the destination vector register ( 0 < index < VLEN/SEW) are zeroed. If vl=0, no operation is performed and the destination register is not updated.

## Slide 67
Backup slides

## Slide 68: FMAC Pipeline (subnormal output detection)
Before normalization shifter:
  Case1 (EXP>-126): 0.0001xxx*2^100
    LZA result (4) for normalization shifter
    After normalization 1.xxx*2^96
  Case2 (EXP>-126): result 0.0001xxx*2^-125
    LZA result (4) for normalization shifter
    After normalization 1.xxx*2^-129
  Case3 (EXP<-126): result 0.0001xxx*2^-130
    LZA result (4) for normalization shifter
    After normalization 1.xxx*2^-134

## Slide 69: FMAC Pipeline (proposed subnormal output detection)
Example:
  Case1: 0.0001xxx*2^100
    EXP(100) and (EXP(100) – LZA(4) =96) > -126
    Select 4 (LZA result) for normalization shifter
    After normalization 1.xxx*2^96
  Case2: result 0.0001xxx*2^-125
    EXP(-125) > -126 and (EXP(-125) – LZA(4) =-129) < -126
    Select 1 (EXP(-125) + 126) for normalization shifter
    After normalization 0.001xxx*2^-127
  Case3: result 0.0001xxx*2^-127
    EXP(-127) < -126
    Select 0 for normalization shifter
    After normalization 0.0001xxx*2^-127

## Slide 70: FMAC Pipeline (subnormal output)
EXP
Result
St1
Sum
Carry
LZA
ovf
inc
rounding mode
sign
St1
VF3
VF4
Normalization Shifter
<<
Dual-adder
LSB-adder
LSB-adder
LSB-adder
Carry and stick Calc.
4-bit low part adder
Round Decision
5-bit adder
5-bit adder
LSB Correction & special value detection
Select
decision
VF2
Subnorm?
EXP result
Result

## Slide 71: FMAC Pipeline(proposed subnormal output detection)
Final EXP?
Subnormal?
if (EXP < -126)
select 0
else if (EXP-LZA) < -126
select EXP + 126
else
select LZA
0
126
Sum
Carry
LZA
VF3
Normalization Shifter
<<
VF2
EXP
EXP-LZA
adder
Subnormal
predict
VF4

## Slide 72: FMAC Pipeline (subnormal output)
EXP
Result
St1
Sum
Carry
LZA
ovf
inc
rounding mode
sign
St1
VF3
VF4
Normalization Shifter
<<
Dual-adder
LSB-adder
LSB-adder
LSB-adder
Carry and stick Calc.
4-bit low part adder
Round Decision
5-bit adder
5-bit adder
LSB Correction & special value detection
Select
decision
VF2
Subnorm?
EXP result
Result

## Slide 73: FMAC Pipeline (proposed subnormal output detection)
Corner case:
  Case4: result 0.1111…*2^-127 (maximum subnormal value)
    EXP(-127) < -126
    Select 0 for normalization shifter
    After normalization 0.1111…*2^-127
    If the final result‘s (fraction) MSB is 1 (e.g.: 1.0000…) after rounding, it the EXP will be modified from 0 to -126 for 1.0000…*2^-126 (minimum normalization value)

## Slide 74: FMAC Pipeline(proposed subnormal output detection)
-126
0
if (EXP < -126)
select 0
else if (EXP-LZA) < -126
select EXP + 126
else
select LZA
0
126
Sum
Carry
LZA
VF3
Normalization Shifter
<<
VF2
EXP
EXP-LZA
adder
Subnormal
predict
Result MSB
Subnormal
detection
if (subnormal & Result MSB==0)
select 0
else if (subnormal & Result MSB==1)
select -126
else
select (EXP-LZA)
EXP result
VF4