## Slide 1
Vector FPU
Ruei-Yuan (2019/6/12)

## Slide 2: Vector FPU
  Support 16-bit (half-precision), 32-bit (single-precision) operations
  Support vector/scalar floating-point instructions
  Fix latency for the vector/scalar floating-point instructions

## Slide 3: Vector FPU
V2
V1
II

## Slide 4: Vector FPU

## Slide 5: Vector FPU per Lane (64-bit)
32/16-bit FPU pipeline
32/16-bit FPU pipeline
32/16-bit FPU pipeline
32/16-bit FPU pipeline
[31:0] or {16’b0, [15:0]}
[63:32] or {16’b0, [31:16]}
32’b0 or {16’b0, [47:32]}
32’b0 or {16’b0, [63:48]}
32’b0 or {16’b0, [63:48]}
32’b0 or {16’b0, [47:32]}
[63:32] or {16’b0, [31:16]}
[31:0] or {16’b0, [15:0]}

## Slide 6: Vector FPU Pipeline
32
32/16-bit FMAC Pipeline
32/16-bit FPU MISC/CVT Pipeline
32/16-bit FPU DIV/SQRT Pipeline

## Slide 7: Vector FPU Interface
input [`VRF_MASK_RANGE] vfxxx_clr_bits;
input [1:0] vfxxx_csr_ediv;
input [`EX_CTRL_RANGE] vfxxx_ex_ctrl;
input [`MOP_CNT_RANGE] vfxxx_mop_cnt;
input [`VRF_MASK_RANGE] vfxxx_msk_bits;
input [2:0] vfxxx_rmode;
input [`DATA_RANGE] vfxxx_rs1_data;
input vfxxx_rs1_valid;
input vfxxx_valid;
input [`CSR_LMUL_RANGE] vfxxx_vtype_lmul;
input [`SEW_RANGE] vfxxx_vtype_sew;
Input vfxxx_wide; // indicate the widening operation
output [`VRF_MASK_RANGE] vfxxx_mask;
output [`VRF_DATA_RANGE] vfxxx_data;
output [4:0] vfxxx_vfcsr_flag_set;
Note: xxx includes: mac, div, mis

## Slide 8: Vector FPU Pipeline
FPU FMAC pipeline: ADD/SUB/MUL/MADD/MSUB/REDSUM/DOT instructions
FPU DIV pipeline: DIV/SQRT instructions
FPU MISC/CVT pipeline: CMP/MERGE/SIGN/MIN/MAX/CLASS/CVT/REDMAX/REDMIN/MV instructions

## Slide 9: FMAC Pipeline (subnormal input)
V2
op1
op2
op3
sub
exp1
exp3
exp2
LZA
St1
Carry
Sum
VF1
VF2
SHIFT
Amount
Calc.
VF3
71-bits Alignment Shift
Stick
Calc.
MUL
St1
3:2
CSA
Sign-detection
HA
carry
HA
carry
HA
sum
CLZ pos
CLZ neg
INV
op2
op1
Hidden1
Gen
op3
Hidden1
Gen
unpacked

## Slide 10: FMAC Pipeline (unpacked logic)
Unpacked logic includes:
  16-bit unpacked
  32-bit unpacked

## Slide 11: FMAC Pipeline (subnormal output)
EXP
Result
St1
Sum
Carry
LZA
ovf
inc
rounding mode
sign
St1
VF3
VF4
Normalization Shifter
<<
Dual-adder
LSB-adder
LSB-adder
LSB-adder
Carry and stick Calc.
4-bit low part adder
Round Decision
5-bit adder
5-bit adder
LSB Correction & special value detection
Select
decision
VF2
Subnorm?
EXP result
Result

## Slide 12: FMAC Pipeline (subnormal output detection)
Before normalization shifter:
  Case1 (EXP>-126): 0.0001xxx*2^100
    LZA result (4) for normalization shifter
    After normalization 1.xxx*2^96
  Case2 (EXP>-126): result 0.0001xxx*2^-125
    LZA result (4) for normalization shifter
    After normalization 1.xxx*2^-129
  Case3 (EXP<-126): result 0.0001xxx*2^-130
    LZA result (4) for normalization shifter
    After normalization 1.xxx*2^-134

## Slide 13: FMAC Pipeline (proposed subnormal output detection)
Example:
  Case1: 0.0001xxx*2^100
    EXP(100) and (EXP(100) – LZA(4) =96) > -126
    Select 4 (LZA result) for normalization shifter
    After normalization 1.xxx*2^96
  Case2: result 0.0001xxx*2^-125
    EXP(-125) > -126 and (EXP(-125) – LZA(4) =-129) < -126
    Select 1 (EXP(-125) + 126) for normalization shifter
    After normalization 0.001xxx*2^-127
  Case3: result 0.0001xxx*2^-127
    EXP(-127) < -126
    Select 0 for normalization shifter
    After normalization 0.0001xxx*2^-127

## Slide 14: FMAC Pipeline (subnormal output)
EXP
Result
St1
Sum
Carry
LZA
ovf
inc
rounding mode
sign
St1
VF3
VF4
Normalization Shifter
<<
Dual-adder
LSB-adder
LSB-adder
LSB-adder
Carry and stick Calc.
4-bit low part adder
Round Decision
5-bit adder
5-bit adder
LSB Correction & special value detection
Select
decision
VF2
Subnorm?
EXP result
Result

## Slide 15: FMAC Pipeline(proposed subnormal output detection)
Final EXP?
Subnormal?
if (EXP < -126)
select 0
else if (EXP-LZA) < -126
select EXP + 126
else
select LZA
0
126
Sum
Carry
LZA
VF3
Normalization Shifter
<<
VF2
EXP
EXP-LZA
adder
Subnormal
predict
VF4

## Slide 16: FMAC Pipeline (subnormal output)
EXP
Result
St1
Sum
Carry
LZA
ovf
inc
rounding mode
sign
St1
VF3
VF4
Normalization Shifter
<<
Dual-adder
LSB-adder
LSB-adder
LSB-adder
Carry and stick Calc.
4-bit low part adder
Round Decision
5-bit adder
5-bit adder
LSB Correction & special value detection
Select
decision
VF2
Subnorm?
EXP result
Result

## Slide 17: FMAC Pipeline (proposed subnormal output detection)
Corner case:
  Case4: result 0.1111…*2^-127 (maximum subnormal value)
    EXP(-127) < -126
    Select 0 for normalization shifter
    After normalization 0.1111…*2^-127
    If the final result‘s (fraction) MSB is 1 (e.g.: 1.0000…) after rounding, it the EXP will be modified from 0 to -126 for 1.0000…*2^-126 (minimum normalization value)

## Slide 18: FMAC Pipeline(proposed subnormal output detection)
-126
0
if (EXP < -126)
select 0
else if (EXP-LZA) < -126
select EXP + 126
else
select LZA
0
126
Sum
Carry
LZA
VF3
Normalization Shifter
<<
VF2
EXP
EXP-LZA
adder
Subnormal
predict
Result MSB
Subnormal
detection
if (subnormal & Result MSB==0)
select 0
else if (subnormal & Result MSB==1)
select -126
else
select (EXP-LZA)
EXP result
VF4

## Slide 19: DIV Pipeline
div_op1
div_op2
VF1
op1
op2
V2
Subnormal normalization
Subnormal detection
Subnormal normalization
Subnormal detection
div_op2
div_op1
result1
result0
op2
op1
VF1
VF2
V2
Vector
Register
file
VF3
Divider
Subnormal detection & normalization
FSM

## Slide 20: DIV Pipeline
quotient1
quotient0
remainder1
quotient_sel
exp
remainder0
result
rounding mode
VF3
VF4
Result+1
Round Decision
special value
detection
VF2
Subnormal Shifter
>>
adder & stick Gen.
Round & Stick
Special Value Detection

## Slide 21: Reduction Sum Operation (Unordered) per Lane (64-bit)
FMAC pipe0
FMAC pipe2
FMAC pipe0
FMAC pipe0
FMAC pipe1
FMAC pipe2
FMAC pipe3
4T
4T
4T
Vs2[0]
Vs2[1]
Vs2[3]
Vs2[2]
Vs1[0]

## Slide 22: Reduction Sum Operation (Unordered) per Lane
Lane0 | Result(T0) | Result(T1) | Result(T2)
pipe0 | Vs1[0]+Vs2[0] | P0_T0+Vs2[1] | P0_T1+P2_T1
Pipe1 | x | x | x
Pipe2 | x | Vs2[2]+Vs2[3] | x
Pipe3 | x | x | x
LMUL=1, T= 4 cycles
Operation: vd[0] = sum( vs2[*] , vs1[0] )

## Slide 23: Widening Reduction Sum Operation (Unordered) per Lane
Lane0 | Result(T0) mop0 | Result(T1) mop0 | Result(T2) mop1 | Result(T2) mop1
pipe0 | Vs1[0]+Vs2[0] | P0_T0+Vs2[1] | P0_T1+Vs2[2] | P0_T2+Vs2[3]
Pipe1 | x | x | x | 
Pipe2 | x | x | x | 
Pipe3 | x | x | x | 
LMUL=1, T= 4 cycles
The widening reduction sum (unordered) will be decomposed to the micro-instructions
Operation: vd[0] = sum( vs2[*] , vs1[0] )

## Slide 24: Reduction Sum Operation per Lane
V2 stage
Vs1[0]
Vs2[0]
Vs2[2]
Vs2[3]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control

## Slide 25: Reduction Sum Operation per Lane
Vs2[1]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[3]
Vs2[3]
Vs2[2] + Vs2[3]
Vs2[1]
Vs2[0]+Vs1[0]

## Slide 26: Reduction Sum Operation per Lane
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[2]+Vs2[3]
Vs2[1]+Vs2[0]+Vs1[0]

## Slide 27: Reduction Sum Operation per Lane
Vs2[2]+Vs2[3]
Vs2[1]+Vs2[0]+Vs1[0]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control

## Slide 28: Reduction Sum Operation (Unordered) per Lane
Lane0 | Result(T0) | Result(T1) | Result(T2)
pipe0 | V4[0]+V8[0] | P0_T0+V5[0] | P0_T1+V6[0]
Pipe1 | x | V4[1]+V5[1] | P1_T1+V6[1]
Pipe2 | x | V4[2]+V5[2] | P2_T1+V6[2]
Pipe3 | x | V4[3]+V5[3] | P3_T1+V6[3]
LMUL>1, T= 4 cycles, e.g.: LMUL=4, and Vs2=V4,V5,V6,V7 and Vs1=V8
Operation: vd[0] = sum( vs2[*] , vs1[0] )

## Slide 29: Reduction Sum Operation (Unordered) per Lane
Lane0 | Result(T3) | Result(T4) | Result(T5)
pipe0 | P0_T2+V7[0] | P0_T3+P1_T3 | P0_T4+P1_T4
Pipe1 | P1_T2+V7[1] | x | x
Pipe2 | P2_T2+V7[2] | P2_T3+P3_T3 | x
Pipe3 | P3_T2+V7[3] | x | x
Operation: vd[0] = sum( vs2[*] , vs1[0] )
LMUL>1, T= 4 cycles, e.g.: LMUL=4, and Vs2=V4,V5,V6,V7 and Vs1=V8

## Slide 30: Reduction Sum Operation (Unordered)
4T*LMUL+8T
Vs1[0]
Vs2[1]
4T
4T
4T
Vs2[N]
.
.
.
Vs1[N]

## Slide 31: Reduction Sum Operation (Unordered) for Lane
 | Result(T0) | Result(T1) | Result(T2) | Result(T3)
Lane0 | L0_T0 | L0_T0+L1_T0 | L0_T1+L2_T1 | L0_T2+L4_T2
Lane1 | L1_T0 | x | x | 
Lane2 | L2_T0 | L2_T0+L3_T0 | x | 
Lane3 | L3_T0 | x | x | 
Lane4 | L4_T0 | L4_T0+L5_T0 | L4_T1+L6_T1 | 
Lane5 | L5_T0 | x | x | 
Lane6 | L6_T0 | L6_T0+L7_T0 | x | 
Lane7 | L7_T0 | x | x | 
LMUL>=1, T0= 4*LMUL + 8 cycles, T1, T2, T3 = 4 cycles

## Slide 32: Reduction Sum Operation

## Slide 33: Reduction Sum Operation (step1 * LMUL)

## Slide 34: Reduction Sum Operation (step 2)

## Slide 35: Reduction Sum Operation (step 3)

## Slide 36: Reduction Sum Operation (step 4)

## Slide 37: Reduction Sum (Unordered) Instructions Latency
Instruction | Latency (sew=16)
Reduction sum (unordered) | ((Log2(elements)*4) + 4)*LMUL 4*LMUL+20
Instruction | Latency (sew=32)
Reduction sum (unordered) | (Log2(elements)*4)*LMUL 4*LMUL+16

## Slide 38: Reduction Sum Operation (Ordered)
Reuse the unordered logic for the reduction sum ordered operation.

## Slide 39: Reduction Sum Operation per Lane
Vs1[0]
Vs2[0]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
Vs2[2]
Vs2[3]

## Slide 40: Reduction Sum Operation per Lane
Vs2[1]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
Vs2[2]
Vs2[3]
Vs1[0] + Vs2[0]

## Slide 41: Reduction Sum Operation per Lane
Vs1[0] + Vs2[0]+Vs2[1]
Vs2[2]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
Vs2[2]
Vs2[3]

## Slide 42: Reduction Sum Operation per Lane
Vs1[0] + Vs2[0]+Vs2[1]+Vs2[2]
Vs2[3]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
Vs2[2]
Vs2[3]

## Slide 43: Reduction Sum Operation per Lane
Vs1[0] + Vs2[0]+Vs2[1]+Vs2[2]+Vs2[3]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
Vs2[2]
Vs2[3]

## Slide 44: Reduction Sum Operation

## Slide 45: Reduction Sum (Ordered) Instructions Latency
Instruction | Latency (sew=16)
Reduction sum (ordered) | 4*32*LMUL
Instruction | Latency (sew=32)
Reduction sum (ordered) | 4*16*LMUL

## Slide 46: Widening Operation
Convert the all source operand (e.g. 16-bit) to 32-bit (single precision) for the widening operation.
Case1: 2*SEW = SEW + SEW
Case2: 2*SEW = 2*SWE + SEW

## Slide 47: Dot Product Operation
Reuse the reduction unordered logic to implement dot product operation.

## Slide 48: Dot Product Operation per Lane
Lane0 | Result(T0) | Result(T1)
pipe0 | Vs2[0]*Vs1[0] | P0_T0+Vd[0]
Pipe1 | Vs2[1]*Vs1[1] | P1_T0+Vd[1]
Pipe2 | x | x
Pipe3 | x | x
T= 4 cycles, the latency is 2T = 8
Operation: Vd[i] = vd[i] + vs1[i] * vs2[i], sew=32 and ediv=1
Lane0 | Result(T0) | Result(T1)
pipe0 | Vs2[0]*Vs1[0] | P0_T0+Vd[0]
Pipe1 | Vs2[1]*Vs1[1] | P1_T0+Vd[1]
Pipe2 | Vs2[2]*Vs1[2] | P2_T0+Vd[2]
Pipe3 | Vs2[3]*Vs1[3] | P3_T0+Vd[3]
T= 4 cycles, the latency is 2T = 8
Operation: Vd[i] = vd[i] + vs1[i] * vs2[i], sew=16 and ediv=1

## Slide 49: Dot Product Operation per Lane
Lane0 | Result(T0) | Result(T1) | Result(T2)
pipe0 | Vs2[0][15: 0]*Vs1[0][15: 0] | P0_T0+P1_T0 | P0_T1+Vd[0][31:0]
Pipe1 | Vs2[0][31:16]*Vs1[0][31:16] | x | x
Pipe2 | Vs2[1][15: 0]*Vs1[1][15: 0] | P2_T0+P3_T0 | P2_T1+Vd[0][31:0]
Pipe3 | Vs2[1][31:16]*Vs1[1][31:16] | x | x
T= 4 cycles, the latency is 3T = 12
Operation: Vd[i] = vd[31:0] + (vs1[31:16] * vs2[31:16]) +
(vs1[15: 0] * vs2[15: 0]), sew=32 and ediv=2

## Slide 50: Dot Product Operation per Lane
Vs2[0][15:0]
Vs1[0][31:16]
Vs2[0][31:16]
Vs1[1][15:0]
Vs2[1][15:0]
Vs2[1][31:16]
Vs1[1][31:16]
Vs2[0][15:0]
FMAC pipeline0
FMAC pipeline3
op1
op2
FMAC pipeline1
FMAC pipeline2
op1
op2
op1
op2
op1
op2
Reduction control

## Slide 51: Dot Product Operation per Lane
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1][31:16] * Vs1[1][31:16]
Vs2[1][15:0] * Vs1[1][15:0]
Vs2[0][31:16] * Vs1[0][31:16]
Vs2[0][15:0] * Vs1[0][15:0]

## Slide 52: Dot Product Operation per Lane
Vd[1][31:0]
Vs2[1]
Vd[0][31:0]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
Vs2[1]
0
(Vs2[1][31:16] * Vs1[1][31:16]) +
(Vs2[1][15:0] * Vs1[1][15:0])
(Vs2[0][31:16] * Vs1[0][31:16]) +
(Vs2[0][15:0] * Vs1[0][15:0])

## Slide 53: Dot Product Operation per Lane
(Vs2[1][31:16] * Vs1[1][31:16]) +
(Vs2[1][15:0] * Vs1[1][15:0])
+ Vd[1][31:0]
FMAC pipeline0
FMAC pipeline3
op1
op3
FMAC pipeline1
FMAC pipeline2
op1
op3
op1
op3
op1
op3
Reduction control
(Vs2[0][31:16] * Vs1[0][31:16]) +
(Vs2[0][15:0] * Vs1[0][15:0])
+ Vd[0][31:0]

## Slide 54: Instructions Latency
Instruction | Latency
ADD/SUB/MUL/MADD/MUSB | 4 + (LMUL-1)
DIV/SQRT | 17*LMUL (sew=32, single precision) 10*LMUL (sew=16, half precision)
DOT (sew=16/32, ediv=1) | 8*LMUL
DOT (sew=32, ediv=2) | 12*LMUL
Reduction sum (unordered) | 4*LMUL+4*log2(512/SEW)
Reduction sum (ordered) | 4*(512/SEW)*LMUL