## Slide 1: Panther Bus Interface
Driving Innovations™
Kane
2015-10-08

## Slide 2: Basic Structure
Instruction and Data channel
  AXI4 x2
  Configurable address width: 24 to 64 bits
  Data width: 64-bit
Synchronous bus clock domain
  Clock phase enable signal
  Synchronous FIFO
Snoop Channel
axi_wrapper
ahb
ocp
biu_path
sync_fifo
bus clk domain
core clk domain
SCU

## Slide 3: Requirement
Cacheability indication
  Use “C” field from $MR3 (TLB_DATA)
  Translate to output AR/WCACHE[3:0] for memory type encoding (AXI4)

## Slide 4: Requirement - 2
Interface change between BIU and other internal modules
  Add wait-cycle to return data phase
    ready-valid (ack) handshaking protocol
  Pros:
    Other internal modules don’t have to receive the response data immediately (when “ack” is asserted)
    No pre-allocated buffer is needed for each module, reduce area overhead
  Cons:
    The return data has to be kept in BIU, one extra buffer is needed for BIU

## Slide 5: Requirement - 3
BIU
Snoop channel for ACU
  How to cancel WB command/data queue entry after hit by snoop
    In-queue
    Not observed by AXI interface (not top)
LSU
SCU
wb_fifo_0
wb_fifo_1
wb_fifo_2
wb_fifo_3
ACU
Provide snoop data
cmd/data
lsu_wb_0
lsu_wb_1
lsu_wb_2
lsu_wb_3
Cancel FIFO entry