## Slide 1: biu_sync_fifo enhancement for the bus half-cycle transition
Driving Innovations™
Ruei-Yuan Jou
2017-06-06

## Slide 2: Bus half-cycle transition
The read data of biu_sync_fifo may be changed at the bus half-cycle causing the haddr toggling .
Biu_sync_fifo
Biu_ahb_wrapper

## Slide 3: Original biu_sync_fifo
wr_ptr
wr_data
rd_ptr
rd_data
core_clk
bus_clk
FIFO

## Slide 4: Enhanced biu_sync_fifo
wr_ptr
wr_data
rd_ptr
rd_data
bypass_wr_data
core_clk
bus_clk
bypass_wr_data = wr & (wr_ptr == next_rd_ptr)
FIFO
bus_clk

## Slide 5: Back to back write data (1:1 ratio)
Bus has zero wait cycle.

## Slide 6: Back to back write data (1:1 ratio)
Bus has wait cycle.

## Slide 7: Back to back write data (2:1 ratio)
The first wr_data is written when the wr_estrb is 0.

## Slide 8: Back to back write data (2:1 ratio)
The first wr_data is written when the wr_estrb is 1.

## Slide 9: Back to back write data (2:1 ratio)
The first wr_data is written when the wr_estrb is 1.
The bus has wait cycle.

## Slide 10: RTL code changes in biu_sync_fifo
assign bypass_wr_data = wr & (wr_ptr == next_rd_ptr);
assign rd_data_nx = bypass_wr_data ? wr_data : mem[next_rd_ptr[POINTER_INDEX_WIDTH-2:0]];
always @(negedge r_reset_n or posedge r_clk)
begin
if (!r_reset_n)
rd_data <= {(DATA_WIDTH){1'b0}};
else
rd_data <= rd_data_nx;
end

## Slide 11: Synthesis result
GW_config8 (500Mhz, TSMC40nm) | Original design | After design enhancement
Performance | 1 | 1
Timing | -8ps | No timing violation
Bus half-cycle transition | Yes | No
Area | 1 | 1+0.6k~0.9k

## Slide 12
Thank You!