## Slide 1: AXI RAW FIFO
Along

## Slide 2: Introduction
AXI 6 entries RAW FIFO
The newer write information will push to the smallest number entry and shift the others.
The FIFO will shift(only shift the smaller than match entry) and kill the oldest match entry.

## Slide 3
assign raw_match[0] = (raw_queue0_id == bid) & raw_queue0_valid & bvalid;
assign raw_addr_match[0] = (raw_queue0_addr[11:5] == addr_out[11:5]) & raw_queue0_valid & ~write_out;
assign raw_valid[0] = raw_queue0_valid;
assign raw_queue0_id_nx = awid_nx;
assign raw_queue0_valid_nx = a_wcmd_en;
assign raw_queue0_addr_nx = awaddr_nx[11:5];
assign raw_queue0_enable = bus_clk_en & ((a_wcmd_en & (|(~raw_valid & 6'b111111))) | (b_ch_taken & (|(raw_match & 6'b111111))));
always @(posedge core_clk or negedge core_reset_n) begin
if (!core_reset_n) begin
raw_queue0_valid <= 1'b0;
raw_queue0_id <= {(BIU_ID_WIDTH){1'b0}};
raw_queue0_addr <= 7'b0;
end
else if (raw_queue0_enable) begin
raw_queue0_valid <= raw_queue0_valid_nx;
raw_queue0_id <= raw_queue0_id_nx;
raw_queue0_addr[11:5] <= raw_queue0_addr_nx[11:5];
end
end
The newer store can be save if any queues are not valid.
The oldest store with ID match should be cleared.

## Slide 4
assign raw_match[1] = (raw_queue1_id == bid) & raw_queue1_valid & bvalid;
assign raw_addr_match[1] = (raw_queue1_addr[11:5] == addr_out[11:5]) & raw_queue1_valid & ~write_out;
assign raw_valid[1] = raw_queue1_valid;
assign raw_queue1_id_nx = raw_queue0_id;
assign raw_queue1_valid_nx = raw_queue0_valid & ~(raw_match[0] & ~(|(raw_match & 6'b111110)));
assign raw_queue1_addr_nx = raw_queue0_addr;
assign raw_queue1_enable = bus_clk_en & ((a_wcmd_en & (|(~raw_valid & 6'b111110))) | (b_ch_taken & (|(raw_match & 6'b111110))));
always @(posedge core_clk or negedge core_reset_n) begin
if (!core_reset_n) begin
raw_queue1_valid <= 1'b0;
raw_queue1_id <= {(BIU_ID_WIDTH){1'b0}};
raw_queue1_addr <= 7'b0;
end
else if (raw_queue1_enable) begin
raw_queue1_valid <= raw_queue1_valid_nx;
raw_queue1_id <= raw_queue1_id_nx;
raw_queue1_addr[11:5] <= raw_queue1_addr_nx[11:5];
end
end
Case1: aw channel only
Case2: b channel only
raw_match[0/1]=1
raw_queue1_valid_nx=1
raw_queue0_valid_nx=0
Case3: aw and b taken
raw_match[0/1]=1
raw_queue1_valid_nx=1
raw_queue0_valid_nx=1
The young store should be shift if any older store matches.

## Slide 5: Newer Store arrived
raw_valid[0] 1 | raw_valid[1] 1 | raw_valid[2] 0 | raw_valid[3] 0 | raw_valid[4] 1 | raw_valid[5] 1
raw_queue0_id 0 | raw_queue1_id 0 | raw_queue2_id - | raw_queue3_id - | raw_queue4_id 1 | raw_queue5_id 0
raw_queue0_enable 1 | raw_queue1_enable 1 | raw_queue2_enable 1 | raw_queue3_enable 1 | raw_queue4_enable 0 | raw_queue5_enable 0
Newer store, awid=2
raw_valid[0] 1 | raw_valid[1] 1 | raw_valid[2] 1 | raw_valid[3] 0 | raw_valid[4] 1 | raw_valid[5] 1
raw_queue0_id 2 | raw_queue1_id 0 | raw_queue2_id 0 | raw_queue3_id - | raw_queue4_id 1 | raw_queue5_id 0
((a_wcmd_en & (|(~raw_valid & 6'b110000)))
110011

## Slide 6: B response arrived
raw_valid[0] 1 | raw_valid[1] 1 | raw_valid[2] 0 | raw_valid[3] 0 | raw_valid[4] 1 | raw_valid[5] 1
raw_queue0_id 0 | raw_queue1_id 0 | raw_queue2_id - | raw_queue3_id - | raw_queue4_id 1 | raw_queue5_id 0
raw_match[0] 1 | raw_match[1] 1 | raw_match[2] 0 | raw_match[3] 0 | raw_match[4] 0 | raw_match[5] 1
raw_queue0_enable 1 | raw_queue1_enable 1 | raw_queue2_enable 1 | raw_queue3_enable 1 | raw_queue4_enable 1 | raw_queue5_enable 1
Bid = 0
raw_valid[0] 0 | raw_valid[1] 1 | raw_valid[2] 1 | raw_valid[3] 0 | raw_valid[4] 0 | raw_valid[5] 1
raw_queue0_id - | raw_queue1_id 0 | raw_queue2_id 0 | raw_queue3_id - | raw_queue4_id - | raw_queue5_id 1
(b_ch_taken & (|(raw_match & 6'b100000)))
110001

## Slide 7: AW & B arrived
raw_valid[0] 1 | raw_valid[1] 1 | raw_valid[2] 1 | raw_valid[3] 1 | raw_valid[4] 1 | raw_valid[5] 1
raw_queue0_id 0 | raw_queue1_id 0 | raw_queue2_id 0 | raw_queue3_id 2 | raw_queue4_id 1 | raw_queue5_id 0
raw_match[0] 1 | raw_match[1] 1 | raw_match[2] 1 | raw_match[3] 0 | raw_match[4] 0 | raw_match[5] 1
raw_queue0_enable For aw 0 | raw_queue1_enable For aw 0 | raw_queue2_enable For aw 0 | raw_queue3_enable For aw 0 | raw_queue4_enable For aw 0 | raw_queue5_enable For aw 0
raw_queue0_enable For b 1 | raw_queue1_enable For b 1 | raw_queue2_enable For b 1 | raw_queue3_enable For b 1 | raw_queue4_enable For b 1 | raw_queue5_enable For b 0
Awid= 3, Bid = 1
raw_valid[0] 1 | raw_valid[1] 1 | raw_valid[2] 1 | raw_valid[3] 1 | raw_valid[4] 1 | raw_valid[5] 1
raw_queue0_id 3 | raw_queue1_id 0 | raw_queue2_id 0 | raw_queue3_id 0 | raw_queue4_id 2 | raw_queue5_id 0