## Slide 1: BIU

## Slide 2: Block diagram
BIU
Prefetch
biu_path
AXI/AHB wrapper
cfifo
wfifo
rfifo
ICU
LSU/DCU
MMU

## Slide 3: Interface(ICU)
output biu_icu_grant;
output biu_icu_last;
output biu_icu_rdata;
output biu_icu_read_ack;
output biu_icu_read_error;
input icu_biu_addr;
input icu_biu_cacheability;
input icu_biu_hw_pf_inv;
input icu_biu_length;
input icu_biu_privileged;
input icu_biu_rdata_wait;
input icu_biu_req;
input icu_biu_size;

## Slide 4: Interface(MMU)
output biu_mmu_grant;
output biu_mmu_rdata;
output biu_mmu_read_ack;
output biu_mmu_read_error;
input mmu_biu_addr;
input mmu_biu_cacheability;
input mmu_biu_length;
input mmu_biu_privileged;
input mmu_biu_req;
input mmu_biu_size;
Single transfer.
The interface should be removed after move page information to dcu.

## Slide 5: Interface(IPIPE)
output biu_ipipe_standby_ready;
//for WFI use, all R/W transfer are done.

## Slide 6: Interface(LSU)
output biu_lsu_load_grant;
output biu_lsu_load_last;
output biu_lsu_load_lock_fail;
output biu_lsu_load_rdata;
output biu_lsu_load_read_ack;
output biu_lsu_load_read_error;
output biu_lsu_load_resp_id;
output biu_lsu_load_rsnoop; //MP, ACU bus
output biu_lsu_load_write_ack; // data is write to slave
output biu_lsu_load_write_error;
output biu_lsu_store_ack; // data is write to slave
output biu_lsu_store_data_ack; // data write to wrapper
output biu_lsu_store_error;
output biu_lsu_store_grant;
output biu_lsu_store_resp_id;
output biu_lsu_no_pending_wdata;//all wdata transfer done
input lsu_biu_hw_pf_inv;
input lsu_biu_load_addr;
input lsu_biu_load_bwe;
input lsu_biu_load_cacheability;
input lsu_biu_load_id;
input lsu_biu_load_kill;
input lsu_biu_load_length;
input lsu_biu_load_lock;
input lsu_biu_load_lock_clear; // only for ahb
input lsu_biu_load_privileged;
input lsu_biu_load_rdata_wait; // rfifo can’t pop
input lsu_biu_load_req;
input lsu_biu_load_size;
input lsu_biu_load_type; //MP, ACU bus
input lsu_biu_load_wdata;
input lsu_biu_load_write;
input lsu_biu_store_addr;
input lsu_biu_store_bwe;
input lsu_biu_store_cacheability;
input lsu_biu_store_data_valid; //data can write to wrapper
input lsu_biu_store_id;
input lsu_biu_store_last; // bypass last signal only for axi
input lsu_biu_store_length;
input lsu_biu_store_lock;
input lsu_biu_store_precise; //device or uncache should return ack
input lsu_biu_store_privileged;
input lsu_biu_store_req;
input lsu_biu_store_size;
input lsu_biu_store_type; //MP, ACU bus
input lsu_biu_store_wdata;

## Slide 7: Interface(wrapper)
input path_wrapper_addr;
input path_wrapper_cmd;
input path_wrapper_bwe;
input path_wrapper_req_id;
input path_wrapper_length;
input path_wrapper_size;
input path_wrapper_lock;
input path_wrapper_cacheability;
input path_wrapper_precise;.
input path_wrapper_wdata;
input path_wrapper_wlast;
input path_wrapper_privileged;
input path_wrapper_cfifo_wr;
input path_wrapper_wfifo_wr;
input path_wrapper_rdata_wait;
input path_wrapper_type; //MP acu bus
output wrapper_path_rfifo_valid_n;
//this signal will be low when any data push to rfifo
output wrapper_path_rfifo_rdata;
output wrapper_path_rfifo_load_error;
output wrapper_path_rfifo_store_error;
output wrapper_path_rfifo_id;
output wrapper_path_rfifo_lock_fail;
output wrapper_path_rfifo_last;
output wrapper_path_rfifo_wresp;
output wrapper_path_rfifo_rsnoop; //MP acu bus
output wrapper_path_bus_busy;
output wrapper_path_cfifo_full;
output wrapper_path_cfifo_empty;
output wrapper_path_wfifo_full;
output wrapper_path_wfifo_empty;
output wrapper_path_no_pending_wdata;

## Slide 8: BIU ID Mapping
READ |  | 
LSU(include AMO, LR/SC) | 0 | From dcu
MMU | 1 | 
ICU | 2 | 
LOCK_CLEAR_ID(only for AHB) | 4 | 
UNCACHE_LOAD_ID | 7 | From dcu
ICU_PREFETCH_ID | 8 | 
LSU_PREFETCH_ID0 | 9 | 
LSU_PREFETCH_ID1 | a | 
LSU_PREFETCH_ID2 | b | 
MSHR | 10~1f | From dcu
WRITE |  | 
LSU | 3 | From dcu
Vector FP(fast path) | 18~1f | From dcu

## Slide 9: AXI wrapper(25)
AR
AW
compare
W
CFIFO
WFIFO
RFIFO
B
R
RAW

## Slide 10: AXI wrapper(A27)
AR
AW
compare
W
CFIFO
WFIFO
RFIFO
B
R
RAW

## Slide 11: AXI RAW fifo
AXI 6(25)/8(A27) entries RAW FIFO
The newer write information will push to the smallest number entry and shift the others.
The FIFO will shift(only shift the smaller than match entry) and kill the oldest match entry.
The RAW compare will be disable if access to cacheable region since L2C can guarantee the order in ACU bus.
Next stage: the depth should be configurable.

## Slide 12: Attribute Transfer table for AXI
Type | ARCACHE | AWCACHE
Device, Non-bufferable | 0000 | 0000
Device, bufferrable | 0001 | 0001
Memory, Non-cacheable, Non-bufferable | 0010 | 0010
Memory, Non-cacheable, Bufferable | 0011 | 0011
Memory, Write-through, No-allocate | 1010 | 0110
Memory, Write-through, Read-allocate | 0110 | 0110
Memory, Write-through, Write-allocate | 1010 | 1010
Memory, Write-through, Read and Write-allocate | 1110 | 1110
Memory, Write-back, No-allocate | 1011 | 0111
Memory, Write-back, Read-allocate | 0111 | 0111
Memory, Write-back, Write-allocate | 1011 | 1011
Memory, Write-back, Read and Write-allocate | 1111 | 1111
MP not support
write-through

## Slide 13: AHB wrapper
wdata
wfifo
rfifo
ack_info
Bus resp, ready, rdata
cfifo
ctrl_signal
+
retry
burst
haddr_valid
hwdata
addr_non_comp
hretry_valid | do_burst

## Slide 14: Attribute Transfer table for AHB
Encoding Value | Type | HPROT[3] cacheable | HPROT[2] bufferable | HPROT[1] privileged | HPROT[0] data/fetch
0-1 | Device | 0 | 0 | - | -
2-3 | Memory, Non-cacheable | 0 | 0 | - | -
4-7 | Memory, Write-through | 1 | 0 | - | -
8-11 | Memory, Write-back | 1 | 1 | - | -

## Slide 15: JG AHB
AHB Master
dummy Master
AHB Slave
arbiter
M2S
Master monitor