## Slide 1: D23 BIU

## Slide 2: Discussion (3/2)
Requirement Review
PPI data width
  Fixed to 32 or not ?
FIO TYPE?
  Should it be 1 cycle response?

## Slide 3: Discussion (3/9)
Requirement Review (Requirement - 3)
CHECK APB related IP for AE350 (SIZEDN … etc.)
Low Latency Port (LLP) in AE350
HEXCL in AHB5
HMASTERLOCK in N22

## Slide 4: Discussion (3/16)
Block Diagram
  CMD/RESP Queue: configurable or remove
AHB5 – HPORT changes
  Spec: AHB5 + AHB4 compatible?
AE350
  Demo PPI and LLP usage on AE350

## Slide 5: Discussion (3/22)
Block Diagram Detail
  Arbiters
  Decode
  PPI/LLP Base + Size (Aligned)
  Path function

## Slide 6: Discussion (3/29) - TODO
BIU discussion is temporary done in 3/22
Start PMP/other discussion on 3/29
  ePMP
    ePMP
    utlb(?)
  CLIC or PLIC / PLMT (embedded) / PLDM (embedded)

## Slide 7: D23 BIU Requirement - 1
Interface:
  CPU internal:
    IFU/LSU Load/LSU Store/MMU
    Extendable to 4
  CPU out: (Flop-Out) / (Input timing should be block at bus-wrapper) / (Bus protocol configurable)
    System Bus (AHB-Lite or AXI)  Ref. to N22 BIU
    Peripheral Port (APB or AHB)  Ref. to N22 PPI
    Low Latency Port (AHB or AHB)  Ref. to N22 FIO
Spec - System Bus AHB
  Data Width: 32/64 (power of 2, >32)
  Address Width: 24 – 64 (parameter)
  Type: SINGLE-BYTE/WORD/H-WORD/D-WORD, WRAP4/8/16-WORD, INCR4/8/16-WORD
    WRAP and INCR support depends on Cache Config.
  Always support sync N:1 clock ratio
  HMASTERLOCK is supported.
    (TODO: Detail) (HL2H support LOCK?) (How to support LOCK in AHB-L)

## Slide 8: D23 BIU Requirement - 2
Spec – Peripheral Port APB
  Data Width: Same as CPU data width
    Depends on CPU data width => Add SIZEDN on platform when CPU data width is 64
  Address Width: Depends on Peripheral Port SIZE
  Type: SINGLE-BYTE/WORD/H-WORD/D-WORD
  Handle Burst transaction from Internal request
  Always sync N:1 clock ratio
  Config/Control CSR support
  Connect to APB-Subsystem in AE350
  Outstanding request: AHB/APB/AHB-Low-Latency
Spec – Low Latency Port AHB
  Configurable
  Data Width: Same as CPU data width
  Address Width: Depends on Low Latency Port SIZE Same as CPU address width
  Type: Same as system port
  Always support sync N:1 clock ratio
  Connect to each bus slave (?)

## Slide 9: D23 BIU Requirement - 3
Spec – Internal request support
  Outstanding request to multiple destination port (response outstanding or in sequence?)
    LSU is ID-based implementation => out-of-order response is acceptable
    IFU is not ID-based now => the response should be in sequence now.
  Different interface: No out-standing, Same interface: out-standing is acceptable.
  *** consider no response buffer in BIU
  *** 1. back-to-back 2. reduce gate-count
  I/D Cache Support – burst transaction
    The I/D Cache only issues WRAP burst
Spec – MISC.
  Different Port region can not overlap
  CPU-out Interface can issue back-to-back transfer.
  AHB: should burst be early terminated when error response happen. (?)
    In N22, the burst transaction is not be early terminated by error response now.
  Report address when error response happens

## Slide 10: Reference: N22 BIU Spec – AHB-L
AHB-Lite:
  Address Width: 24/32
  Data Width: Fixed to 32
  Configurable sync N:1 clock ratio
  Type: SINGLE-BYTE/WORD/H-WORD, INCR8-WORD (Only when I$ is supported)
  HMASTERLOCK is supported.

## Slide 11: Reference: N22 AMO by HMASTERLOCK
The HMASTERLOCK is an address phase signal
The HMASTLOCK signal is asserted to lock the AHB-Lite bus once the LR instruction is executed.
BIU will hold the lock until it executes the SC instruction or the internal lock is cleared.

## Slide 12: Reference: AHB5 interface
Signal | Destination | Description
HNONSEC | Slave and decoder | Indicates that the current transfer is either a Non-secure transfer or a Secure transfer. This signal is supported if the AHB5 Secure_Transfers property is True.
HEXCL master out | Exclusive Access Monitor | Exclusive Transfer. Indicates that the transfer is part of an Exclusive access sequence. This signal is supported if the AHB5 Exclusive_Transfers property is True.
HEXOKAY. slv -> mst | Multiplexor | Exclusive Okay. Indicates the success or failure of an Exclusive Transfer. This signal is supported if the AHB5 Exclusive_Transfers property is True.

## Slide 13: Reference: AHB5 Exclusive
An Exclusive access sequence is a sequence of Exclusive Transfers from a single master that operate using the
** The HEXCL is an address phase signal
** The Transaction with HEXCL is expectedly to get the HEXOKAY
following steps:
Perform an Exclusive Read transfer from an address. (LR)
Calculate a new data value to store to that address that is based on the data value obtained from the Exclusive Read.
Between the Exclusive Read and the Exclusive Write there can be other Non-exclusive transfers.
Perform an Exclusive Write transfer to the same address, with the new data value(SC)
The response to the Exclusive Write transfer indicates if the transfer was successful or if it failed.
HEXOKAY must only be asserted in the same cycle as HREADY is asserted.
HEXOKAY must not be asserted in the same cycle as HRESP is asserted.
Can add an assertion.

## Slide 14: Reference: AHB5 HPROT
Bit | Name | Desctipion
HPROT[0] | Data/Inst | 0: Inst Fetch 1: Data Access
HPROT[1] | Privileged | 0: Unprivileged 1: Privileged
HPROT[2] | Bufferable | Memory Type setting (Next page.)
HPROT[3] | Modifiable | 
HPROT[4] | Lookup | 
HPROT[5] | Allocate | 
HPROT[6] | Shareable | 

## Slide 15: Reference: AHB5 HPROT
Device-nE / E: indicates the early write is acceptable or not:
  Early write: the write response should be issued by the final-destination

## Slide 16: Reference: AHB5 HPROT
HPROT mapping between AHB5 and AHB4 AHB5/4 will be selected by core config
allocate/lookup means Cacheable: AHB5-HPROT[6] mapping to AHB4-HPROT[3] BIU will get MTYPE, use AHB4/5 decode
Bufferable has the same meaning: AHB5-HPROT[2] mapping to AHB4-HPROT[2] Prepare MTYPE to AHB5/4, AXI, APB (use case)

## Slide 17: REF: HPROT in AHB4

## Slide 18: HPROT [0], [1]
HPROT[0]
  0: Inst
  1: Data
HPROT[1]
  0: U-Mode
  1: M-Mode

## Slide 19: MTYPE to AHB4.HPROT
MYPE |  | Description | HPROT[3] Cacheable | HPROT[2] Bufferable
4’b0000 | 0 | Device non-buffer | 0 | 0
4’b0001 | 1 | Device Bufferable | 0 | 1
4’b0010 | 2 | Normal Non-cacheable Non-bufferable | 0 | 0
4’b0011 | 3 | Normal Non-cacheable Bufferable | 0 | 1
4’b0100 | 4 | Write-through No-allocate | 1 | 0
4’b0101 | 5 | Write-through Read allocate | 1 | 0
4’b0110 | 6 | Write-through Write-allocate | 1 | 0
4’b0111 | 7 | Write-through Read and Write-allocate | 1 | 0
4’b1000 | 8 | Write-back No-allocate | 1 | 1
4’b1001 | 9 | Write-back Read-allocate | 1 | 1
4’b1010 | 10 | Write-back Write-allocate | 1 | 1
4’b1011 | 11 | Write-back Read and Write-allocate | 1 | 1

## Slide 20: MTYPE to AHB5.HPROT
MYPE |  | Description | HPROT[6] Shareable | HPROT[5] Allocate | HPROT[4] Lookup | HPROT[3] Modifiable | HPROT[2] Bufferable
4’b0000 | 0 | Device non-buffer | 0 | 0 | 0 | 0 | 0
4’b0001 | 1 | Device Bufferable | 0 | 0 | 0 | 0 | 1
4’b0010 | 2 | Normal Non-cacheable Non-bufferable | 1 | 0 | 0 | 1 | 0
4’b0011 | 3 | Normal Non-cacheable Bufferable | 1 | 0 | 0 | 1 | 1
4’b0100 | 4 | Write-through No-allocate | 0 | 0 | 1 | 1 | 0
4’b0101 | 5 | Write-through Read allocate | 0 | 1 | 1 | 1 | 0
4’b0110 | 6 | Write-through Write-allocate | 0 | 1 | 1 | 1 | 0
4’b0111 | 7 | Write-through Read and Write-allocate | 0 | 1 | 1 | 1 | 0
4’b1000 | 8 | Write-back No-allocate | 0 | 0 | 1 | 1 | 1
4’b1001 | 9 | Write-back Read-allocate | 0 | 1 | 1 | 1 | 1
4’b1010 | 10 | Write-back Write-allocate | 0 | 1 | 1 | 1 | 1
4’b1011 | 11 | Write-back Read and Write-allocate | 0 | 1 | 1 | 1 | 1

## Slide 21: Reference – N22 and D23

## Slide 22: BIU Block Diagram
System bus wrapper
  AHB/AXI … etc.
Bus interfaces are flop-out
  It can be treated as 1 CMD queue
  CMD Queue should have 1 entry for back-to-back transaction
Resp Queue at least 2 entry since the RDATA should be flopped before using.
BIU Path can reuse vc_biu_path.v
Dest Decode
  Default port: system_bus
  Decode the req_addr and issue to different biu_wrapper
  (?) Keep each wrapper’s status, and block the different port req.
  EX: system bus is doing the translation from LSU, Dest_dec should block the LSU-to-PPI request.
CSR-BIU interface: indicates the PPI/LLP setting
  Previous conclusion:
  Different interface: No out-standing, Same interface: out-standing is acceptable.
  arbiter detail
  decoder detail
  Path = decoding + arbiter
  Port crossing will not happen (define in interface)
  PUSH/POP cross region
  Parameter

## Slide 23: Block Diagram (3/22)
  Req_Issue block should block the IFU/LSU request when the destination port is out-standing
    Ex. SYS_BUS is handling a IFU request, than the next IFU request to PPI/LLP will be blocked
  Since the spec define the BPA must aligned size, the comparator can be implemented by AND/OR
  The ID will be issued by Req_Issue to indicate source, the Resp_Gen will generate the response by ID
  biu_path should record the out-standing request number for each port
  If bus error happens, the addr should be return to LSU (can reuse resp data)
  Resp Data width should be the max value of BIU_DATA and BIU_ADDR
  ID: use the IFU/LSU’s ID (extend 2bit or define not overlap)

## Slide 24: Block Diagram (3/22)
  Do the arbitration first than issue the request can reduce comparators (?
  keep it as a reduce gate count version

## Slide 25: Reference: N22 BIU Spec – PPI
APB (PPI: private peripheral interface)
  APB Bus interface
  Data Width: Same as CPU data width
  Addr Width: Depends on PPI-SIZE
  Config/Control CSR:
    Config: MMSC_CFG.PPI (Bit[25])
    Control: MMPIB (0x7f0)
BPA
0
SIZE
EN
Field | Bits | Description | Type
BPA | [31:10] | PA Base | Read-Only
SIZE | [5:1] | PPI Size (0~2G) | Read-Only
EN | [0] | PPI Enable | Read-Only

## Slide 26: Reference: N22 BIU Spec – FIO
FIO (Fast I/O)
  Self-define interface (cmd valid/ready)
  Data Width: Same as CPU data width
  Addr Width: Depends on FIO size
  Only Load/Store can access.
  1 Cycle response.
  Config/Control CSR:
    Config: MMSC_CFG.FIO (Bit[26])
    Control: MFIOB (0x7f1)
BPA
0
SIZE
EN
Field | Bits | Description | Type
BPA | [31:10] | PA Base | Read-Only
SIZE | [5:1] | FIO Size (0~2G) | Read-Only
EN | [0] | FIO Enable | Read-Only

## Slide 27: Self Define Interface in N22
Signal name | Source | Destination | Description
biu_dm_cmd_valid | biu | dm | Transfer valid
biu_dm_cmd_dmode | biu | dm | Transfer in Debug Mode
biu_dm_cmd_mmode | biu | dm | Transfer in M-mode
biu_dm_cmd_addr | biu | dm | Address
biu_dm_cmd_wmask | biu | dm | Write data mask
biu_dm_cmd_wdata | biu | dm | Write data
biu_dm_cmd_read | biu | dm | Transfer direction
dm_biu_resp_rdata | dm | biu | Read data
dm_biu_resp_err | dm | biu | Error response

## Slide 28: PPI/LLP Usage
SIZE: PPI Region Size
  0: 0Byte
  1: 1K
  2: 2K
  …
  22: 2G
  23 -> 31: reserved
  PA = {BPA[31:10], 10’h0}
BPA
0
SIZE
EN
BPA: Base Physical Address
  The BPA should be aligned to SIZE
  The Config tool should check the alignment.
  The Config tool will check the LLP/PPI region will not cross the max value of BIU_ADDR
  Check the LLP and PPI region will not overlap.
  Priority
    Small size has the higher priority
[31:10]
[5:1]