## Slide 1: ATCTLC2AXI500
Driving Innovations™
Alex
2020/08/07

## Slide 2: Features
AXI Clock
  Synchronous N:1 (N could be 1, 2, 3 …)
  Asynchronous
Timing Requirement
  All AXI output signals should be flop-out
  All AXI input signals should be flop-in
Data-Width
  32/64/128/256
Address-Width
  32-64
AXI ID Width
  4-8

## Slide 3: Latency
A/C Channel Latency
  a_valid/c_valid to arvalid/awvalid/wvalid
  1 cycle (min)
D Channel Latency
  rvalid/bvalid to d_valid
  1 cycle
E channel latency
  0 cycle
B channel
  Hardwired to 0

## Slide 4: Clock/Reset
TL-C Clock Domain
  clk
  resetn
  aclken
AXI Clock Domain
  aclk
  aresetn

## Slide 5: ASYNC FIFO
FIFO Depth Parameter
  default is 3